## Slide 1
Security Level: public
End-to-End Low Latency Real-Time Communication Using H.264 and H.265 in 3GPP Networks with 5G Quality of Service S4-250233 3GPP SA4 Geneva February 2025

## Slide 2: Agenda Items
Motivation for End-End Real-Time Video Communication
3GPP Networks and 5G Technology for real time communication
Codec Implementation for real time communication
Error Resilience in low latency communications
Potential work ahead for SA4
Case study
Objectives and Timelines
Notes: We will begin with an introduction to real-time communication, discussing its definition, significance, and the challenges it poses. Next, we'll dive into the technical details of H.264 and H.265 codecs, followed by an overview of 3GPP networks and the advantages of 5G technology. Finally, we will examine Quality of Service in 5G and discuss case studies.

## Slide 3: Motivations for potential study on End-End Real-Time Communication
Notes: Real-time communication is crucial in today’s digital landscape, enabling instant data exchange. This section highlights its importance across various sectors and the inherent challenges that come with ensuring minimal latency in communication.

## Slide 4: Definition and Importance of Real-Time Communication
What is Real-Time Communication?
  Real-time communication involves the immediate exchange of information through various channels such as voice, video, or data.
Applications in Video Conferencing
  In video conferencing, real-time communication is crucial, as any delays can negatively affect the flow of discussions.
Impact on Online Gaming
  In online gaming, real-time communication enhances user experience, as latency can disrupt gameplay and interactions.
Impact on Extended Reality Applications
  In the case of extended reality especially when content is rendered it is good requires low latency transmission
Notes: Real-time communication refers to the live exchange of information, whether through voice, video, or data. Its importance lies in applications like video conferencing and online gaming, where delays can significantly impact user experience.

## Slide 5: Challenges in Real-Time Communication
Network Latency
  3GPP 5GS QoS provisions for bounds Packet Delay but it is not end-end
Bandwidth Limitations
  3GPP 5GS QoS has guaranteed bit-rate support but it is not end-end
Variations in Data Transmission
  3GPP 5GS QoS has provisions for limiting jitters but it is not end-end
Systemic Latency related to format semantics
  Codec structure (prediction structures) can lead to additional latency
  Loss/Error resilience
  In real time communications packet drop may cause visual quality degradation
  Study for profiles for enabling real time communication
Notes: Challenges include network latency, bandwidth limitations, and variations in data transmission. Addressing these issues is vital for maintaining the quality and reliability of real-time communications.

## Slide 6: H.264/AVC in wireless environments
IEEE TCVST [1] H.264 in wireless environments
  Network Abstraction Layer Units
  The H.264 standard is essential for HD video streaming, enabling smooth playback and high-resolution content delivery over the internet. There is a bit error rate and mobile devices are moving, constrained baseline and contrained high profile supported in TS 26.114
Coding Tools
Slice interleaving, group of macroblock, flexible macro bock ordering, data partitioning, redundant slices (adopted in TS 26.114 as optional).
Decoding tools
Intra frame error concealment, loss detection, de-blocking filter.
  [1] T. Stockhammer, Miska Hannuksela, Wiegand H.264 in wireless environments IEEE TCSVT 2003
Notes: H.264 is widely used for video compression due to its ability to deliver high-quality video at lower bitrates. It is essential for HD video streaming and broadcasting applications.

## Slide 7: H.265 in wireless environment and low latency [2]
DASH Streaming a key use case
  Wavefront processing, parallel encoding and parallel architectures, higher qualities more delay, also in streaming there is typically a delay up to 60 seconds
Coding Tools for H.265 wireless environments
  Network abstraction layer unit, slice and tile based coding
Decoding tools for low latency in wireless environments
  WPP Wavefront parallel processing
  Was there more emphasis on high quality delivery over robust channels ? HD signals also require more processing and transmission bandwidth
  Redundant slice heard is not supported in HEVC
  [2] Overview of the HEVC VIdeo Coding Standard G.sullivan, J. Ohm, Woo-jin han, Thomas Wiegand
Notes: H.265, or HEVC (High-Efficiency Video Coding), improves upon H.264 by providing better compression rates, allowing for higher resolutions at similar bitrates, which is crucial for 4K and beyond.

## Slide 8: 3GPP Networks and 5G Technology
Notes: 3GPP networks are foundational to mobile telecommunications, and the advent of 5G technology brings enhanced capabilities. This segment introduces 3GPP standards and highlights key features of 5G.

## Slide 9: 5G QoS for Low Latency Transmission
5QI (PDB, PER, priority)
  5G system features different QoS parameters for different types of traffic enabling prioritization at NG-RAN to enable low latency use cases.
Latency constraints (PDB)
  Packet Delay Budget is one aspect in 5QI, but only between UE and UPF
  Losses on real time traffic
  Error rate is part of 5qi and some packets may be dropped in the RAN.
PDU Set QoS
  By dropping groups of correlated packets a more efficient
Notes: 5G technology introduces lower latency, higher bandwidth, and increased connectivity. These advancements enable new applications in various sectors, including smart cities and autonomous vehicles.

## Slide 10: 5G QoS in core, RAN and application 2 way
UE
RAN
UPF
DN
RTC AS
Encode latency
Capture latency
Packager latency
Latency in RAN UL QoS
Latency in CN UL
Latency in N6
Server latency (in case stream routing)
Latency = UE_latency_sender + RAN_UL + RAN_DL UPF_UL + UPF_DL, N6_latency + UE_latency_receiver
UE
Decoder latency
Render latency
Jitter Buffer latency
RAN
Latency in RAN DL QoS
UPF
Latency UPF CN DL
DN
Latency in N6
Server latency (in case stream routing)
100-300 ms for real time

## Slide 11: Codec Implementation
Notes: 3GPP networks are foundational to mobile telecommunications, and the advent of 5G technology brings enhanced capabilities. This segment introduces 3GPP standards and highlights key features of 5G.

## Slide 12: Decoder implementation
Hardware Decoding
  Best to receive and decode in real time with low energy usage
Software Decoding
  Alternative to investigate if this is suitable for real time communication.
Tools for Real time and low latency
  Need to check if and what tools are available in current implementations
Notes: QoS parameters include latency, availability, and reliability. These metrics are essential for evaluating the performance of real-time communication applications in 5G networks.

## Slide 13: Encoder implementation
Hardware Encoding
  What is the availability
Software Encoding
  - Usually available
Tools for Real time
  - Need to check if and what tools are available such as data partition fmo redundant slices
Notes: QoS parameters include latency, availability, and reliability. These metrics are essential for evaluating the performance of real-time communication applications in 5G networks.

## Slide 14: Error Resilience
Notes: 3GPP networks are foundational to mobile telecommunications, and the advent of 5G technology brings enhanced capabilities. This segment introduces 3GPP standards and highlights key features of 5G.

## Slide 15: Forward Error correction
Forward Error Correction
  IDS codes require overhead of k and still enable receiving M packets
Computational complexity
  Forward error correction introduces additional computation at sender and receiver and potentially additional algorithmic latency as all source packets may be needed
Bandwidth Overhead
  Forward error correction does increase the bandwidth overhead in the network, that may as a side benefit also increase end to end latencies
Notes: 5G networks employ various mechanisms and policies to manage traffic efficiently and ensure that high-priority applications maintain the necessary service quality.

## Slide 16: Retransmission
RTP Retransmission
  Methods for real time protocol retransmission
RTP redundant transmission
  this would lead to significant overhead
Notes: The impact of QoS policies on real-time communication is profound, as they directly influence user experience by minimizing latency and ensuring consistent data delivery.

## Slide 17: Coding Tools for error resilience
Flexible Macroblock Ordering FMO
Redundant slices [26.114]
PDU set importance for less important media slices see TS 26.522
Tiled content [H.265]
Send parameter sets multiple times (RTP) [26.114]
Notes: The impact of QoS policies on real-time communication is profound, as they directly influence user experience by minimizing latency and ensuring consistent data delivery.

## Slide 18: Work Ahead for SA4 for Latency Communication
Notes: Implementing low latency communication involves careful consideration of system architecture and optimization techniques. This section discusses strategies to achieve optimal performance.

## Slide 19: Test condition development
Extend the scenario for conversational and real-time communication
  This scenario for XR and conversation encoding and decoding is used in real time and the 5G network may be taken as the reference network
Develop codec test condition for conversation and real time communication
  bit-rate and channel conditions (bandwidth can be defined), bit error rates can again be introduced in the tests,
BaseLine/Anchor
  Initial quality evaluation and codec characterization can be developed
Notes: To maintain end-to-end QoS in 5G networks, continuous monitoring and adaptive QoS management strategies must be employed. This ensures that service levels meet user demands.

## Slide 20: Explore coding configuration to support low latency
Coding configuration
  Develop coding configuration for h.264 and h265 based on existing profiles that better support low latency cases
Characterization
  Based on bit-rate and channel conditions based on 5G networks (bandwidth can be defined, loss ratio and nature of the losses) to develop the end-end characterization in terms of quality under a low latency constraint providing quality metrics using well known objective metrics
Error Resilience and Forward error correction
  Explore configurations of the codec and potential FEC schemes to check if quality can be improved in conditions and study the related losses.
Notes: To maintain end-to-end QoS in 5G networks, continuous monitoring and adaptive QoS management strategies must be employed. This ensures that service levels meet user demands.

## Slide 21: Expected SA4 output and potential Normative Work
Updated/improved Video operating points
  If new coding configurations are developed with settings that are good for low latency they can be candidate for normative work introducing a new video coding operating point
Update the characterization and evaluation, including new test conditions for low latency and error resilience
  TR 26.955 and potential new TR to include the experimental conditions
Influence on future video coding requirements
  Align with MPEG/JVET colleagues working on low latency coding tools, especially regarding the test condition
  Potentially a new specification on coding tools for real time communication
  In case findings cannot be embedded in current specifications
Notes: To maintain end-to-end QoS in 5G networks, continuous monitoring and adaptive QoS management strategies must be employed. This ensures that service levels meet user demands.

## Slide 22: Case Studies and Practical Applications
Notes: This section presents real-world examples of low latency communication systems in action. Understanding these applications helps illustrate the concepts discussed throughout the presentation.

## Slide 23: Testing
Device testing
  It may be helpful to get some experimental data from running RTC workflows on devices like state of the art terminals
Software testing
  It may be helpful to run some SoA software to create real time media processing flows and collect some data to provide insight
FEC Tools testing
  Some FEC tooling can be assessed and tested for their accuracy.
Notes: This concluding slide will explore emerging trends and innovations that are poised to shape the future of real-time communication, including advancements in AI and machine learning integration.

## Slide 24: Timeline and objectives
Notes: This section presents real-world examples of low latency communication systems in action. Understanding these applications helps illustrate the concepts discussed throughout the presentation.

## Slide 25: Objectives
O1: Develop and document test conditions using emulation based on 5G core and RAN and potentially N6/Internet for different bit-rate, error-rate, latency to enable characterization of codec tools including 3GPP network specific. Test conditions and emulation may also include common quality of service conditions.
O2: Investigate encoder/decoder implementations for error resilience tools and low latency features in 3GPP tools and potentially other available tools.
O3: Explore Potential coding profiles or configurations to support low latency and error prone transmission
O4: Potentially include error resilience tools not part of the video codec such as FEC in the study, by documenting them and potentially include them in the evaluation.
O5: Develop End-to-End characterization of quality/latency in some of the developed test conditions (O1) using coding configurations (O3, O4)
O6: Communicate findings to external organization developing next generation video codecs to consider our requirements and test conditions, organizations such as MPEG, ITU, JVET and other similar organizations.
Notes: To maintain end-to-end QoS in 5G networks, continuous monitoring and adaptive QoS management strategies must be employed. This ensures that service levels meet user demands.

## Slide 26: Timeline
April 2025: Draft study item, additional evidence of end-end codec characterization for low latency end-end video coding
May 2025: SA4 approval of study item
  June 2025: SA approval of study item
  Aug 2025: Test and emulation framework and test conditions
  Nov 2025: Investigation of coding tools and proposed coding configurations
  Dec 2025: TR for information to SA
  Feb 2026: complete end-to-end characterization and conclude on proposed coding configurations
  March 2026: TR for approval to SA
Notes: To maintain end-to-end QoS in 5G networks, continuous monitoring and adaptive QoS management strategies must be employed. This ensures that service levels meet user demands.

## Slide 27: Proposal
Discuss and take this into account
Sollicit interested companies
Notes: To maintain end-to-end QoS in 5G networks, continuous monitoring and adaptive QoS management strategies must be employed. This ensures that service levels meet user demands.

## Slide 28: Conclusion
Low Latency Codecs
Understanding codec tools for low latency and their configuration is crucial for effective real-time communication, influencing audio and video quality. Not only the codec features are important but also the related support in devices and software/hardware implementations
3GPP 5G Systems
5G System model can be used for experiments considering typical 5QI QoS parameters used and related network emulators can be used for experiments
Quality of Service
Quality of Service (QoS) mechanism can be included in the evaluation. New mechanisms developed in 3GPP such as QoS for XR can also be used to evaluate and make sure end-end latencies can be achieved
Additional Strategies
Third party FEC or other tools for providing error resilience can potentially be used. In addition codec requirements and potential tools for low latency can be derived and shared with external SDO, especially in case SA4 adopts some of the tools
Notes: In conclusion, understanding the interplay between codecs, network standards, and Quality of Service is essential for delivering effective real-time communication solutions. As technology evolves, so too will the strategies to meet the demands of this dynamic field.