## Slide 1: 3GPP Status on Enhanced TV Service Layer Aspects

## Slide 2: 3GPP Status (Network architecture)
SA1:
  Service Requirements completed in TS22.101, section 32.
SA2:
  Study complete – TR 23.746v0.4.0 -> TR 23.746v1.0.0 sent for approval
  Normative work completed for: Receive Only Mode, Shared MBMS Network, Broadcast+Unicast
  Waiting for SA4 to progress work on TMB2 to complete this feature. (Declared 85%)
SA4:
  Progress on FS_USE_3GPP_4_TV study item to address service requirements
  Initiated study on external interface for BMSC (Xm).
  Agreed to WID for general external interface with primary focus on TV aspects (completion target March’17).
RAN2:
  Needs to follow up on normative work from SA2
RAN3:
  Define Stage 3 for M1-s (Shared MBMS Network)
CT1/3/4/6:
  Stage 3 aspects for UE configuration (CT1:ROM), CT4: CN aspects of SMN, CT3: Stage 3 of TMB2.

## Slide 3: SA2 Status

## Slide 4: Rel-14 Features for eMBMS for TV – Receive Only Mode
Allows UEs to receive Broadcast Service only via eMBMS with:
  No need for PLMN subscription
  No need for uplink capability
  Target goal: Digital TV eMBMS receivers
  Receives MBMS service only on a range of standardized TMGIs
    Operators which do not want receive only devices on their network, do not use these TMGI values
Receive Only Mode UE is configured with:
  PLMN ID(s) that provide the eMBMS service.
  TMGI(s):
    In the case of the network providing MBMS service in MBMS transport only mode, the TMGI(s) for each MBMS service need to be configured in the UE.
    The UE may be configured to receive TMGI(s) via Service Announcement USD(s).
  USD(s)
  RAN specific information (frequency bands, etc).

## Slide 5: Rel-14 Features for eMBMS for TV – Receive Only Mode (2)
Receive only Mode with independent unicast:
  A UE may be configured as Receive Only Mode with independent unicast using EPS bearer contexts.
  This allows a UE to operate as Receive Only Mode (as defined above) for MBMS broadcast service, and independently follow regular NAS/RRC procedures for unicast service with a PLMN.
  Requires USIM and PLMN subscription to receive unicast service.
  No additional subscription or credentials are required to receive MBMS broadcast service.

## Slide 6: Rel-14 Features for eMBMS for TV – Shared MBMS Network (1)
Shared MBMS Network (SMN):
  An MBMS network (at least BM-SC and MBMS-GW) shared by multiple PLMNs with a common entry point.
  An MBMS service area may span across RAN nodes from different participating PLMNs.
  The Shared MBMS network consists of the following shared network elements:
  The shared MBMS network may also include shared eNB(s), MCE(s), and MME(s)
    This option allows for Standalone MBMS network
Rel-14 SMN Architecture:
New Inter-PLMN reference points
  M1-s: Inter-PLMN reference point between the Shared MBMS GW and the E-UTRAN node from a participating PLMN.
  Sm-s: Inter-PLMN reference point between the Shared MBMS GW and MME from a participating PLMN.

## Slide 7: Rel-14 Features for eMBMS for TV – Shared MBMS Network (2)
TMGI handling for Shared MBMS Network:
  Option 1: Shared PLMN ID
    A Shared PLMN ID is used for the shared MBMS service. The shared PLMN ID is broadcasted in the cells broadcasting the shared MBMS service content.
  Option 2: Internal PLMN ID in the Shared MBMS network
    The Shared MBMS network assigns and internal PLMN ID configured for the shared MBMS service provided by participating PLMNs.
    The MBMS-GW is configured for each internal PLMN ID, the PLMN IDs of the participating PLMNs.
    The MBMS-GW performs a translation of the PLMN ID field of the TMGI:
      From internal PLMN ID to the PLMN ID of the receiving PLMN when transmitting over M1-s or Sm-s.
      From the received PLMN ID to internal PLMN ID, when receiving from M1-s or Sm-s.
UE aspects:
  UE Scenario 1: The UE receives both unicast and broadcast service from same PLMN.
  UE Scenario 2: The UE receives broadcast MBMS service only with no unicast service, i.e., the UE has no valid PLMN subscription. The UE acts in Receive Only mode.
  UE Scenario 3: The UE receives unicast service from one serving PLMN (e.g. the PLMN for which it has unicast subscription), and receive MBMS service through a different PLMN. The UE acts in Receive Only mode with independent unicast.

## Slide 8: Rel-14 enTV Feature: Broadcast + Unicast Service
Unicast transport for TV:
  Dedicated APN for TV services.
  Allows for specific charging for TV services, and configuration of QoS.
  Requires MNO subscription.
Deployment Option 1: Joint broadcast + unicast TV service through BM-SC
    The TV service includes a TV Service subscription associated with the operator subscription, which allows tuning to TV unicast and MBMS broadcast for transport.
    Broadcast/Unicast decision at 3GPP network using MBMS operations on Demand (MooD):
      The operator monitors the TV service consumption per channel in areas and decide to use unicast or MBMS broadcast usage.
      For unicast BM-SC reroutes data to P-GW via SGi
      The operator may provide usage information to the Content Provider.
Deployment Option 2: Broadcast/unicast decision at Content Provider
  Separate direct broadcast service through BM-SC and direct unicast service via SGi through PDN GW.
  For Unicast TV transport, the Content Provider uses regular unicast data connectivity. For MBMS broadcast, the Content Provider provides the content of the TV channel via user plane.
  In order to monitor popularity in the MBMS Broadcast Areas, the operator can expose popularity information (derived from HTTP Consumption Reporting) to the Content Provider via external interface (TMB2).

## Slide 9: Rel-14 enTV Feature: Broadcast + Unicast Service (2)
Scenario 1:
Scenario 2:
Content Provider
(TV Channel
/ Broadcast Operator)
P
-
GW
E
-
UTRAN
S
-
GW
BM
-
SC
MBMS
GW
MME
S1
-
MME/M3
TV UE1
TV UE2
BC
U
C
LTE
Uu
MNO1 Network Elements
MNO1 Elements for unicast and MBMS
User Plane Data for a TV Channel
PSS
TV Service UE
TMB2
SGmb
SGi
SGi
Content Provider
(TV Channel
/ Broadcast Operator)
P
-
GW
E
-
UTRAN
S
-
GW
BM
-
SC
MBMS
GW
MME
S1
-
MME/M3
TV UE1
TV UE2
BC
U
C
LTE
Uu
MNO1 Network Elements
MNO1 Elements for unicast and MBMS
User Plane Data for a TV Channel
TV Service UE
TMB2
SGmb
SGi
Si

## Slide 10: Rel-14: Standard External interface TMB2(Xm)
TMB2 Functionality already provided by existing MB2 reference point:
  Content Provider request the activation/deactivation of MBMS bearer,
  Content Provider request to activate, deactivate, and modify an MBMS bearer.
  BM-SC notification to the application of the status of an MBMS bearer.
TMB2 New functionality:
  Indication of MBMS Service Type 1 "Transport only mode" or MBMS Service Type 2 "Full MBMS service mode" per MBMS bearer service or per MBMS User Service .
  Indication by content provider whether an MBMS bearer service (identified by TMGI) is for broadcast only mode devices.
  Mechanism for the MNO to exchange information (such as QoE information, consumption information, user service registration information, and delivery information) with the 3rd party content provider.
  The content provider can request creation/modifications of broadcast/unicast sessions with additional capabilities such as error recovery, reporting (QoE, consumption, etc.), service announcement etc. The information to be exchanged between content provider and BM-SC is described in section 6.3.1.3.

## Slide 11: SA4 Status

## Slide 12: Overview of Work (1)
One telco prior to SA4#90
  Agreed on use cases generated with EBU in principle, not yet added
During SA4#90 (Sep 3-7, 2016, Ljubljana, Slovenia)
  FS_USE_3GPP_4_TV:
    Little time during the meeting, focus was on some normative work in other areas
    progressed TR TR 26.917: http://www.3gpp.org/ftp/tsg_sa/WG4_CODEC/TSGS4_90/Docs/S4-161095.zip
    Addition of
      Context and Motivation
      use case with associated working assumptions on broadcast TV service delivery over eMBMS as a MBMS User Service,
      a gap analysis of the MBMS USD versus the DVB Service Information (SI),
      and assessment of several solution frameworks to fulfil the gaps from the gap analysis
      IP-based broadcast TV services over eMBMS
  Progressed work on FS_xMBMS
    architecture model and provisioning procedures for DASH streaming and file delivery services.
    Updated Technical Report in S4-161124.
  Sent LS to SA2 to agree completing stage 2 for TMB2
  Agreed new work item on “Mobile Network Interface for MBMS Delivery of Media and TV services” to define the stage 2 for TMB2, as defined in S4-161128

## Slide 13: Overview of Work (2)
Next meeting SA4#91 (Oct 24-28, 2016, Bangalore, India)
  Progress SA4 study on FS_USE_3GPP_4_TV
  Possibly complete normative work “Mobile Network Interface for MBMS Delivery of Media and TV services”
  Scope normative work for Service Layer for “3GPP Service Layer”
Expected interim adhoc meeting Nov 2016
  Progress the above work if necessary
SA4#92 (Jan 23 – 27, 2017, Tallinn), last meeting for Rel-14
  Complete SA4 study on FS_USE_3GPP_4_TV
  Initiate normative work for Service Layer for “3GPP Service Layer”
Note: Rel-14 may be extended for one additional meeting cycle
Rel-15 will start during SA4#93 (Apr 24-28, 2017)

## Slide 14: Service Layer Aspects
Two basic branches are defined
  Transport-only/Pass-through mode:
    basically all service layer functionality is defined outside 3GPP
    Service definition, codecs, encapsulation and so on
    Expected to have two modes: IP-based and MPEG-2 TS
    At least from Qualcomm perspective, may be broadcast/receive-only
    Attempt to complete all normative work in Rel-14
  MBMS-based service layer
    Expected to be addressed as normative work in Rel-15
    Include addressing all gaps identified in FS_USE_3GPP_4_TV
    Include codecs, encapsulation, service definition, TV centric codecs
On transport-only/pass-through mode
  Work expected to be done outside 3GPP