## Slide 1: A summary of OMAF DIS to SoDIS updates
Ye-Kui Wang
Director, Technical Standards
August 14, 2017

## Slide 2: Updates of DIS to Study of DIS include
Agreements made at the Berlin OMAF AHG meeting on June 1-2, 2017, and
Agreements made at the Torino MPEG meeting (including the weekend OMAF AHG meeting) on July 15-21, 2017.
The summary was made in a hurry, thus can definitely be improved.

## Slide 3
Coordinate systems
Profiles and codecs
Projection
Region-wise packing
Rotation
Content coverage
Fisheye omnidirectional video
Regional metadata
Guard band
Region-wise quality ranking
Sub-picture tracks
Generic signalling
Stereoscopic information signalling
Omnidirectional images
DASH signalling
MMT signalling
Categories of updates

## Slide 4: Coordinate systems
The ISO 23008-3 MPEG-H 3D audio coordinate system is the same as in the current OMAF text, just naming of the axes as X, Y, Z different.
OMAF: forward <-> Z, up <-> Y, right <-> X
23008-3: forward <-> X, up <-> Z, right <-> Y
JVET-Z1005: forward <-> X, up <-> Y, right <-> −Z
Aligned the OMAF coordinate system with MPEG-H audio
Global coordinate system: the default with no rotation
Local coordinate system: after rotation

## Slide 5: Profiles and codecs
Adopted four media profiles
  HEVC viewport independent baseline profile
  HEVC viewport dependent baseline profile
  OMAF 3D audio baseline profile
  OMAF 2D audio legacy profile
Under consideration
  Three additional media profiles
    AVC viewport dependent profile
    HEVC viewport independent fisheye video profile
    Timed text profile
      Either WebVTT or TTML/IMSC1
  A presentation profile
Codecs agreed to be supported
  HEVC Main 10 profile Main tier Level 5.1
  AVC High profile Level 5.1
  MPEG-H 3D Audio Low Complexity profile
  MPEG-4 AAC LC

## Slide 6: Projection
Cubemap projection added
Now both equirectangular projection (ERP) and cubemap projection (CMP) are supported
  The HEVC viewport independent baseline profile supports ERP only
  The HEVC viewport dependent baseline profile supports both ERP and CMP

## Slide 7: Region-wise packing
Signalling of projected and packed regions in relative units
Constrained to only signal he 2D Cartesian content coverage for the HEVC viewport independent baseline profile (without other functionalities like repositioning, resizing, mirroring, rotating of regions)
Projected regions can overlap, for support of the AVC viewport dependent profile.
Packed regions can overlap, for support of “systems-level intra block copy”.
Added back seam support.
Various other improvements.

## Slide 8: Rotation
Rotation equations corrected
By converting a sphere location coordinates to 3D Cartesian coordinates first, then perform 3D Cartesian rotations, and lastly convert 3D Cartesian coordinates back to sphere location coordinates
)

## Slide 9: Content coverage
Indicate the coverage information relative to the global coordinate axes (for both file format level and MPD level signalling)
The coverage information box can be present either in sample description entry or sub-picture composition track group description entry.
  In the former, it describes content coverage of the track itself.
  In the latter, it describes content coverage of the entire content.

## Slide 10: Fisheye omnidirectional video
Allowed fisheye video to be split into sub-pictures before encoding and carried using sub-picture tracks
Allowed use of regional timed metadata with fisheye video
Added explicit signalling of stereoscopic video information such as being stereoscopic or monoscopic, left or right view.

## Slide 11: Regional metadata
Allowed use of regional timed metadata with fisheye video
For recommended viewport timed metadata, added recommended viewport type and a textual description string.

## Slide 12: Guard band
Always signal guard band type separately for each edge.

## Slide 13: Region-wise quality ranking
Signalling optimizations like stereoscopic information indication
Alignment between sphere and 2D signalling

## Slide 14: Sub-picture tracks
Allowed a sub-picture to go across the right picture boundary to the left picture boundary (or in the vertical direction) by a wrapping around operation.
Use a flag in the track header box instead of using a special box for indication of a track not intended to be presented alone.
Added constraints on sub-pictures of one sub-picture composition track group and one alternate group to have neither overlaps nor gaps
Mathematically clearly specified the derivation process of the composition picture.
Allowed track references to refer to track group IDs.

## Slide 15: Generic signalling
Specified the ‘codecs’ parameter of media streams using restricted schemes.
Specified new restricted scheme types for use in media profile definitions.
Allowed signalling of multiple restricted scheme types for one track.

## Slide 16: Stereoscopic information signalling
Added a generic mechanism for stereoscopic video track grouping.
Added stereoscopic information signalling to fisheye video signalling and content coverage signalling.
Improved existing stereoscopic information signalling in region-wise quality ranking signalling, e.g., on frame packing type and the QuincunxSamplingFlag in MPD descriptors.

## Slide 17: Omnidirectional images
Added a clarification that, for single image, the initial viewpoint metadata can be used for appropriate rendering.
Added content coverage metadata for omnidirectional images that are specified as descriptive image properties.
Added fisheye parameters for omnidirectional images that are specified as descriptive image properties.
Added a rotation signalling.

## Slide 18: DASH signalling
Added a descriptor for signalling of 2D region-wise quality ranking.
Added a description on signalling of frame packing in MPD.
Added a description of carriage of timed metadata.
Added a mechamism for grouping of adaptation sets carrying sub-picture composition tracks.
Agreed that for all the MPD descriptors defined in this specification, the values should use the same data format and constraints as in the corresponding file format fields.
Agreed to avoid using of comma separated values, and generate the XML schema whenever a box is defined.
Various other improvements on projection type (PT), region-wise packing format (RWPK), content coverage (CC), region-wise quality ranking (RWQR) descriptors.

## Slide 19: MMT signalling
Added OMAF signalling in MPEG composition information.
Added VR application-specific MMT signalling
  VRInformation asset descriptor
  VRViewDependentSupportQuery
  VRViewDependentSupportResponse
  VRViewportChangeFeedback
  VRViewDependentAssetInformation
  Region guide message
  Stereo video asset descriptor