## Slide 1: TR196 Enhancements Presentation to SA5 & BBF
2016-05-05
SCF Team:
Prabhakar Chitrapu, David Smith (AT&T)
Mark Grayson, Vladimir Yanover (Cisco)
Neil Piercy (ipAccess)
Antonio Garcia (Accelleran)
Tim Carey (Nokia)
Ray Williamson (Huawei)

## Slide 2: Purpose
Clearly define the TR196 enhancements that SCF has identified
Develop a strategy for pursuing them
      Go/No classification
      Organization to pursue Go-items
      Define deliverables
      Prioritization & Time Scale

## Slide 3: Setting the Stage
Small Cell Forum, with its Operator & Vendor members, has a rich history of developing Small Cell Technology, based on 3GPP & BBF standards, sometimes developing solutions ahead of the SDOs in order to cater to the urgent needs of the Small Cell Industry at large. SCF subsequently reached out to appropriate SDOs, either directly or via its member companies to absorb the results in various standards. Crowning Examples:
        Iuh interface between SC & Operator Core Network (3GPP standard)
        FAPI Interface between HW/PHY & SW/Higher Layers in a SC product (DeFacto Industry standard)
Over the years, several other Small Cell technology developments took place, which, for the benefit of the SC Industry at large, deserve to be specified by relevant and larger SDOs. SCF would like to discuss some of them related to TR196 with 3GPP-SA5 and BBF and develop a strategy for standardization, where appropriate.
The topics identified fall into 2 broad categories:
      Those already implemented by SC industry at large
      Those that are being developed currently.

## Slide 4: TR196 Enhancements identified by SCF
Completion of 3GPP Standards Gaps (Antonio)
Virtualisation and the nFAPI interface (Neil)
SON (Rajat)
Carrier Aggregation (Prabhakar)
Provisioning of Edge Based Services (Ray/Andy)
Multi-Operator Support (Mark)

## Slide 5: Completion of 3GPP Standards Gaps

## Slide 6: Completion of 3GPP Standards Gaps 1/3
Background
        A number of important gaps in the LTE parts of the FAPService:2 data model as defined in TR-196 up to and including version 2.1 have been identified
        Currently, any vendor who wants to manage an LTE HeNB using TR-069 would have to add vendor-specific extensions to the FAPService:2 data model in order to be able to configure even a fairly basic, standard, LTE service conforming to 3GPP Release 9 specifications

## Slide 7: Completion of 3GPP Standards Gaps 2/3
Main gaps
        No support for the eNB Name carried in S1AP messages (format/size different from FAPService.{i}.AccessMgmt.LTE.HNBName used for SIB9 broadcasting)
        No support for full range of LTE frequency bands (opportunity for updating definition and descriptive text of FAPService.{i}.CellConfig.LTE.RAN.RF.FreqBandIndicator)
        Insufficient support for S1 handover ‘Target ID’ in neighbour cell object
        No support for RAN sharing in neighbour cell object
        Issues with support for controlling whether optional IEs in SIBs are transmitted or not
        No support for cell selection based on signal quality
        No support for antenna port information for intra-freq cells
        …

## Slide 8: Completion of 3GPP Standards Gaps 3/3
  …
  No support for the allowed measurement bandwidth of neighbour cells being different from the DL bandwidth of the serving cell
  No support for avoiding unnecessary UE measurements of intra-freq cells based on signal quality
  No support for intra-freq cell reselection based on signal quality
  No support for CSG cell identification assistance during intra-freq cell reselection
  No support for antenna port information for inter-freq carriers
  No support for allowed measurement bandwidth for inter-freq carriers
  No support for MBSFN neighbour cell config for inter-freq neighbour cells
  No support for avoiding unnecessary UE measurements of inter-freq and inter-RAT cells based on signal quality
  No support for inter-freq cell reselection based on signal quality
  No support for quality based reselection to lower priority frequencies
  No support for inter-RAT TDD UTRA cell reselection at all
  No explicit support for defining a common set of parameters for cell reselection to multiple inter-RAT GERAN carrier freqs
  No support for access class barring for special ACs
  No support for service specific access class barring

## Slide 9: Virtualisation and the nFAPI interface

## Slide 10: Existing SCF Multi-vendor RAN Decomposition
Recognition that one of the greatest successes of the Forum has been around already defining a small cell RAN decomposition based on SC-API
The key question which initiated these discussion was whether existing FAPI functional decomposition and associated multi-vendor ecosystem can be evolved to be able to support virtualization
SCF published study (SCF106) in June 2014 which recommended a MAC/PHY based approach
Operator Group of SCF triggered formalization on “networked FAPI” (nFAPI) interface
PHY/RF
RLC/MAC
FAPI
Vendor B
Vendor A
Shared
memory
Access
Physical Base Station
PDCP
RRC
TR-
069
PHY
CTRL
SCHEDULER

## Slide 11: Board agreed work item to develop definition of nFAPI central/remote MAC/PHY spilt
Conventional Small Cell
PHY / RF
Layer 2
RRC
S1 / X2 Client
IPsec
GPS / Location
Timing/Sync
SC Management
TLS / IPSec
Small Cell EMS
VNF Centralized Functions
Layer 2
RRC
S1 / X2 Client
IPsec
Timing/Sync
Management
TLS / IPSec
VNF EMS
PNF Remote SC Radio
PNF EMS
Timing/Sync
PNF Management
GPS / Location
PHY / RF
Service Discovery
Service Discovery

## Slide 12: Board agreed work item to develop definition of nFAPI central/remote MAC/PHY spilt
VNF Centralized Functions
Layer 2
RRC
S1 / X2 Client
IPsec
Timing/Sync
Management
TLS / IPSec
VNF EMS
PNF Remote SC Radio
PNF EMS
Timing/Sync
PNF Management
GPS / Location
PHY / RF
Service Discovery
P9
P2
P10
P3
nFAPI Decomposition
P2 – Service Discovery
P3 – Positioning
P4 – NMM
P5 – RF and PHY Control
P7 – MAC-PHY main SAP
P8 – PHY Diagnostics
P9 – OAM
P10 – Synchronization – Frequency, Phase and Time
P5, P7, P8
P4

## Slide 13: Virtualisation and the nFAPI interface: Context of PNF
PNF contains only the eNB PHY
VNF contains the MAC and all upper layer, S1, etc
VNF includes OAM for the complete eNB, including PHY management
PNF OAM limited to:
        Device management
        PHY service partitioning between multiple VNFs

## Slide 14: Virtualisation and the nFAPI interface: Relationship of nFAPI and FAPI

## Slide 15: Virtualisation and the nFAPI interface Structure of PNF Data Model
TR-181i2
  Defines version 2 of the TR-069 Device data model (Device:2). The Device:2 data model applies to all types of TR-069-enabled devices, including End Devices, Residential Gateways, and other Network Infrastructure Devices. It represents a next generation evolution that supersedes both Device:1 and InternetGatewayDevice:1.
  The Device:2 data model consists of a set of data objects covering things like basic device information, time-of-day configuration, network interface and protocol stack configuration, routing and bridging management, throughput statistics, and diagnostic tests. It also defines a baseline profile that specifies a minimum level of data model support.
TR-157
  Defines additional management objects for use in CWMP managed devices including fault management, location management, software module management and security.
TR-262
  Defines Femto specific components which are used to define common functions independent of the Femto devices’ radio technologies.
TR-XXX
  Based on Femto Access Point (FAP) Service Data Model (TR-196)

## Slide 16: Virtualisation and the nFAPI interface: Proposed PNF Data Model Structure
PNF device accommodates one or more PNF services
A PNF service may be an LTE cell and /or Network Monitor.
Each LTE cell accommodates one or more carriers

## Slide 17: Virtualisation and the nFAPI interface: Proposed Data Model objects
A complete object model has been proposed based on TR-196
Could be a new TR-xxx, or could be extra optional objects in TR-196

## Slide 18: SON

## Slide 19: SON
Category 1: Convert scalar to list/range.
For SON to perform optimization, several parameters should be list/range instead of single value.
handover event thresholds and offsets
neighbor cell individual offsets (CIO)
…
Category 2: Missing functions w.r.t. 3gpp
Functions which are omitted from TR-196
X2 configuration. This was added for HeNB in 3gpp later releases and TR-196 should be updated
…
Category 3: Missing functions w.r.t. SCF SON API
Functions which are introduced in SCF SON API
Control over MRO for inter-freq and intra-freq
Frequent handover (ping pong) mitigation
Backhaul monitoring
…

## Slide 20: Carrier Aggregation

## Slide 21: Carrier Aggregation
Carrier Aggregation is an LTE-Advanced feature used to increase bitrate for end users, by increasing the bandwidth.
Carrier aggregation can be used for both FDD and TDD.
Intra-band contiguous (FDD)
Intra-band and inter-band CA alternatives

## Slide 22: Carrier Aggregation
In order to support CA Configurations aligned with Rel-12, the following changes are recommended to TR-196 Issue 2 for the FAPService:2 data model.
Add
1. CellConfig:LTE + LTE
2. Supporting Rel 12 options
3. AccessMgmt: LTE+LTE
4. Capabilities: LTE+LTE
5. FAPControl: LTE+LTE
6. REM:multiple LTE
7. Transport: location mgmt
8. FM: LTE+LTE
9. PM: LTE+LTE
FAPService Issue 2 data model to update

## Slide 23: Multi-Operator Support

## Slide 24: Multi-Operator Support in TR-196 Background
Increasingly, multi-operator is seen as a requirement for small cell deployments, and the ability to serve all venue visitors, irrespective of carrier affiliation
SCF published SCF069, “Enterprises and multi-operator small cells” as part of its Enterprise Release 2 in December 2013 (available from www.scf.io )
The document is currently being revised to update sections to include:
MORAN based sharing
Active DAS based sharing
Sharing based on Wi-Fi technologies (trusted WLANs and un-trusted ePDG based)

## Slide 25: Multi-Operator Support in TR-196 Enhanced Management of Multi-Operator Small Cells
SCF069 examines management aspects of shared small cells and has identified a number of gaps:
Multiple PLMN-IDs for shared small cells: While the LTE MIB defines FAPService.{i}.CellConfig.LTE.EPC.PLMNList.{i}, no equivalent PLMN list is defined for 3G
Qualification of network listen derived neighbour cells: While TR-196v2 PLMN List object can be used by the small cell to qualify network listen derived neighbour cell information, no equivalent capability is defined for 3G
Resource Partitioning: The definition of a shared small cell raises the issue of how to partition the small cell resources between the multiple core network operators and how such information gets configured.

## Slide 26: Strategy
Item | Go/No | SCF/SA5/BBF | Deliverable | Priority | Date
Virtualisation and the nFAPI interface |  |  |  |  | 
SON |  |  |  |  | 
Service level APIs |  |  |  |  | 
Carrier Aggregation |  |  |  |  | 
Completion of 3GPP Standards Gaps |  |  |  |  |