## Slide 1: 3GPP Progress on Network Slicing
NGMN Forum
October 25-26, 2017
Seattle, USA

## Slide 2: 3GPP 5G Timeline
5G release timeline
Two phases for the normative 5G work
  Rel-15 (a.k.a. "5G phase 1")
    to be completed by June 2018
    aim at a first phase of expected 5G deployments in 2020
  Rel-16 (a.k.a. "5G phase 2")
    to be completed by December 2019
    meet the ITU IMT-2020 submission requirements
June 2018
December 2019
March 2017

## Slide 3: Main concepts of Network Slicing
Network slicing is a key feature for the next generation network
  It is about transforming the network/system from a static "one size fits all" paradigm, to a new paradigm where logical networks/partitions are created, with appropriate isolation, resources and optimized topology to serve a particular purpose or service category (e.g. use case/traffic category, or for internal reasons) or even individual customers (logical system created "on demand")
Definitions of network slicing from TS 23.501:
  Network Slice: A logical network that provides specific network capabilities and network characteristics.
  Network Slice instance: A set of Network Function instances and the required resources (e.g. compute, storage and networking resources) which form a deployed Network Slice.

## Slide 4: Main concepts of Network Slicing
Network slices may differ for supported features and network functions optimisations. The operator may deploy multiple Network Slice instances delivering exactly the same features but for different groups of UEs, e.g. as they deliver a different committed service and/or because they may be dedicated to a customer.
A single UE can simultaneously be served by one or more Network Slice instances via a 5G-AN. A single UE may be served by at most eight Network Slice instances at a time.

## Slide 5: 5G Network Slicing in SA1
Service requirements for the 5G system (TS 22.261 Rel-15)
  Specify the concepts, use cases and derives requirements for network slicing in 5G network.
  Identify the requirements for management of network slice, different features and KPIs for different kind of slices, and the association between UEs and slices.
New SID on Business role models for network slicing (Rel-16)
  Examine the business role models for network slicing in order to identify potential requirements that will enable a 3GPP system to adequately support those models
  Study business role models for network slicing, (e.g., monitor, limited control, enhanced control, private slice)
  Study trust relationships and security impacts between MNOs (Mobile Network Operators) and slice tenants under various business role models

## Slide 6: 5G Network Slicing in SA2
Supporting network slicing as a basic mechanism and requirement for the design of 5G network architecture
  Define the concepts/terminologies used for supporting network slicing, e.g. Network slice, Network slice instance.
  Define identifiers relevant to network slice, e.g. SST (Slice Service Type), NSSAI (Network Slice Selection Assistance Information), S-NSSAI etc.
  Define 3 standardized SST values: eMBB, mIoT, URLLC.
  Define network slice selection procedures for UE (User Equipment) accessing network in non-roaming and roaming scenarios.
  Decoupling 5G NFs (Network Functions) to support the flexible deployment of network slice.
Relevant Technical Specifications
  TS 23.501 System Architecture for the 5G System
  TS 23.502 Procedures for the 5G System
  TS 23.503 Policy and Charging Control Framework for the 5G System

## Slide 7: 5G Network Slicing in SA2
The design of network architecture supports UE accessing to one or multiple network slices simultaneously.
  Introduce standalone NSSF (Network Slice Selection Function) for network slice selection.
  To support the case with UE accessing to multiple network slices simultaneously, some NFs, e.g. AMF (Access and Mobility Management Function) can be shared by multiple network slices, while other NFs shall be network slice specific.
  UE traffics of a specific session are transferred within one specific network slice to ensure the handling of traffics can be customized and isolated from other network slices.

## Slide 8: 5G Network Slicing in SA3
3GPP SA3 is responsible for addressing all security issues relevant to network slicing encountered in any other working group or SDO
  This includes, but is not limited to, SA2, SA5, RAN3, RAN2, etc.
  NGMN requirements and use cases will be considered as input
Study on the security aspects of the next generation system (TR 33.899)
  Collection of threats, potential requirements and solutions for the security of next generation mobile networks.
  Network slicing security, as one of security areas for 5G, covers security issues related to slice isolation, slice security mechanism differentiation, UE access to slices etc.

## Slide 9: 5G Network Slicing in SA3
Study on security aspect of 5G Network Slicing Management (TR 33.811)
  Investigate and make recommendations on security aspects of features described in TS 28.530 and TS 28.531 for network slicing:
  1) TS 28.530 Management of Network Slicing in Mobile Networks, Concepts, Use cases and Requirements
  2) TS 28.531 Provisioning of network slicing for 5G networks and services
  The work in ETSI NFV and NGMN on this topic will also be taken into account.
Security aspects of 5G System - Phase 1 (TS 33.501 )
  Specify the security architecture, i.e., the security features and the security mechanisms for the 5G System, and the security procedures performed within the 5G System including the 5G Core and the 5G New Radio.
  Security procedure and privacy related to network slice selection assistance information (NSSAI) will be specified.

## Slide 10: 5G Network Slicing in SA5
Study on management and orchestration of network slicing for next generation network (TR 28.801)
  Identify management concepts, use cases, potential requirements and potential solutions for lifecycle management, fault management, configuration management, performance management, and policy management for network slicing
  Identify three management functions, CSMF (Communication Service Management Function), NSMF (Network Slice Management Function) and NSSMF (Network Subnet Slice Management Function), involved in management and orchestration of network slicing
Management of network slicing in mobile networks, concepts, use cases and requirements (TS 28.530)
  Specify the concepts, use cases and requirements for management of network slicing in mobile networks
  The interfaces and information exchanged between the different management entities (e.g. CSMF, NSMF, NSSMF) will be described.
  The specification of the management architecture, interfaces and information exchange will be done separately in other work items belonging to this feature
Network slice related management functions

## Slide 11: 5G Network Slicing in SA5
Provisioning of network slicing for 5G networks and services (TS 28.531)
  Specify use cases and requirements for provisioning of network slices for 5G networks and services
  Specify solutions to enable the provisioning of network slices for 5G networks and services
    Specify the information model to support different Slice/Service type;
    Specify the information model and interfaces to handle service requirements associated to the network slice;
    Specify network slice template and define the relation of network slice template and network slice instance;
    Specify the procedures for provisioning of network slices instance;
    Specify the protocol-independent information model of network slice and slice subnet;
    Specify the corresponding solution sets.

## Slide 12: 5G Network Slicing in SA5
The 3GPP management system directly manages only the parts of the network that consist of network functions specified in 3GPP. For the network functions specified in other SDOs, elements of indirect management can be addressed
For example, regarding the TN (Transport Network) part supporting connectivity within and between CN (Core Network) and RAN (Radio Access Network) parts, 3GPP management system may provide link requirements (e.g. topology, QOS parameters) to the TN management system
SA5 will identify relevant standard groups and industry fora, and trigger the cooperation with them to address the elements of indirect management for the non-3GPP network functions
NGMN NWMO requirements and use cases will be considered as input

## Slide 13: 5G Network Slicing in SA5
High-level business roles (TR 28.801) include:
  Communication Service Customer (CSC): Uses communication services.
  Communication Service Provider (CSP): Provides communication services. Designs, builds and operates its communication services.
  Network Operator (NOP): Provides network services. Designs, builds and operates its networks to offer such services.
  Virtualization Infrastructure Service Provider (VISP): Provides virtualized infrastructure services. Designs, builds and operates its virtualization infrastructure(s). VISP may also offer their virtualized infrastructure services to other types of customers including to CSPs directly, i.e. without going through the NOP.
  Data Centre Service Provider (DCSP): Provides data centre services. Designs, builds and operates its data centres.
  Network Equipment Provider (NEP): Supplies network equipment. For sake of simplicity, VNF Supplier is considered here as a type of NEP.
  NFVI Supplier: Supplies network function virtualization infrastructure to its customers.
  Hardware Supplier: Supplies hardware.
  Depending on actual deployments, the roles defined above can be played by one single organization or by several ones.

## Slide 14: 5G Network Slicing in SA5
Use cases related to Network Slice management (TR 28.801)
  Network Slice Instance(s) lifecycle management
  Network Slice Instance(s) fault management
  Network Slice Instance(s) performance management
  Network Slice Instance(s) configuration management
  Network Slice Instance(s) policy management
  Communication service support with network slice
  Management data isolation
  Multiple operator coordination management
  Automation of the network slice management
  Other Network Slice Instance(s) management use cases
Use cases related to Network Slice Subnet(s) management (TR 28.801)
  Network Slice Subnet Instance(s) lifecycle management
  Network Slice Subnet Instance(s) fault management
  Network Slice Subnet Instance(s) performance management
  Network Slice Subnet Instance(s) configuration management
  Other Network Slice Subnet Instance(s) management use cases

## Slide 15: SA5 5G WIDs approved in October 2017
TDoc | Title | Source
S5-175463 | Management of 5G networks that include virtualized network functions | Intel
S5-175464 | Network Resource Model (NRM) Integration Reference Point (IRP) for 5G network functions management | Nokia
S5-175466 | Fault Supervision for 5G network and network slicing | ZTE
S5-175487 | Assurance data and Performance Management for 5G networks and network slicing | China Mobile, Intel
Note: These WIDs will be submitted to TSG SA#78 for approval in December 2017 but SA5 will start some preliminary work at November 2017 SA5 meeting.

## Slide 16
Study on charging aspects of 5G system architecture Phase 1 (TR 32.899)
  Specify the evolution of charging architecture to support the Network slicing, including relationship between charging system and network slicing;
  Specify the key issues, potential charging requirement and solution for a single UE served by one or more Network Slice Instances;
  Specify the key issues, potential charging requirement and solution for a CSP (also referred to as "Tenant“, Provides communication services Designs, builds and operates its communication services) who utilizes a specific Network Slice Instance.
SA5 Charging will consider the business scenarios and charging requirements from NGMN
5G Network Slicing in SA5 - Charging

## Slide 17: Relationships between 3GPP SA5 and other SDOs/fora
GSMA
  Indicated their expectation to collaborate with 3GPP on Network Slicing (incl. SA5) – LS at SA5#114 (S5-174046)
BBF
  Indicated their expectation to collaborate with 3GPP SA5 – LS at SA5#114 (S5-174085)
  SA5 sent the reply LS on cooperation on Network Slicing in S5-174382
IETF
  Asked to 3GPP: "Does 3GPP currently have dedicated requirements for any kind of IETF protocol or activity related to nw-slicing?"
  Answer from 3GPP Liaison Officer at IETF 99 (July 2017): "At the moment: No."
  Has initiated several Internet Drafts in Network Slicing, incl. Network Slicing – 3GPP Use Case (https://datatracker.ietf.org/doc/draft-defoy-netslices-3gpp-network-slicing/)
ETSI NFV
  EVE, in their Report on Network Slicing Support with ETSI NFV Architecture Framework, is making a deep analysis of 3GPP TR 28.801

## Slide 18
RAN2 targets that RAN solutions for network slicing should be able to support a large number of slices (e.g. hundreds of slices) (latest RAN2#99 Agreements)
  From UE perspective, the UE can be configured to support the requirements of the supported slices (e.g. by appropriate configuration of different DRBs of different PDU (Protocol Data Unit) sessions)
  For intra-frequency cell reselection the UE try to always camp on the best cell
  For needs of slicing, appropriate configuration of the dedicated priorities provided from the gNB can be used to control the frequency on which the UE camps. (i.e. reuse of same mechanism as in LTE)
  We will not support additional functionality for RACH resource isolation/differentiated treatment for slicing for Rel-15
  RAN2 assumption is that MSG5 is the earliest message that can be used to deliver assistance information for AMF selection
5G Network Slicing in RAN2

## Slide 19
General Principles and Requirements (TS 38.300)
  RAN awareness of slices to support a differentiated handling of traffic for different network slices
  Resource management between slices as per service level agreements
  Support of QoS (Quality of Service) differentiation within a slice
  RAN selection of CN entity
  Resource isolation between slices by means of RRM policies
  Slice Availability as some slices may be available only in part of the network
  Support for UE associating with multiple network slices simultaneously
  PDU session granularity of slice awareness
  Validation of the UE rights to access a network slice
5G Network Slicing in RAN3

## Slide 20
Slice-aware Signalling aspects (TS 38.413 and TS 38.423)
  CN Instance and NW Slice Selection
    NG-RAN selects AMF based on a Temp ID or assistance information provided by the UE over RRC
  PDU Session Handling/UE Context Handling
    S-NSSAI information is added per PDU session, so NG-RAN is enabled to apply policies at PDU session level according to the SLA (Service Level Agreement) represented by the network slice, while still being able to apply (for example) differentiated QoS within the slice
  Mobility
    S-NSSAI is introduced as part of the PDU session information that is transferred during mobility signalling. This enables slice-aware admission and congestion control
  Dual connectivity
    S-NSSAI is transferred per associated PDU session during SN addition procedure
5G Network Slicing in RAN3

## Slide 21: NGMN slicing concepts are reflected in 3GPP / SA5
The network slicing conceptual outline from NGMN (see NGMN Description of Network Slicing Concept v1.0.8, September 2016) has been reflected in 3GPP
The network slicing concept consists of 3 layers (TR 28.801):
Service Instance Layer
Network Slice Instance Layer
Resource layer

## Slide 22: NGMN slicing architecture is considered in 3GPP
The NGMN network slicing architecture (see NGMN 5G End-to-End Architecture Framework v0.8.1, September 2017) is considered in 3GPP ongoing work, such as
  The scope of a network slice is end to end.
  The 5G network shall be capable of slicing by service categories that consist of enhanced Mobile Broadband (eMBB), massive Internet of Things (mIoT), Ultra-Reliable Low-Latency Communication (URLLC), and other new arising categories
  The 5G system shall allow a common core network associated with one or more access networks to be part of a network slice (e.g. fixed and mobile access within the same network slice)
  Network Slicing – single administrative domain
  Network Slicing – multiple administrative domains

## Slide 23: NGMN slicing definitions and scenarios are considered in 3GPP
NGMN network slicing definitions (see NGMN Description of Network Slicing Concept v1.0.8, September 2016) are considered as input for the network slicing definitions of 3GPP specification
Scenarios with multiple service providers (see NGMN Description of Network Slicing Concept v1.0.8, September 2016) are considered in 3GPP ongoing work
  Two general categories of scenarios where network services need to be provided across multiple service providers:
    Roaming scenario
    Business verticals

## Slide 24: ANNEX

## Slide 25: 3GPP Structure
TSG RAN Radio Access Network
RAN WG1 Radio Layer 1 spec
RAN WG2 Radio Layer 2 spec Radio Layer 3 RR spec
RAN WG3 lub spec, lur spec, lu spec UTRAN O&M requirements
RAN WG4 Radio Performance Protocol aspects
RAN WG5 Mobile Terminal Conformance Testing
RAN WG6 GSM EDGE Radio Access Network
TSG SA Service & Systems Aspects
SA WG1 Services
SA WG2 Architecture
SA WG3 Security
SA WG4 Codec
SA WG5 Telecom Management
SA WG6 Mission-critical applications
TSG CT Core Network & Terminals
CT WG1 MM/CC/SM (lu)
CT WG3 Interworking with external networks
CT WG4 MAP/GTP/BCH/SS
CT WG6 Smart Card Application Aspects
Project Co-ordination Group (PCG)

## Slide 26
Organizational Partners (SDOs)
Organizational Partners
  ARIB (Japan)
  ATIS (USA)
  CCSA (China)
ETSI (Europe)
TTA (Korea)
TTC (Japan)
TSDSI (India)

## Slide 27
Market Representative Partners
  17 Market partners representing the broader industry:
Market Representative Partners
5G Americas, 5G Infrastructure Association, COAI (India), CTIA, GCF, GSA, GSMA, IPV6 Forum, | MDG (formerly CDG), NGMN Alliance, Public Safety Communication Europe (PSCE) Forum, Small Cell Forum, TCCA, TD Industry Alliance, TD-Forum, Wireless Broadband Alliance NEW: 5G Automotive Association (5GAA)

## Slide 28: The 3GPP-centric standards map
ITU-R/T
Reference to 3GPP specs
SDO Partners govern the project & transpose 3GPP specs locally
Cross reference
Direct
Requirements
Japan
EU
Korea
China
North America
3GPP Market Partners
Terminal certification based on 3GPP specs
India
5G Projects
Requirements
via
Member
contributions

## Slide 29
~400 Companies from 39 Countries
50.000 delegate days per year
40.000 documents per year
1.200 specs per Release
New Release every ~18 months
3GPP Facts and Figures
Chart: 
| 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017
R99 | 1408 | 4398 | 2266 | 1004 | 581 | 512 | 111 | 42 | 23 | 5 | 5 | 1 | 0 | 0 | 0 | 0
Rel-4 | 376 | 2828 | 1900 | 690 | 257 | 122 | 63 | 48 | 22 | 20 | 13 | 11 | 8 | 7 | 2
Rel-5 | 27 | 644 | 3274 | 2842 | 2162 | 1357 | 509 | 94 | 25 | 22 | 7 | 7 | 5 | 3 | 2
Rel-6 | 172 | 1088 | 2458 | 3721 | 2074 | 1078 | 212 | 74 | 19 | 17 | 10 | 4 | 4
Rel-7 | 1 | 20 | 663 | 2529 | 3132 | 1262 | 492 | 176 | 91 | 43 | 25 | 15
Rel-8 | 49 | 777 | 4609 | 7073 | 2347 | 706 | 347 | 184 | 91 | 46 | 22 | 6
Rel-9 | 49 | 2918 | 4991 | 3252 | 1366 | 376 | 165 | 70 | 26 | 17
Rel-10 | 47 | 1722 | 3800 | 3103 | 1636 | 584 | 267 | 50 | 13
Rel-11 | 32 | 1152 | 4178 | 3525 | 2186 | 622 | 163 | 22
Rel-12 | 6 | 102 | 2254 | 5181 | 4287 | 1530 | 127
Rel-13 | 8 | 200 | 2648 | 5571 | 1214
Rel-14 | 24 | 2315 | 3269
R99
R4
R5
R6
R7
R8
R9
R10
R11
R12
R13
R14
Approved CRs per year per Release

## Slide 30
  AMF Access and Mobility Management Function
  CN Core Network
  CSMF Communication Service Management Function
  CSC Communication Service Customer
  CSP Communication Service Provider
  DCSP Data Centre Service Provider
  MNO Mobile Network Operator
  NEP Network Equipment Provider
  NF Network Function
  NOP Network Operator
Acronyms

## Slide 31
  NSSAI Network Slice Selection Assistance Information
  NSSF Network Slice Selection Function
  NSMF Network Slice Management Function
  NSSMF Network Slice Subnet Management Function
  PDU Protocol Data Unit
  QoS Quality of Service
  RAN Radio Access Network
  SLA Service Level Agreement
  SDO Standards Developing Organization
  TN Transport Network
  UE User Equipment
  VISP Virtualization Infrastructure Service Provider
Acronyms

## Slide 32
SA1
  TS 22.261 Service requirements for next generation new services and markets
SA2
  TS 23.501 System Architecture for the 5G System
  TS 23.502 Procedures for the 5G System
  TS 23.503 Policy and Charging Control Framework for the 5G System
SA3
  TR 33.899 Study on the security aspects of the next generation system
  TS 33.501 Security aspects of 5G System - Phase 1
  TR 33.811 Study on security aspects of 5G Network Slicing Management
Technical Reports and Specifications

## Slide 33
SA5
  TR 28.801 Study on management and orchestration of network slicing for next generation network
  TR 32.899 Study on charging aspects of 5G system architecture Phase 1
  TS 28.530 Management of network slicing in mobile networks; Concepts, use cases and requirements
  TS 28.531 Provisioning of network slicing for 5G networks and services
RAN2
  TS 38.300 NR; Overall description; Stage 2
RAN3
  TS 38.413 NG-RAN; NG Application Protocol (NGAP)
  TS 38.423 NG-RAN; Xn Application Protocol (XnAP)
Technical Reports and Specifications

## Slide 34
www.3gpp.org
contact@3gpp.org
Thank You!