## Slide 1: SA5 OAM&P SWG Exec Report SA5#124, 25 February – 1 March 2019 Taipei (Taiwan)
Jean-Michel CORNILY, SA5 Vice-Chair, ORANGE
Christian TOCHE, SA5 Vice-Chair, HUAWEI

## Slide 2: Incoming LSs
Tdoc | Title | Source | Decision | ReplyIn
S5-192046 | Resubmitted LS from ITU-T to SA5 on Draft new Recommendation E.RQST – “KPI targets for mobile networks” | ITU-T SG12 | available | 
S5-192047 | Resubmitted LS from ITU-T to SA5 - Update of Technical Report – “Transport network support of IMT-2020/5G” | ITU-T SG15 | replied to | S5-192304
S5-192049 | Reply LS from SA2 to SA5 on Slice related Data Analytics | S2-1901294 | replied to | S5-192308
S5-192050 | Ls from SA2 ccSA5 on providing information on SLA fulfilment to NG-RAN | S2-1901382 | replied to | S5-192309
S5-192051 | Ls from SA4 cc SA5 on Collection of Slice Related Data Analytics from UEs | S4-190195 | replied to | S5-192310

## Slide 3: Outgoing LSs
Tdoc | Title | To | Cc | ReplyTo
S5-192308 | LS on Reply LS on Slice related Data Analytics | SA2 |  | S5-192049
S5-192309 | Reply to: Ls from SA2 ccSA5 on providing information on SLA fulfilment to NG-RAN | SA2, RAN2 | RAN3 | S5-192050
S5-192310 | Reply to: Ls from SA4 cc SA5 on Collection of Slice Related Data Analytics from Ues For e-mail approval |  |  | S5-192051
S5-192454 | LS on PCF and NEF discovery for Edge Computing | SA2 |  | 

## Slide 4
New or Revised Work Items / Study Items
Tdoc | Type | Title | Source
S5-192150 | WID revised | Updated WID Performance assurance for 5G networks including network slicing | Intel
S5-192176 | WID revised | Revised WID on discovery of management services in 5G | Huawei
S5-192411 | WID revised | Revised WID on NRM enhancements | Nokia, Nokia Shanghai Bell

## Slide 5
OAM&P Maintenance and Rel-16 small Enhancements
CRs for approval by SA5 closing plenary (1/4)
TDoc | Title | Source
S5-192145 | Rel-16 CR 28.552 Add measurements related to registration via untrusted non-3GPP access for AMF | Intel
S5-192149 | Rel-16 CR 32.425 Add measurements related to WLAN connection status report | Intel
S5-192181 | Correct cardinality of EP to target | Ericsson
S5-192183 | Remove ExternalNRCellCU.pLMNIdList | Ericsson
S5-192184 | Use bS (not bs) to prefix all BS attributes | Ericsson
S5-192192 | Update 5G JSON Solution Set to align with generic NRM | Nokia, Nokia Shanghai Bell
S5-192230 | Rel-15 CR 28.628 Correction of AAS IP Throughput load rate definition | P.I. WORKS
S5-192313 | Rel-15 CR 28.541 Correct the definition of nSSIId | Huawei
S5-192314 | Rel-15 CR 28.541 Add missing attribute constraints for class definition of NSSFFunction | Huawei
S5-192316 | Rel-15 CR 28.541 Correct attribute constraints for RRMpolicy related attributes in NRCellCU | Huawei

## Slide 6
OAM&P Maintenance and Rel-16 small Enhancements
CRs for approval by SA5 closing plenary (2/4)
TDoc | Title | Source
S5-192317 | Rel-15 CR 28.550 Add the missing RESTFul API definitions | Intel
S5-192318 | Rel-15 CR 28.531 Correct management service term | Huawei
S5-192319 | Rel-16 CR 28.531 Correct management service term | Huawei
S5-192321 | Correct Import table | Ericsson
S5-192322 | Correct PLMN Id definition | Ericsson
S5-192323 | Correction of State attributes descriptions | Ericsson
S5-192324 | Update State management SS to support JSON | Nokia, Nokia Shanghai Bell
S5-192325 | Update Generic NRM Solution Set to support JSON | Nokia, Nokia Shanghai Bell
S5-192326 | Update YANG Solution Set to align with Stage 2 definition | Nokia, Nokia Shanghai Bell
S5-192327 | Update Information Service to fix Network Slice modeling issue | Nokia, Nokia Shanghai Bell

## Slide 7
OAM&P Maintenance and Rel-16 small Enhancements
CRs for approval by SA5 closing plenary (3/4)
TDoc | Title | Source
S5-192328 | Update Solution Set to fix Network Slice modeling issue | Nokia, Nokia Shanghai Bell
S5-192329 | Add availability in service profile of network slice resource model | Nokia, Nokia Shanghai Bell
S5-192330 | Rel-15 CR 28.541 Align the term mFIdList and constituentNSSIIdList | Huawei,Ericsson
S5-192333 | CR Rel-16 28.541 Name datatypes SliceProfile and ServiceProfile | Ericsson
S5-192334 | CR Rel-16 28.541 Add datatype definition for S-NSSAI | Ericsson
S5-192335 | CR Rel-16 28.541 Add datatype definition for TAC | Ericsson
S5-192336 | CR Rel-15 28.541 Name datatype RRMPolicyRatio2 | Ericsson
S5-192338 | Correct the DN to URI mapping rules | Nokia
S5-192350 | Rel-15 CR 28.550 Correction on MDAS | Intel
S5-192371 | Rel-16 CR 28.550 Add operations for establishing and terminating streaming connection | Intel

## Slide 8
OAM&P Maintenance and Rel-16 small Enhancements
CRs for approval by SA5 closing plenary (4/4)
TDoc | Title | Source
S5-192377 | Rel-16 CR TS 28.552 Add measurements of RRC connection re-establishment | ZTE, China Mobile
S5-192378 | Rel-16 CR TS 28.552 Add measurements of RRC connection resume | ZTE, China Mobile
S5-192381 | Add use case and definitions of QoS level measurement over N3 | ETRI
S5-192383 | Rel-16 CR 28.552 Add measurements related to inter-AMF handover | Intel
S5-192400 | Update definition of mean number of PDU sessions KPI | ETRI
S5-192401 | Rel-16 CR 28.552 Correction of percentage unrestricted volume measurements | P.I. WORKS
S5-192402 | Rel-15 CR 28.552 Correction of percentage unrestricted volume measurements | P.I. Works
S5-192418 | Rel-15 CR 28.541 Update to sST attribute stage 3 | Ericsson
S5-192434 | Rel-15 CR 28.541 Add sST attribute to ServiceProfile | Ericsson
S5-192436 | CR Rel-16 28.541 Add datatype definition for CoverageAreaTA | Ericsson
S5-192441 | Rel-16 CR 28.552 Add mean radio resource utilization of network slice instance measurements | Huawei

## Slide 9
Documents endorsed by OA&M SWG
TDoc | Title | Source
S5-192331 | Discussion paper around sST attribute | Ericsson
S5-192375 | Discussion paper on TS 28.552 re-organization approach | Huawei
S5-192389 | TD Support Service Managed Object | Nokia, Nokia Shanghai Bell
S5-192410 | TD Support State of Managed Service | Nokia, Nokia Shanghai Bell
S5-192451 | Discussion paper on lifecycle management of communication services | Ericsson
S5-192453 | Discussion paper on discovery of MnS in 5G | Huawei
S5-192456 | TD Support Registration State of Managed Service | Nokia, Nokia Shanghai Bell

## Slide 10
Rel-16 OAM&P WIs (1/11)
Work Item | Management of QoE measurement collection |  | QOED
 |  |  | 760058
Rapporteur | Ericsson | Percentage of completion | 50% -> 55%
Target | SA#85 – Sep. 2019 | Main TSs | TS 28.404, 28.405, 28.406, 28.307, 28.308, 28.309
Summary of progress | Activating and reporting in UTRAN are clarified with sequence diagram and textual description; Handling of QoE measurement handling during handover between RNCs in UTRAN is specified; TS 28.404 is updated according to comments from Edithelp. |  | 
Outstanding issues | None. |  | 
Documents for approval by SA5 | None. |  | 

## Slide 11
Rel-16 OAM&P WIs (2/11)
Work Item | Energy efficiency of 5G |  | EE_5G
 |  |  | 810023
Rapporteur | Orange | Percentage of completion | 40% -> 40 %
Target | SA#86 – Dec. 2019 | Main TSs | TS 28.310
Summary of progress | One discussion paper on data volume measurements in NG-RAN for EE purposes was discussed. After discussions, it was agreed that, due that gNB can be multi-vendor and split (or not), it is necessary to define PEE measurements per gNB component, and aggregate them at gNB level. For non-split gNBs, the PEE measurement could be done at the ManagedElement level, provided that the subject ME does not contain other network functions (e.g. UPF) as well. It was agreed that more discussion is needed on this. |  | 
Outstanding issues | None. |  | 
Documents for approval by SA5 | None. |  | 

## Slide 12
Rel-16 OAM&P WIs (3/11)
Work Item | OAM aspects of LTE and WLAN integration |  | OAM_LTE_WLAN
 |  |  | 810024
Rapporteur | Intel | Percentage of completion | 80% -> 100%
Target | SA#84 – June 2019 | Main TSs | 
Summary of progress | The WLAN status report related measurements have been discussed and agreed The WI is completed. |  | 
Outstanding issues | None. |  | 
Documents for approval by SA5 | One CR. |  | 

## Slide 13
OAM aspects of LTE and WLAN integration
CRs for approval by SA5 closing plenary
TDoc | Title | Source
S5-192149 | Rel-16 CR 32.425 Add measurements related to WLAN connection status report | Intel

## Slide 14
Rel-16 OAM&P WIs (4/11)
Work Item | Network policy management for mobile networks based on NFV scenarios |  | NETPOL
 |  |  | 810025
Rapporteur | China Mobile | Percentage of completion | 10% -> 10%
Target | SA#85 – Sept. 2019 | Main TSs | TS 28.311
Summary of progress | No session at this meeting. |  | 
Outstanding issues | None. |  | 
Documents for approval by SA5 | None. |  | 

## Slide 15
Rel-16 OAM&P WIs (5/11)
Work Item | Methodology for 5G management specifications |  | METHOGY
 |  |  | 810026
Rapporteur | Ericsson | Percentage of completion | 80% -> 85%
Target | SA#84 – June 2019 (Previously SA#83 – March 2019) | Main TSs | TS 32.160
Summary of progress | As input to the meeting there were 8 contributions amongst which 2 were discussion papers. Further discussion is needed to resolve the question on which rules/style guidelines are needed for stage 2 to stage 3 mapping to Yang, XML and JSON. It was agreed that a smaller group would work on this during the week. |  | 
Outstanding issues | None. |  | 
Documents for approval by SA5 | None. |  | 

## Slide 16
Rel-16 OAM&P WIs (6/11)
Work Item | Intent driven management services for mobile networks |  | IDMS_MN
 |  |  | 810027
Rapporteur | Huawei | Percentage of completion | 60% -> 30%
Target | SA#86 – Dec. 2019 (Previously SA#84 – June 2019) | Main TSs | TR 28.812, TS 28.312
Summary of progress | Percentage of completion: overall 30%. The work item includes a study phase and a work item phase: Study phase 65 % (previously 60%); Work item phase is not started. Concept of IDMS, some intent driven use cases, the relation between intent and automation have been discussed. |  | 
Outstanding issues | None. |  | 
Documents for approval by SA5 | None. |  | 

## Slide 17
Rel-16 OAM&P WIs (7/11)
Work Item | Enhancement of performance assurance for 5G networks including network slicing |  |  | 5G_SLICE_ePA
 |  |  |  | 810031
Rapporteur | Intel, China Mobile | Percentage of completion |  | 50% -> 60%
Target | SA#86 – Dec. 2019 (Previously SA#84 – June 2019) | Main TSs |  | TS 28.550, 28.552, 28.554
Summary of progress | The group discussed the following topics: |  |  | 
 | Threshold monitoring service; Threshold monitor IOCs; Performance data streaming operations; Update of the WID; Restructure of TS 28.552; E-UTRA-NR Dual Connectivity related measurements; Measurements related to RRC connection re-establishment; Measurements related to RRC connection resume; RSRP measurements for Beams; TA related measurements; PDCP data volume in DC scenario; PDCP throughput measurements; |  | QoS flow measurements for N3; Packet loss rate measurement over N3; Measurements related to registration via untrusted non-3GPP access; Measurements related to inter-AMF handover; PDCP split volume measurements; Mean radio resource utilization of network slice instance measurements; KPI and measurements on DRB retainability; LS to RAN on data activity reporting; Update definition of mean number of PDU sessions KPI; Correction of percentage unrestricted volume measurements. | 
Outstanding issues | None. |  |  | 
Documents for approval by SA5 | CRs – see next slide. |  |  | 

## Slide 18
Rel-16 OAM&P WIs (8/11)
Work Item | Discovery of management services in 5G |  | 5GDMS
 |  |  | 820035
Rapporteur | Huawei | Percentage of completion | 15% -> 25%
Target | SA#85 – Sept. 2019 (Previously SA#84 – June 2019) | Main TSs | 
Summary of progress | As input to the meeting there were 5 contributions, amongst which 1 was a late contribution. All available contributions, besides 1 late contribution, were treated. The group discussed: MnS discovery approach available options and way forward; Stage 1 discovery of MnS access information use case; Stage 1 discovery of MnS access information use case related requirements; Stage 1 MnS exposure governance use case; Stage 1 MnS exposure governance use case related requirements. |  | 
Outstanding issues | Revised WID (S5-192176). |  | 
Documents for approval by SA5 | None. |  | 

## Slide 19
Rel-16 OAM&P WIs (9/11)
Work Item | NRM enhancements |  | eNRM
 |  |  | 820032
Rapporteur | Nokia | Percentage of completion | 0% -> 10%
Target | SA#85 – Sept. 2019 (Previously SA#84 – June 2019) | Main TSs | 
Summary of progress | During this meeting, 3 contributions were discussed for endorsement, which proposed Network Resource Model (NRM) definition for managed service IOC and constituted attributes, especially state and registration state of the managed service. Updated the WID to add impacted TSs and time scale. |  | 
Outstanding issues | Revised WID (S5-192411). |  | 
Documents for approval by SA5 | None. |  | 

## Slide 20
Rel-16 OAM&P WIs (10/11)
Work Item | Trace Management in the context of Services Based Management Architecture |  | TM_SBMA
 |  |  | 820036
Rapporteur | Nokia | Percentage of completion | 0% -> 0%
Target | SA#84 – June 2019 | Main TSs | 
Summary of progress | No session at this meeting. |  | 
Outstanding issues | None. |  | 
Documents for approval by SA5 | None. |  | 

## Slide 21
Rel-16 OAM&P WIs (11/11)
Work Item | Integration of ONAP and 3GPP 5G management framework (Preliminary work before SA approval) |  | ONAP3GPP
 |  |  | ??????
Rapporteur | AT&T | Percentage of completion | 0% -> 5%
Target | SA#87 - March 2020 | Main TSs | 
Summary of progress | A draft CR proposed an approach to produce a new RESTful JSON solutions set for the integration of the fault supervision data report service with the ONAP VES Collector. Questions have been raised on: The support of notifyNewAlarm parameter ‘eventType’. Solved during offline discussion (eventType is an attribute of IOC AlarmNotification, not a parameter of the notification); Resource names – to be studied further; The column ‘SS parameter location’: during offline discussion, it was agreed that this column can be deleted as it brings no value. An updated (draft) CR will be submitted at next meeting, based on the comments received. |  | 
Outstanding issues | None. |  | 
Documents for approval by SA5 | None. |  | 

## Slide 22
OAM&P SIs (1/10)
Study Item | Study on integration of ONAP DCAE and 3GPP management architecture |  | FS_ONAPDCAE
 |  |  | 780031
Rapporteur | AT&T, Orange | Percentage of completion | 95% -> 100%
Target | SA#83 – March 2019 | Main TR | TR 28.890 (Previously TR 28.900)
Summary of progress | One pCR dealing with Heartbeat and Communication Surveillance was presented, discussed, and approved. After the session, it was agreed that the existing empty clause 7 (Overall conclusion) will be deleted by the Rapporteur when implementing agreed pCRs. |  | 
Outstanding issues | TR 28.890 to be sent out to SA#83 for Approval (cf. S5-192270). |  | 
Documents | One pCR. |  | 

## Slide 23
OAM&P SIs (2/10)
Study Item | Study on integration of ONAP and 3GPP configuration management services for 5G networks |  | FS_ONAPCINT
 |  |  | 800038
Rapporteur | Ericsson | Percentage of completion | 61% -> 100%
Target | SA#83 – March 2019 | Main TR | TR 28.890 (Previously TR 28.900)
Summary of progress | The following pCRs on ONAP integration for CM have been discussed: Configuration Management handling Add Handling of configuration notification Technical Corrections Add the description of SDNC add the description of 3GPP provisioning management service Conclusion on CM After the session, it was agreed that the existing empty clause 7 (Overall conclusion) will be deleted by the Rapporteur when implementing agreed pCRs. |  | 
Outstanding issues | TR 28.890 to be sent out to SA#83 for Approval (cf. S5-192270). |  | 
Documents | pCRs. |  | 

## Slide 24
OAM&P SIs (3/10)
Study Item | Study on protocol enhancement for real time communication |  | FS_PROTIMP
 |  |  | 800037
Rapporteur | Nokia | Percentage of completion | 0% -> 0%
Target | SA#83 – March 2019 | Main TR | TR 28.823
Summary of progress | No session at this meeting. |  | 
Outstanding issues | None. |  | 
Documents | None. |  | 

## Slide 25
OAM&P SIs (4/10)
Study Item | Study on management aspects of edge computing |  | FS_MAN_EC
 |  |  | 800039
Rapporteur | Intel | Percentage of completion | 40% -> 50%
Target | SA#85 – Sept. 2019 (Previously SA#83 – March 2019) | Main TR | TR 28.803
Summary of progress | The group discussed the following contributions: Add a use case for performance measurements related to end-to-end QoS; Add a solution for edge computing deployment Add use case on PCF and NEF discovery for EC [Draft] LS on PCF and NEF discovery for Edge Computing |  | 
Outstanding issues | None. |  | 
Documents | pCRs. |  | 

## Slide 26
OAM&P SIs (5/10)
Study Item | Study on tenancy concept in 5G networks and network slicing management |  | FS_TENANCYC
 |  |  | 810022
Rapporteur | Huawei | Percentage of completion | 25% -> 25%
Target | SA#85 – Sept. 2019 (Previously SA#84 – June 2019) | Main TR | TR 28.804
Summary of progress | As input to the meeting there were 6 contributions. All contributions were treated. The group discussed the tenancy concept in context of: Add managed data isolation concept Add use case for dedicated performance measurement data Add use case for 3GPP network represented as tenant in NFV MANO Add tenant types Add potential solutions and recommendations |  | 
Outstanding issues | None. |  | 
Documents | pCRs. |  | 

## Slide 27
OAM&P SIs (6/10)
Study Item | Study on management aspects of communication services |  | FS_CSMAN
 |  |  | 810029
Rapporteur | Ericsson | Percentage of completion | 60% -> 70%
Target | SA#85 – Sept. 2019 (Previously SA#84 – June 2019) | Main TR | TR 28.805
Summary of progress | As input to the meeting there were 18 contributions amongst which 8 were late and not treated. The treated contributions include: discussion paper on concept, discussion paper of functionalities, use cases, requirements and a solution. The group made good progress in understanding the scope of management of communication services. |  | 
Outstanding issues | None. |  | 
Documents | pCRs. |  | 

## Slide 28
OAM&P SIs (7/10)
Study Item | Study on Self-Organizing Networks (SON) for 5G |  |  | FS_SON_5G
 |  |  |  | 810030
Rapporteur | Intel | Percentage of completion |  | 30% -> 40%
Target | SA#86 – Dec. 2019 (Previously SA#84 – June 2019) | Main TR |  | TR 28.861
Summary of progress | The group discussed contributions related to the following topics: |  |  | 
 | add requirements for NSI resource allocation optimization UC; add use cases for Mobility Robustness Optimisation, automatic NSI creation, and self-monitoring of network performance; Add concept, use case and requirements for Self-healing; |  | Update the concept, usecase of Self-establishment of eNodeB; Add NSI PM input to support CCO; Management Data Analytics Service and SON functions; | 
Outstanding issues | None. |  |  | 
Documents | pCRs. |  |  | 

## Slide 29
OAM&P SIs (8/10)
Study Item | Study on non-file-based trace reporting |  | FS_OAM_RTT
 |  |  | 820037
Rapporteur | Nokia | Percentage of completion | 0% -> 0%
Target | SA#84 – June 2019 | Main TR | TR 28.806
Summary of progress | No session at this meeting. |  | 
Outstanding issues | None. |  | 
Documents | None. |  | 

## Slide 30
OAM&P SIs (9/10)
Study Item | Study on non-public networks management (Preliminary work before SA approval) |  | FS_OAM_NPN
 |  |  | ??????
Rapporteur | Huawei | Percentage of completion | 0% -> 0%
Target | SA#86 – Dec. 2019 | Main TR | 
Summary of progress | No session at this meeting. |  | 
Outstanding issues | None. |  | 
Documents | None. |  | 

## Slide 31
OAM&P SIs (10/10)
Study Item | Study on management and orchestration aspects with integrated satellite components in a 5G network (Preliminary work before SA approval) |  | FS_5GSAT_MO
 |  |  | ??????
Rapporteur | Thales | Percentage of completion | 0% -> 0%
Target | SA#86 – Dec. 2019 | Main TR | 
Summary of progress | No session at this meeting. |  | 
Outstanding issues | None. |  | 
Documents | None. |  | 

## Slide 32: TRs / TSs to be sent to SA#83
Tdoc | Title | Source | Sent for
S5-192270 | TR 28.890: Management and orchestration; Study on integration of Open Network Automation Platform (ONAP) and 3GPP management for 5G networks | Orange | Approval

## Slide 33: TRs / TSs to be sent to Edithelp
Title | Source

## Slide 34: Thank you!