## Slide 1
3GPP TSG SA WG5 Ad-Hoc
June 25th - 28th 2019, Sapporo, Japan
Source: | Samsung
Title: | Synergizing Edge Computing SA5 SA6
Document for: | Discussion
Agenda Item: | 4.4.1 - Study on management aspects of edge computing
Abstract of the contribution: This document discusses various Edge Computing related activities ongoing in 3GPP and tries to attain synergy between them.
S5-194065

## Slide 2: SA6 – FS_EDGEAPP (Study on Application Architecture for enabling Edge Applications)
Application architecture for enabling edge applications over 3GPP networks
Supported functionalities
  UE provisioning to connect to edge network
  Edge network discovery, registration and selection
  Edge apps enablement (registration, discovery) in edge network
  Network capability exposure (SCEF, NEF) to Edge apps.
  Service continuity at UF handoff to new location.
Out-of-scope
  Edge App Orchestration
  Configuring Edge Data Network Configuration Server with required Configurations for Edge Data Network.
Orchestration of Edge Application can be enabled by 3GPP management system.
3GPP management system can configure EDNCS with required information utilizing NF Provisioning MnS.

## Slide 3: SA5 – FS_MAN_EC (Study on management aspects of edge computing)
Enabling (Requirements & Solutions) the management of edge computing functionality in 3GPP systems.
Management of Edge application requires coordination between 3GPP management and non-3GPP management systems.
The requirements on 3GPP management system is:
  To enable LCM of UPF (edge App).
  To provide information about UPF to be used by Edge Apps.
  To configure other NF in terms of UPF being used.
Target to finish by Sep 2019

## Slide 4: Needed Clarifications
What is edge computing management system? Does it always have to be a non-3gpp management system?
  We have a 3gpp edge computing system being worked on in SA6. The management provisions of the same need to be provided by SA5 i.e 3GPP edge computing management system.
  Edge computing management system should not be restricted to non-3GPP system (e.g ETSI MEC).
AF and Local data network is marked as “Non-3GPP access network”
  As per the work being done in SA6, they both can possibly form part of 3gpp system too. The figure needs an update.
  23.501 also describe AF in section 6 where it defines NFs in 5GC.
3GPP TS 23.501

## Slide 5: FS_MAN_EC (SA5) Missing Pieces with respect to FS_EDGEAPP (SA6)
Edge Application (Virtualized Infrastructure) Orchestration.
  The Orchestration of Edge Applications are considered out-of-scope of SA6 and falls under jurisdictions of SA5.
Edge Data Network UE’s configurations
  Edge Data Network Configuration Server (EDNCS) configure UE with info to connect to edge data network including Edge Enabler Server's FQDN, service areas etc. From where the EDNCS get this info is considered out-of-scope of SA6. SA5 Provisioning MnS can be used for the same.

## Slide 6: Way Forward for FS_MAN_EC
Enhancing the document to include a management system, called 3gpp edge computing management system, managing the 3GPP edge computing system (Slide 4).
Enhancing the document with respect to AF/LDN (Slide 4)
Addressing the Gaps identified (Slide 5) with the relevant section/text in the study document.

## Slide 7: Conclusions
Depending on the group decision. CRs can be produced on the following
  Updating the figures of section 4 with relevant text (Slide 4).
  Bringing new use cases and solutions for (Slide 5):
    Orchestration of Edge Applications
    Configuration of Edge Data Network Configuration Server.

## Slide 8
Back up

## Slide 9
Local data network
3GPP edge computing management system
Operations Support Systems
3GPP management system
Operations
Support Systems
ETSI NFV management and Orchestration
Edge computing management system
UE
SMF
AF
Application
RAN
UPF
UPF
(PDU session anchor)
N3
N9
N6
N4
N4
PCF
N7
N5