## Slide 1: 3GPP Edge Enablement (SA5 Perspective)
Deepanshu Gautam, Samsung

## Slide 2: SA6 Initiative
Defined an Application Architecture for Edge in the study.
  Key Issue 12: Lifecycle Management of EAS, EES and EDNCS.
Working on the normative provisions (TS 23.558) based on the study.
LS-out to SA5 S6-200306 (yet to be handled in SA5) asking specific question on if, what and how SA5 plan to address Lifecycle of EAS.
Edge Enabler Server: A functional entity resident in the Edge Hosting Environment providing services for the Edge Applications and Edge Enabler Clients
Edge Enabler Server provides supporting functions needed for Edge Applications to run in an Edge Data Network e.g configuration, Edge application server availability etc.
Edge Data Network Configuration Server provides supporting functions needed for the UE to connect the Edge Enabler Server in the Edge Data Network e.g EES URI.
Key Take Away: SA6 have defined a 3GPP specific edge computing architecture introducing new entities to be managed by OAM/SA5.

## Slide 3: SA2 Initiative
On-Going Rel-17 Study
  Discovery of Edge Application Server
  Edge relocation (change of PSA), EAS relocation
  Network Information Provisioning to Local Edge Application Server with low latency
  Activating the traffic routing towards Local Data Network per Edge Application Server request
The definition of Edge Application Server in SA2 is being referred to 23.758.
SA WG1 defined the term Service Hosting Environment that has been translated and broadened in SA WG2 work in the present TR to Edge Hosting Environment as the environment providing support required for Edge Application Server's execution.
Three hosting models
  The MNO is in control of the edge and provides the edge computing infrastructure, the connectivity and the application platform, and manages the Edge Application Servers.
  The MNO hosts its own or a 3rd party application platform on its edge computing infrastructure. MNO provides the routing and IP network stitching between the connectivity and the platform which exposes APIs for application management.
  The MNO provides distributed connectivity to a DN, and cloud providers host the application servers on their application platform on the edge.
Service Hosting Environment (defined in 22.261)
  The environment, located inside of 5G network and fully controlled by the operator, where Hosted Services are offered from.
Key Take Away: SA2 have adopted Edge Application Server as the AF/AS which will be deployed at the edge of the network and may or may not be in control of Operator.

## Slide 4: SA5 Initiative
Completed study on management aspect of edge computing.
  Edge Deployment
  UPF management at edge
  Access to 5GC via NEF
  …
LS reply (S5-197752) to SA6 indicating relevance of Key Issue 12 with SA5.
Key Take Away: The objectives of the study conducted did not include the architecture defined in SA6.

## Slide 5: Consideration for SA5
What is EAS?
  An AF/AS hosted in an environment (Edge Hosting Environment) controlled/managed by the operator.
EAS will be a black box for SA5, SA5 will provide mechanism to manage (LCM, PM, FS) this box without getting into its internal logic and functionality.
  This is following the same logic with AF IOC in NRM. AF IOC (with no attributes) is defined for only purpose to describe the IOCs representing its interaction interface with 5GC i.e. EP_Rx and EP_N5
What are EES and ECS (EDNCS)?
  New Edge specific 3GPP NFs deployed at Edge Hosting Environment.
SA5 may receive additional requirements, from the SA2 study and SA6 WID, which we have to entertain in future.
Edge Application Server: An Application Server resident in the Edge Hosting Environment.
Edge Hosting Environment: An environment providing support required for Edge Application Server's execution.
Edge Enabler Server: A functional entity resident in the Edge Hosting Environment providing services for the Edge Application Servers and Edge Enabler Clients
Source: TR 23.758
SA WG1 defined the term Service Hosting Environment that has been translated and broadened in SA WG2 work in the present TR to Edge Hosting Environment as the environment providing support required for Edge Application Server's execution.
Source: SA2 Enh_EC
Service Hosting Environment: The environment, located inside of 5G network and fully controlled by the operator, where Hosted Services are offered from
Source: TS 22.261
Key Take Away: SA5 shall define management provision for EAS, EES and ECS.

## Slide 6: SA5 Implications
SA5 need to deliver on the following
  LCM of Edge Application Server (EAS) located at the edge of 5G network fully controlled by the operator.
  LCM of Edge Enabler Server (EES) and Edge Data Network Configuration Server (EDNCS).
  Performance Assurance of EAS, EES and EDNCS.
  Fault Supervision on EAS, EES and EDNCS.
  Network Slice management consisting EAS(s).
  Communication service deployment utilizing EAS(s).
Key Take Away: SA5 need to study how the architectural entities defined in SA6 will be managed (Lifecycle, Provisioning, Performance, Fault, etc.)

## Slide 7: LS Reply to SA6
SA5 thanks SA6 for their update.
SA5 would like to inform SA6 that LCM of EAS (Edge Application Server) in very well in-scope of SA5.
SA5 will study the concept and then decide on the probable solution.
SA5 plan to start related work on edge computing in Rel-17.
Further, SA5 would also like to inform SA6 that in addition to EAS, 23.758 has also define EES (Edge Enabler Server) and EDNCS (Edge Data Network Configuration Server). The management of both these entities are well in-scope of SA5.
S6-200306
SA6 thanks SA5 for the reply LS in S5-197752 which asked us to keep SA5 informed of issues resulting from this work that may need OAM involvement.
At SA6#35 we have approved the attached pCR to TS23.558. During discussions on that pCR the Lifecycle Management operations below were mentioned. We therefore ask SA5 the following;
Does SA5 consider that any of the following application layer LCM operations are covered by their terms of reference and are therefore within SA5’s current scope?
  On-boarding an Edge Application Server;
  Offboarding an Edge Application Server;
  Instantiating an Edge Application Server which has already been onboarded;
  Terminating an Edge Application Server;
  Subscription to receive notifications about status changes of Edge Application Servers.
Does SA5 consider that some LCM operations for Edge Application Servers could follow similar procedures already specified for LCM of mobile networks that include virtualized network functions (with necessary modifications if needed) as per the TS28.52x series of specifications?
Does SA5 plan any work on LCM for edge applications in Release 17?
In addition, SA6 informs SA5 that the target for completion of our specification for this (TS23.558) is September 2020.
S6-200305 (attached pCR)
Lifecycle management
[A.5.3.x-a] The application layer architecture shall support interactions with a lifecycle management system

## Slide 8: For Endorsement
It is proposed to endorse the “SA5 Implications” presented in Slide 6.
  Related WID has been submitted already.
It is proposed to endorse the text for LS reply to SA6 on Slide 7

## Slide 9: Thank you!