## Slide 1: 3GPP SA5 inputs to progressing the Multi SDO Autonomous Network coordination
Zou Lan, SA5 Vice Chair (Huawei)

## Slide 2: Contents
Background
3GPP SA5 opinion on progressing the Multi-SDO Autonomous Network coordination
Overview of 3GPP SA5 Rel-17 WIs/Sis
3GPP SA5 Concepts and Definitions
  Autonomous Network
  Autonomous Network Level
  Intent driven management
  Control loops
Summary

## Slide 3: Background
  1. 20200928 Multi-SDO Autonomous Network Coordination Workshop: SA5 has shared SA5 introduction as captured in “S5-204551 3GPP SA5 introduction on Autonomous Networks”
  3GPP is an industry driven standardization activity with truly global reach.
  Standardization of interfaces enables an interoperable, multi-vendor approach to deployment and generates mass market economies of scale.
  3GPP SA5 has built up experience related to autonomous networks since 2008.
  3GPP SA5 has already made some progress on autonomous networks and continues to deliver more features to support autonomous networks.
  3GPP SA5 is actively involved and developing specifications with full support of automation.
  3GPP SA5 is happy to cooperate with other SDOs on autonomous networks.
  2. Incoming TMF Liaison Progressing the Multi SDO Autonomous Network coordination on Feb.18th ,2021: First meeting 22nd Feb 2021 11:00-12:30 GMT/UTC with subsequent meetings occurring monthly.
  For a 2-hour timeslot, we suggest that each meeting considers a single topic:
  Concepts and model alignment
  Intent driven interactions / APIs
  definitions of:
    o Autonomous Networks,
    o Control loops,
    o Autonomous Networks Levels,
    o Autonomous Domain
  3. 2021-02-22 AN Multi SDO Coordination( TM Forum Host) #2
  Draft introduction slides at 2021-02-22 Multi-SDO Autonomous Networks Workshop #2 Meeting Notes - AN-SDO Collaboration - TM Forum Confluence

## Slide 4: SA5 opinion on progressing the Multi-SDO Autonomous Network coordination
The Multi-SDO coordination should take into account of existing available deliverables and align the standardization work across different groups as much as possible.
The coordination work should consider the following technical aspects:
  Alignment of Autonomous networks related concepts and definitions, e.g.
    Autonomous Networks
    Intent driven interactions
    Control loops
    Autonomous Networks Levels
    Autonomous Domain
    More to be added if needed
  Coordination on the architectural framework
  Coordination on the key features and related multi-players interoperable management services to be supported towards autonomous networks
  Proof of Concept to show the Multi-SDO coordination achievement
Note: The following slides address the topic “Alignment of Autonomous networks related concepts and definitions”.

## Slide 5: Overview of 3GPP SA5 Rel-17 WIs/SIs
The Multi-SDO coordination related activities will be discussed under the related 3GPP SA5 Rel-17 Workitems/Study Items.

## Slide 6: SA5 concepts and definitions-Autonomous Network (TS 28.100)
Definition:
Autonomous Network: telecommunication system (including management system and network) with autonomy capabilities which is able to be governed by itself with minimal to no human intervention.
Concept:
4.1 Autonomous network concept
The network become complex due to large number of devices and diversity of services. Different autonomy mechanisms are introduced in the industry to reduce the complexity of mobile network management and control. The ultimate goal for autonomous network is to enable telecommunication system (including management system and network) within the autonomy mechanisms (e.g. AI/ML) to be governed by itself with minimal to no human intervention. Autonomous network can reduce the operating expenditure (OPEX) associated with the autonomous management and control of the complexity network and improve the service experience to enable various vertical industries (e.g. autonomous vehicle, smart city). Following are concepts related to autonomous network.
- Autonomous network level is used to describe the level of autonomy capabilities in the autonomous network.
- Self-Organization Network, Management data analytics, Intent driven management, closed loop SLS assurance are examples of enablers for autonomous network.

## Slide 7: SA5 concept and definitions- Autonomous Network Level (TS 28.100)
Definition:
Autonomous Network Level: describes the level of autonomy capabilities in the autonomous network.
Concept:
4.2 Autonomous network level concept
Different autonomy mechanisms in the telecommunication system may lead to different capabilities of autonomy and different operation efficiency on network management and control workflow, and indicates the level of autonomy of the network. The term Autonomous network level is used to describe the levels of autonomy capabilities in the autonomous network to improve the efficiency for network management and control. Participation of the human and telecommunication system in the network management and control workflow are different for each level and are important factors to evaluate the autonomous network levels. For each autonomous network level, some tasks can be performed by telecommunication system, some performed by human, and some performed by cooperation of human and telecommunication system. For example, in the highest autonomous network level, all tasks are performed by telecommunication system.
Editor's Note: the concept of autonomous network and autonomous network level need to be revised and coordinated with other SDOs.

## Slide 8: SA5 concept and definitions- Intent driven management (TS 28.312) - 1
Definition:
Intent: the expectations including requirements, goals and constraints given to a 3GPP system, without specifying how to achieve them.
Concept:
4.1 Intent concept
4.1.1 Introduction
An intent specifies the expectations including requirements, goals and constraints for a specific service or network management workflow. The intent expression information may include particular objective and possibly some related details. Following are some general concepts for intent:
Intent is understandable by humans, and also needs to be interpreted by the machine without any ambiguity.
Intent is declarative, which focus more on describing the “What” but less on “How”, which not only relieves the burden of the consumer knowing implementation details but also leaves room to allow the producer to explore alternative options and find optimal solution. Intent describes the properties that allows a satisfactory outcome.
The expectations expressed by an intent is agnostic to the underlying system implementation, technology and infrastructure. Area can be used as managed object in the expectations expressed by an intent to achieve system implementation, technology and infrastructure agnostic.
Intent needs to be quantifiable from network data so that the fulfilment result can be measured and evaluated.
Intent can be categorized based on different user types or different management scenario types.

## Slide 9: SA5 concepts and definitions- Intent driven management (TS 28.312) - 2
4.1.2 Intent categorizes based on user types
Intent from Communication Service Customer (Intent-CSC): Intent from Communication Service Customer enables Communication Service Customer (CSC) to provide what CSC would like to do for the communication service without knowing how to do the detailed management for communication service. For example, Intent-CSC can be 'Enable a V2X communication service for a group of vehicles in certain time'.
Intent from Communication Service Provider (Intent-CSP): Intent from Communication Service Provider enables Communication Service Provider (CSP) to express an intent about what CSP would like to do for network without knowing how to do the detailed management for network. For example, Intent-CSP can be 'Provide a network service supporting V2X communications for highway-417 to support 500 vehicles simultaneously'.
Intent from Network Operator(Intent-NOP): Intent from Network Operator enables Network Operator (NOP) to provide what NOP would like to do for group of network elements (i.e. subnetwork) management and control without knowing how to do the detailed management for the network elements. For example, Intent-NOP can be 'Provide a radio network service to satisfy the specified coverage requirements and UE throughput requirement in certain area'.
4.1.3 Intent categorizes based on management scenario types
Intent for network and service design/planning: Editor’s Note: The Intent for network and service design/planning is FFS.
Intent for network and service deployment: enables a consumer to express the network or service instance to be deployed. Examples of intent for network and service deployment are “Provisioning radio network in the specified area with specified frequency information, transport information, and radio information (e.g. range of PCI, Cell Id), network capacity and performance information” or “provisioning radio service in the specified area with certain service characteristics (e.g. SLS)”.
Intent for network and service assurance: enables a consumer to express intents for network and service assurance, and the following two sub-groups:
  Intent for network and service maintenance: enables a consumer to express the network and service status (e.g. performance, alarm, issue) to be monitored or the network and service issues to be addressed. Examples of intent for network and service maintenance are “Monitoring coverage performance in the specified area by geographic grid granularity” or “Addressing the certain weak coverage issues in specified area”.
  Intent for network and service optimization/assurance: enables a consumer to express the performance objectives of network and service to be improved. Examples of intent for network and service optimization are “Optimize radio network in the specified area with certain RAN UE throughput objectives (e.g. target average RAN UE DL throughput, target percentage of UE with the RAN UE DL throughout less than 5Mbps)” or “Optimize radio network in the specified area with certain coverage objectives (e.g. target coverage ratio, target average RSRP)”.

## Slide 10: SA5 concept and definitions- Control loops (TS 28.535) - 1
Concept:
4.2.2 Control loops
A control loop is a building block for management of networks and services. The basic principle of any control loop is to adjust the value of a measured or observed variable (expressed as for example an attribute) to equal the value of a desired goal (expressed as for example an attribute). The producer of the measurements or observations, the control service, and the controlled entity are all required to create a control loop.
For the control loop to act on input in the context of the set goal, the control loop provided through following four steps that continuously consume and produce information from each other in a loop in the following sequence monitor, analyse, decide and execute.
A control loop can be an open control loop in which case a human operator or other management entity intervenes inside the loop A control loop can be closed and operates without human operator or other management entity involvement inside the loop other than possibly the initial configuration of the measurement producer and configuration of control loop.
4.2.3 Open control loops
In an open control loop, the human operator intervenes in one or more of the process steps inside the loop, see Figure 4.2.3.1. The human operator is in control of the steps in the control loop, including decisions taken in the loop. The management system collects, analyses and presents the data to the operator, but the operator decides which action to take. In this case, the completion time for control loop is dependent on availability and reaction time of a human operator or other management entity.
4.2.4 Closed control loops
In a closed control loop, there is no direct involvement of a human operator or other management entity in the control loop, the control loop is fully automated. As shown in Figure 4.2.4.1 the human operator or management entity is not directly controlling the details inside the process steps but provides control outside the loop. For example, configuring goals for the control loop to make autonomous decisions within the boundaries of the set goal. Once the control loop is configured with the goal, the controlled entity is adjusted according to the set goals.
In a closed control loop the input to the control loop provided by human operator or other management entity may include the goal or policies. The output of the closed control loop may include closed control loop status to a human operator or other management entity.
Typically, the goal is set within certain parameter boundaries, the closed control loop can automatically adjust the output based on the input within the parameter boundaries. Once a control loop cannot automatically adjust, the human operator or other management entity needs to be informed. The human operator or other management entity may decide to change the management of closed control loop so that it becomes an open control loop, where decisions are made by the human operator or other management entity and not by the closed control loop.
Figure 4.2.3.1: Open control loop entities
Figure 4.2.4.1: Closed control loop entities

## Slide 11: SA5 concept and definitions- Control loops (TS 28.535) - 2
4.2 Management control loops
4.2.1 Overview
For communication service assurance one can identify two interactions of management control loops:
1)Between the CSC and the CSP: In this case, the CSC provides the requirements for an assured communication service to the CSP, the CSP provides the corresponding communication service, the CSP also provides feedback to the CSC. The CSP adjusts the resources used by a communication service or the CSC adjusts the SLS continuously to achieve the assured requirements.
2)Between the CSP and the NSP: the communication service provided by CSP requires the network capabilities. For example, the CSP requires a certain network latency. The NSP management system adjusts the network or CSP adjusts the latency requirement continuously to satisfy the latency requirement.
Figure 4.2.1.1 gives a high level description of interaction process involved in the management closed control loop.
Figure 4.2.1.1: Communication service closed control loop assurance
Generally, the management control loop for CSA consists of the steps Monitoring, Analysis, Decision and Execution. The adjustment of the resources used for the communication service is completed by the continuous iteration of the steps in a management control loop. As described in clause 4.1, the management closed control loop for the resources used for the communication service is deployed in the preparation phase and takes effect during the preparation phase and operation phase.
Figure 4.2.1.2 shows the overall process of communication service assurance using a management control loop.
Figure 4.2.1.2:Management Control Loop

## Slide 12: SA5 concept and definitions- Autonomous Domain (TS 28.533)
SA5 has developed the MnS and MnF concepts which may be related to Autonomous Domain.
4.1 Management Services (MnS)
The fundamental building block of the Service Based Management Architecture (SBMA) is the Management Service (MnS). A MnS is a set of offered capabilities for management and orchestration of network and services. The entity producing an MnS is called MnS producer. The entity consuming an MnS is called MnS consumer. An MnS provided by an MnS producer can be consumed by any entity with appropriate authorisation and authentication.
An MnS producer offers its services via a standardized service interface composed of individually specified MnS components.
Figure 4.1.1: MnS producer and MnS consumer
4.5 Management Function (MnF) concept
A Management Function (MnF) is a logical entity playing the roles of MnS consumer and/or MnS producer.
A Management Service produced by MnF may have multiple consumers. The MnF may consume multiple Management Services from one or multiple Management Service producers. An example of a MnF playing both roles (Management Service producer and consumer) illustrated in the figure 4.5.1 below.
Management Function can be deployed as a separate entity or embedded in Network Function to provide MnS(s). Following figure 4.5.2 shows an example (on the left) which MnF deployed as a separate entity to provide MnS(s) and another example (on the right) which MnF is embedded in Network Function to provide MnS(s):
Figure 4.5.2 Examples of MnS deployment scenario

## Slide 13
Summary
  SA5 is happy to cooperate with other SDOs on autonomous networks topic, we suggest to start from definition and concept alignment first.
    3GPP SA5 has specified the following concepts and definitions which are related to Autonomous Networks :
      Autonomous Network
      Autonomous Network level
      Intent driven management
      Control loops
    3GPP SA5 is happy to clarify the meaning of “autonomous domain” with other SDOs and decide whether related concept and definition are needed to be specified.
  Next SA5 meeting：
Meeting | Start date | End date
SA5#137-e | 10 May 2021 | 19 May 2021

## Slide 14
www.3gpp.org
For more Information:
info@3gpp.org
thomas.tovinger@ericsson.com
zoulan@huawei.com
portal.3gpp.org
Thank you!