## Slide 1: 5G Charging in 3GPP
2.11.2021
Chen Shan SA5 Charging Vice Chair (Huawei)
3GPP SA5 Webinar – Part 2: Charging
Gerald Görmer SA5 Charging Chair SA5 Vice Chair (MATRIXX Software)

## Slide 2: Agenda
3GPP & SA5 introduction (recap. from Webinar Part 1)
Charging high level principles
Principles of Charging in 5G Core network
Charging : 3GPP SBI adoption
Charging : Network Slice performance and management services

## Slide 3: 3GPP standards eco-system
5G Projects
Official Liaisons on specification work:
Certification Bodies
3GPP Organizational Partners (OPs)
The 3GPP Organizational Partners (OP) - 7 Standards Organizations - from China, Europe, India, Japan, Korea and the United States.
Participation in 3GPP by companies and organizations becoming Members of one of these 7 OPs.
Inputs on market requirements may come in to the Project via 3GPP Market Representation Partners (MRP).
There is a lot of additional external liaison activity…SDOs, Industry bodies, projects…
450 MHz Alliance, AISG, Bluetooth, Broadband Forum (BBF), CableLabs, International Special Committee on Radio Interference (CISPR), CTIA, Digital Video Broadcasting (DVB) Project, Ecma, International, Expert Group for Emergency Access (EGEA), Eurescom, COST 273, European Radiocommunications Committee (ERC), Fixed Mobile Convergence Alliance (FMCA), GCF, Global TD-LTE Initiative (GTD), GPS Industry Council, GSM Association, HomeRF Forum, IDB Forum, IEEE, Internet Engineering Task Force (IETF), IrDA, International Multimedia Telecomunications Consortium (IMTC), Internet Streaming Media Alliance, ISO-ITU expert group, ISO MPEG / JPEG, ITU-T SG2, JAIN tm (Javatm APIs for Integrated Networks), The Java Community Process (JCP), Liberty Alliance Project, Metro Ethernet Forum (MEF), NENA, NGMN (Next Generation Mobile Networks), oneM2M, OMA (Open Mobile Alliance ), Open Networking Foundation (ONF), Open IPTV Forum, Object Management Group (OMG), PCS Type Certification Review Board (PTCRB), Portable Computer and Communications Association (PCCA), Presence and Availability Management (PAM) Forum, RSA Laboratories, SDR Forum, Sun Micro Systems Inc., Steerco, SyncML Initiative, Trusted Computing Group (TCG), TeleManagement Forum (TMF), TCCA, TIA /TR45, TIA/TR47, ITU, TV-anytime Forum, Voice eXtensible Mark-up Language (VXML) Forum, Wi-Fi Alliance, Wireless Broadband Alliance (WBA), WLAN Smart Card Consortium, Wireless World Research Forum (WWRF), World Wide Web Consortium (W3C)
(Source: extract from https://www.3gpp.org/about-3gpp/15-bodies-with-which-3gpp-has)
~700 companies
3GPP Market Representation Partners (MRPs)

## Slide 4: Specification Groups
The TSGs prepare, approve and maintain the 3GPP Technical Specifications and Technical Reports.
They are responsible for the detailed time frame and management of the work’s progress;
  Management of work items;
  Technical Co-ordination;
  Proposal and approval of work items within the agreed scope and terms of reference of the TSG
The TSG Chairman is responsible for the overall management of the technical work within the TSG and its Working Groups.
The WG Chairman is responsible for the overall management of the technical work within the WG and its sub-groups.

## Slide 5: Charging High Level Principles

## Slide 6: Setting the Scene for Accounting and Charging in 3GPP
  Charging Levels
    Bearer, Subsystem and Service charging
  Charging Methods
    Offline charging versus Online charging and Converged charging
  Charging Data
    Single, group and mass data
  Charging Trigger
    How, when and what

## Slide 7: Charging Levels
‘Bearer’ Charging, comprising domains:
    Circuit Switched (CS), Packet Switched (GPRS/PS), (WLAN discontinued)
    CP Data Transfer (small data transfer: NIDD), Exposure function for north bound API, 5G Data connectivity, 5G Connection and mobility, Edge Computing (EC)
Subsystem Charging, i.e. IP Multimedia Subsystem (IMS)
Service Charging, comprising Application Services:
    MMS, LCS, PoC, MBMS, SMS, MMTel, VCS, ProSe, Monitoring
    Network Slice management and performance/analytics
Specific Charging services:
    Advice of Charge (AoC), Announcement, Proxy Function

## Slide 8: Charging Methods
Offline Charging Charging mechanism where charging information does not affect, in real-time, the service rendered. The final result of this charging mechanism is the forwarding of CDR files to the Billing Domain.
Online Charging Charging mechanism where charging information can affect, in real-time, the service rendered and therefore a direct interaction of the charging mechanism with bearer/session/service control is required. The mechanism comprises the execution of credit control and subscriber account balance management on the Online Charging System.
Converged Charging A process where online and offline charging are combined. The charging information is utilized by Converged Charging System in one converged charging service which offers charging with and without quota management, as well as charging information record generation.

## Slide 9: Charging Data Information collection and Transfer
Single Count – Charging Event
Collected counts – Charging Data
Grouped counts – Charging Record
Collected Records – Charging Files
CTF -> CDF : Rf / Ro / Gy
  Interface: IETF Diameter Applications
  Data: Attribute Value Pair (AVP)
CDF -> CGF: Ga / Gz
  Interface: 3GPP GTP‘ based on GTP
  Data: unstructured record/container or ASN.1
CGF -> BD : Bx
  Interface: FTP / FT IRP / IPDR
  Data: file format and ASN.1 records
Single Count – Charging Event
Collected counts – Charging Data
CTF -> CHF : Nchf
  Interface: service-based HTTP/2
  Data: HTTP attributes

## Slide 10: Business Paradigma
Charging Model / Charging Method | Offline Charging | Online Charging | Converged Charging
Post-Paid | Collection and transfer in CDR files to the Billing Domain | Real-time collection and transfer in CDRs to the Billing Domain | Real-time/Deferred collection (i.e. without Quota management) and transfer in CDR files to the Billing Domain
Pre-Paid / Real-time | Hot Billing Via single CDR generation and fast transfer to a mediation | Real-time collection and balance control | Real-time collection and account balance control (i.e. Quota management)

## Slide 11: 3GPP Specification Hierarchy

## Slide 12: Structure of TS Series
Architecture and Principles
    Common online and offline charging architecture
    General principles of Charging for all levels
One “Middle Tier” TS per domain / subsystem / service /
Mapping of common architecture onto specific domain
    Domain / subsystem / service specific charging functionality, especially type and content of CDRs and CMDs
Common interfaces and applications between the entities of the common architecture
    Diameter application (TS 32.299)
    Services, op & proc. charging using SBI (TS 32.290)
    5G system; Charging service (TS 32.291)
    FTP to Billing Domain (TS 32.297)
    GTP’ between CDF and CGF (TS 32.295)
    ASN.1 Syntax Description for CDR parameters (TS 32.298)
Special cases:
    Online Charging System (TS 32.296), Advice of Charge (TS 32.280), Announcement Service (TS 32.281), Proxy Function (TS 32.293
32.25x
32.260
28.20x
32.29x
32.240

## Slide 13: Charging Architecture Reference Points (RP) Architecture for Non-5G Systems
Source: TS 32.240
CAP = Mobile SSF
Rf: Diameter AA
Ro: Diameter CC
Gy: Diameter CC
Gz: GTP
Ga: GTP
Bx: FTP
ISC: SIP
----- Not specified in Charging

## Slide 14: Offline and Online Charging Logical Reference Point (RP) Architecture
Charging Trigger Function (CTF)
Collects „Metrics“ from the core system, based on system specific triggers (e.g. signalling events)
Formats these metrics into charging events
Forwards charging events to the CDF via Rf RP / OCF via Ro RP
Charging Data Function (CDF)
Collects charging events and formats them into CDRs according to system specific rules
Forwards CDRs to CGF via Ga reference point
Charging Gateway Function (CGF)
Provides non-volatile CDR file store
Uses Bx reference point for CDR file transfer to Billing Domain
Billing Domain
Receives CDR files from CGF with further standardisation in GSMA
Charging Online Function (OCF)
Receive acknowledgements of the charging events and grants or rejects the network resource usage requested in real-time before service execution
Account Balance Management Function (ABMF)
Access the account of the service request subscription (user/provider)
Rating Function (RF)
Determines the value of chargeable events in terms of monetary or non-monetary units (i.e. quota)
Source: TS 32.240

## Slide 15: Principles of Charging in 5G Core Network

## Slide 16: Overall Charging Architecture
Reference Point (RP) view
Service Based Interface (SBI)
Source: TS 32.240
ONE Charging System architecture will be covered under two variants
When the target charging system (i.e. 5G CCS or EPC OCS/OFCS) needs to support termination of a reference point or interface from the opposite type of core network (i.e. Ro/Rf or Nchf) implementations will need to include interworking between the HTTP used by SBI and the Diameter protocol.

## Slide 17: Converged Charging Logical Service Based Interface (SBI)
Converged Charging System (CCS) consists of four distinct modules
Charging Function (CHF)
Account Balance Management Function (ABMF)
Charging Gateway Function (CGF)
Rating Function (RF)
Nchf Interface: Service-based interface exposed by CHF
Source: TS 32.240

## Slide 18: Mapping of Charging Functions
CHF and CGF integrated in the CCS
CGF in a separate element
CGF integrated in the BD

## Slide 19: Charging Scenarios
Charging Method | Charging Scenarios | 
Online Charging | Immediate Event Charging (IEC) | One-time request
 | Event Charging with Unit Reservation (ECUR) | “Reserve”+”Debit”
 | Session Charging with Unit Reservation (SCUR) | Group of multiple “Reserve+Debit”s
Offline Charging | Event based charging | One-time report
 | Session based charging | Group of multiple reports for one CDR
Converged Charging | Event based charging | One-time request Note: IEC and offline event based charging
 | Session based charging | Group of One or multiple “Reserve+Debit”s, and/or multiple requests

## Slide 20: Session Handling and Triggers for 5G Data Connectivity
Converged charging "PDU session" (from SMF)
  Flow Based Charging (based on PCC Rules)
  Roaming QoS flow Based Charging (QBC)
Trigger mechanism: CHF capability to enable/disable triggers in SMF, and set associated category (i.e. immediate/deferred report to CHF)
Default Triggers list in SMF, e.g. for Flow Based Charging:

## Slide 21: Converged Charging Message Flows
Flows for generic converged charging:
  Event-based (IEC)
  Session-based (SCUR, ECUR)
  Notification
Simplified SCUR Message Flow
Note: although service-based Nchf from CHF is used, the exchanges are reflected as Charging Data Request/Response
Source: TS 32.240

## Slide 22: Charging : 3GPP SBI Adoption

## Slide 23: Charging Specification Overview 5G Data connectivity as the First Domain Applicable for SBI
TS 32.290
Services, operations and procedures of charging using Service Based Interface (SBI)
Generic description of Nchf
TS 32.291
5G system; Charging Services,
stage 3
Nchf (API specification).
TS 32.240
TS 32.255
5G data Connectivity Charging
  PDU session charging from SMF:
    Principles, triggers
    Message flows
    PDU session information specific structure across Nchf
    PDU session charging CHF CDR specific data

## Slide 24: Charging Architecture Service Based Interface (SBI) Architecture for 5G Core Network
Nchf
BILLING DOMAIN
Bx
CCS
CHF
Access and Mobility Management Function (AMF)
Network Exposure Function (NEF)
Short Message Service Function (SMSF)
Session Management Function (SMF)
Policy Control Function (PCF)
SMF
PCF
SMSF
AMF
NEF
N40
N42 (VPLMN)
N41 (HPLMN)
N44
N46
N28
IMS Node
N45

## Slide 25: SBI Functions
Generic functionalities: Re-authorization, Termination action…
Possible use of Network Resource Function (NRF)
CHF discovery by SMF (CHF Service consumer = SMF)
CHF can use the NRF framework to register/deregister/update to NRF Nchf_ConvergedCharging service, based on e.g. Range(s) of SUPIs, Range(s) of GPSIs
Range(s) of PLMNs

## Slide 26: Convergent Charging Using SBI
Nchf_ConvergedCharging service definition and its operations
Common data structure over Nchf
    Charging Data Request (NF consumer => CHF) and Charging Data Response (NF consumer <= CHF)
      Include common information such as NF consumer Identification, Subscriber identifier, Multiple Unit Usage (rating group, requested unit, used unit container with "Quota management indicator" to differentiate the reported usage…).
      Concatened with NF specific information specified for SMF
NF services provided by the CHF
Service Name
Service Operations
Operation
Semantics
Example
Consumer(s)
Nchf_ConvergedCharging
Create
Request/Response
SMF
Update
Request/Response
SMF
Release
Request/Response
SMF
Notify
Notify
SMF
Source: TS 32.255

## Slide 27: Nchf Interface Definition (Stage 3) Service Operation
Nchf-ConvergedCharging service operations (Create, Update, Release and Notify) are described with the associated procedure e.g.:
Source: TS 32.291
  Standard POST method supported for "chargingdata" resource for Create Operation
  Custom operations (mapped to POST) supported by the individual "chargingdataRef" resource for Update/Release Operations
  Standard POST method supported by "notifyUri" resource for Notify Operation

## Slide 28: Nchf Interface Definition (Stage 3) Resource URI Structure
Charging Service API specification is based on OpenAPI specification
  "OpenAPI 3.0.0 Specification"
  https://github.com/OAI/OpenAPI-Specification/blob/master/versions/3.0.0.md.
Nchf_ ConvergedCharging Service API
Resource URI structure :
Source: TS 32.291

## Slide 29: Charging : Network Slice Performance & Management Services

## Slide 30: Overview of 5G Network Slice Charging
  Objective: To support the 5G Network slice charging using Nchf
  Release 16 study: Concept, scenarios and potential charging requirements and solutions– Completed
      3GPP Technical Report (TR) 32.845: “Charging management; Study on charging aspects of network slicing”
  Release 16 normative work item – Completed
      3GPP draft Technical Specification (TS) 28.201 (16.1.0): ”Charging management; Network slice performance and analytics charging in the 5G System (5GS); Stage 2”
      3GPP draft Technical Specification (TS) 28.202 (16.1.0): ”Charging management; Network slice management charging in the 5G System (5GS); Stage 2”
      3GPP draft Technical Specification (TS) 32.291 (17.0.0): ”Telecommunication management; Charging management; 5G system, charging service; Stage 3”
      3GPP draft Technical Specification (TS) 32.298 (17.0.0): ”Telecommunication management; Charging management; Charging Data Record (CDR) parameter description”
  Release 17 study– In Progress
      3GPP Technical Report (TR) 32.847 (0.5.0): ”Study on Charging Aspects for Network Slicing Phase 2”

## Slide 31: Study on charging aspects of Network Slice (TR 32.845)
  Objective：Study the charging scenarios and requirements for different business model (e.g. B2B Services, NSaaS) using network slice and the possible charging aspect for network slice management.
      Topic 1: Network Slice usage
        Usage Based charging: NSI (Network Slice Instance) related usage type may include the volume and duration (per PDU session).
        Event Based Charging: NSI related usage type as chargeable information (e.g. the number of IoT connections) only includes the number of PDU session.
        Performance based charging: the performance data for 5G Network slice may be used to enable network slice instance charging for example:
            Latency.
            Upstream /Downstream Throughput for Single Network Slice Instance.
            Mean number of PDU sessions of network Slice Instance.
        Analytics based charging: Load level related to 5G Network slice may be used to enable NSI charging.
        Template based charging: NSI templates are a possible mechanism to assist in creating network slice instances by the 5G Management system.
      Topic 2: Network Slice management
        NOP and NSaaS: NSI provision charging based on the Management of Network slices in the lifecycle of a NSI.
            Commissioning phase: NSI creation.
            Operation phase: NSI modification, NSI Activation, De-Activation.
            Decommissioning phase: NSI termination.

## Slide 32: NS Performance and Analytics Charging (TS 28.201)
Figure 1: Network slice performance and analytics converged charging architecture
  The Addition of New NF for Network Slice charging : CEF(Charging Enablement Function)
      Subscribes/Unsubscribes to notifications by consuming management services or services exposed by other functions;
      Receiving required charging information from the services/Cancelling the subscription to PA information;
      Determines the occurrence of chargeable events. When it determines that a chargeable event has occurred it then triggers charging by consuming the Nchf services.
      CEF is the consumer of:
        either one or both Performance Management Service (MnS) / Network Data Analytics service (Nnwdaf)
        Charging (Nchf) Service
  NSPA Converged Charging Architecture

## Slide 33: NS Performance and Analytics Charging (TS 28.201)
  The Triggers and NSPA Charging information Reporting:
      Triggers for CEF to invoke a Charging Data Request [Event] towards the CHF based on the trigger conditions.
      When a charging event is issued, it includes details such as Single Network Slice Selection Assistance Information (S-NSSAI) and the NSPA Container information, etc.
      The Stage 3 for details of the NSPA Charging information are specified in the TS 32.291 (Open API) and TS 32.298 (CDR).
Trigger Conditions | Trigger level | Default category | CHF allowed to change category | CHF allowed to enable and disable | Message when "immediate reporting" category
Notify event for a subscription | - | Deferred | Not Applicable | Not Applicable | Charging Data Request [Event]
Expiry of time limit per S-NSSAI | - | Immediate | Not Applicable | Not Applicable | Charging Data Request [Event]
Threshold reached for a performance indicator (e.g. load level per S-NSSAI) | - | Immediate | Not Applicable | Not Applicable | Charging Data Request [Event]
Limit reached for number of notify events per subscription made by CEF | - | Immediate | Not Applicable | Not Applicable | Charging Data Request [Event]
Limit reached for number of notify events per S-NSSAI | - | Immediate | Not Applicable | Not Applicable | Charging Data Request [Event]
NOTE 1:In addition, there may be operator specific triggers. NOTE 2:The threshold and limit is default configured and updated based on the configuration. |  |  |  |  | 
Information Element | Category | Description
Latency | OC | This field holds latency as described in 28.554 [271].
Throughput | OC | This field holds throughput as described in TS 28.554 [271]
Maximum packet loss rate | OC | This field holds maximum packet loss rate as described in TS GSMA NG.116 [500]
Service Experience statistics data | OC | This field holds service experience statistics data as described in TS 23.288 [150]
Number of PDU sessions | OC | This field holds the number of PDU sessions as described in TS 28.554 [271].
Number of registered Subscribers | OC | This field holds the number of registered subscribers as described in TS 28.554 [271].
Load level | OC | This field holds the load level as described in TS 23.288 [150].
Table 1: Default Trigger conditions in CEF
Table 2: Structure of NSPA Container Information

## Slide 34: NS Management Charging (TS 28.202)
Figure1: NSM converged charging architecture (CTF)
Figure 2: NSM converged charging architecture (CEF)
  The following provisioning of network slice procedures are considered for Network Slice Management charging:
      Network Slice Instance (NSI) Creation.
      Network Slice Instance (NSI) Modification.
      Network Slice Instance (NSI) Termination.
  NSM Converged Charging Architecture
  The CEF/CTF for NS Management charging:
      CEF is the consumer of:
        Provisioning service (MnS) for network slice exposed by the MnS Producer
        Charging (Nchf) service.
      Charging Trigger Function (CTF) embedded into the MnS Producer and generates charging events based on the observation of NSM triggers.

## Slide 35: NS Management Charging (TS 28.202)
Table 1: Default Trigger conditions in CEF or Service Producer (CTF)
Table 2: Structure of NSM Charging Information
Trigger Conditions | Trigger level | Default category | CHF allowed to change category | CHF allowed to enable and disable | Message when "immediate reporting" category
Creation Response sent | - | Immediate | Not Applicable | Not Applicable | Charging Data Request [Event]
NSI Modification Response sent | - | Immediate | Not Applicable | Not Applicable | Charging Data Request [Event]
NSI Termination Response sent | - | Immediate | Not Applicable | Not Applicable | Charging Data Request [Event]
Information Element | Category | Description
Management operation | M | This field holds the management operation associated to with the provisioning.
Identifier of NetworkSlice Instance | OM | This field holds the identifier of the Network Slice Instance as defined in TS 28.531 [252] clause 4.6.
List of Service profile charging information | OM | This field holds the list of service profile charging information supported by the Network Slice instance and is defined in clause 6.2.1.3.
Management operation status | OC | This field holds the status of the management operation (Succeeded or Failed), as defined in TS 28.532 [253] clause 11.1.1.1.3.
Operational state | OC | This field indicates the operational state of the network slice instance (enabled or disabled), as defined in TS 28.541 [254] clause 6.4.1.
Administrative state | OC | This indicates the administrative state of the network slice instance (locked, unlocked or shuttingdown), as defined in TS 28.541 [254] clause 6.4.1.
  The Triggers and NSM Charging information Reporting:
      A set of trigger conditions are defined for the CEF or Service Producer (CTF) to invoke a Charging Data Request [Event] towards the CHF, including the NSM Charging information.
      The CDR generation mechanism processed by the CHF upon receiving Charging Data Request [Event] issued by the CEF or Service Producer (CTF) for these chargeable events.
      The Stage 3 for details of the NSM Charging information are specified in the TS 32.291 (Open API) and TS 32.298 (CDR).

## Slide 36: Charging Aspects for Network Slicing Phase 2 (TR 32.847)
  Key Issues:
      Key Issue #1: Converged Charging for simultaneous number of UEs/max. number of UEs per network slice
      Key Issue #2: Converged Charging for concurrent number of PDU sessions/max. number of PDU sessions per network slice
      Key Issue #3: Volume based Converged Charging per network slice
      Key Issue #4: Converged Charging for max duration per network slice
      Key Issue #5: Converged Charging for number of unique UEs per network slice
      Key Issue #6: UE Converged Charging based on network slice charging
      Key Issue #7: Converged Charging for actual duration per network slice
      Key Issue #8: Converged Charging for NSSAA
  Network Slice Phase 2
      Objective: In continuation of the converged charging limited to data collection functionalities, investigate in terms of:
          Network slice converged charging for Network Slices enabled over 3GPP 5GS;
          Correlation aspects between Network Slice charging and the end user charging accessing the Network Slice;
          Inter-Provider (B2B) charging aspects by considering the different Organizations (e.g. MNO, Verticals).
        Conducted by considering TS 23.501 and TS 23.502.
        consider service-based management framework for Network Slicing management specified under TSs series (TS 28.533, TS 28.532 and TS 28.541).

## Slide 37
www.3gpp.org
For more information:
info@3gpp.org
gerald.goermer@matrixx.com
Chenshan@Huawei.com
portal.3gpp.org
Thank you!