## Slide 1: Discussion on QoS enhancement in NRM (SA5 #146)
Nokia, Nokia Shanghai Bell

## Slide 2: Background/Problem
In 145e meeting the following solution proposed:
  S5-225120 Rel-18 CR 28.541 Add Enhanced QoS support in NRM (stage 2).doc
  S5-225121 Rel-18 CR 28.541 Add Enhanced QoS support in NRM (stage 3, YANG).doc
A few aspects are open for discussion
  Observed design related open points
  Why GNBDUFunction needs the QoS information
  This DP is to discuss the above open points

## Slide 3
Observed open points with the proposed solution on QoS Enhancement
Observed Open points:
1> Semantic issue with name containment syntax (in Figure 2)
 TS 32.156 specified that, name contained shall be used when there is no navigability between two IOC. But for e.g., here GNBCUUPFunction has a pointer (Navigable) to Configurable5QISet. Same issues observed to the Dynamic5QISet changes.
2> Multiple copies of Configurable5QISet MOI, instead of one set under one ManagedElement (or a SubNetwork) and referenced by the GNBCUCPFunction / GNBCUUPFunction MOI.  For e.g., in the model in Figure 1, from instance association view, if one gNB(i.e., one ManagedElement) contains 100 MOIs of Configurable5QISet, then all the 100 MOIs can be navigated/referenced by GNBCUCPFunction and GNBCUUPFunction instances inside the gNB. With proposed change (Figure 2), it could be a cases, with 100 MOIs of Configurable5QISet, 30 of them are contained by GNBCUCPFunction, another 30 MOIs contained by GNBCUUPFunction, rest 40 MOIs contained by GNBDUFunction instances. (Note: the 30 MOIs of Configurable5QISet contained by GNBCUCPFunction instance can only be contained by GNBCUCPFunction, i.e, these instances cannot be contained by the other two function or gNB as a ManagedElement)
In modeling of Figure 2 with the depicted association diagram, is the design intended such that one instance of GNBCUCPFunction may access/navigate to all the 100 MOI of Configurable5QISet (just like that in Figure 1)? The following points are open:
1) How to separate which Function shall contain which Configurable5QISet instance(s)?
2) One Fucntion accessing the the Configurable5QISet instance contained by other Function: what’s the use cases?
3> Currently the Configurable5QISet and Dynamic5QISet are associated to PCFFunction and/or SMFFunction, but the proposed change has impact to this association, while this is not clearly specified.
Figure 1: Original NRM association relationship in TS 28.541
Figure 2: Proposed change (part 1) from S5-225120 for Enhance QoS Support

## Slide 4
Observed open points with the proposed solution on QoS Enhancement
Figure 3/4: Original NRM association relationship in TS 28.541
Observation:
What’s the impact of proposed change to SMFunction / PCFFunction?

## Slide 5
Why DU need the QoS information
F1AP (TS 38.473) message flow from CU to DU
This message is sent by the gNB-CU to request the setup of a UE context.
Direction: gNB-CU  gNB-DU.
Observations:
TS 38.473 (F1AP) uses names:
“Non Dynamic 5QI Descriptor” for Standardized 5QI and
“Dynamic 5QI Descriptor” for Configurable 5QI.
Because one of the above is sent in F1AP “UE Context Setup Request” msg in “DRB to be Setup List” IE, then questions are:
Why configurable 5QI would be needed in gNB-DU NRM? or
Is there any configuration/information currently missing in F1AP for Dynamic 5QI from CU to DU?

## Slide 7
Summary
  GNBDUFunction does not need the QoS information or further technical clarification is needed.
  Design related open points shall be clarified or resolved.

## Slide 8: Thanks

## Slide 9
Backup

## Slide 10
Standardized 5QI to QoS characteristics mapping (23.501 5.7.4 table 5.7.4-1)
5QI Value | Resource Type | Default Priority Level | Packet Delay Budget (NOTE 3) | Packet Error Rate | Default Maximum Data Burst Volume (NOTE 2) | Default Averaging Window | Example Services
1 | GBR | 20 | 100 ms (NOTE 11,NOTE 13) | 10-2 | N/A | 2000 ms | Conversational Voice
2 | (NOTE 1) | 40 | 150 ms (NOTE 11,NOTE 13) | 10-3 | N/A | 2000 ms | Conversational Video (Live Streaming)
3 |  | 30 | 50 ms (NOTE 11,NOTE 13) | 10-3 | N/A | 2000 ms | Real Time Gaming, V2X messages (see TS 23.287 [121]). Electricity distribution – medium voltage, Process automation monitoring
4 |  | 50 | 300 ms (NOTE 11,NOTE 13) | 10-6 | N/A | 2000 ms | Non-Conversational Video (Buffered Streaming)
76 |  | 56 | 500 ms (NOTE 11, NOTE 13, NOTE 15) | 10-4 | N/A | 2000 ms | "Live" Uplink Streaming (e.g. TS 26.238 [76])
5 | Non-GBR | 10 | 100 ms NOTE 10,NOTE 13) | 10-6 | N/A | N/A | IMS Signalling
6 | (NOTE 1) | 60 | 300 ms (NOTE 10,NOTE 13) | 10-6 | N/A | N/A | Video (Buffered Streaming) TCP-based (e.g. www, e-mail, chat, ftp, p2p file sharing, progressive video, etc.)
7 |  | 70 | 100 ms (NOTE 10,NOTE 13) | 10-3 | N/A | N/A | Voice, Video (Live Streaming) Interactive Gaming
8 |  | 80 | 300 ms (NOTE 13) | 10-6 | N/A | N/A | Video (Buffered Streaming) TCP-based (e.g. www, e-mail, chat, ftp, p2p file sharing, progressive
10 |  | 90 | 1100ms (NOTE 13) (NOTE 17) | 10-6 | N/A | N/A | Video (Buffered Streaming) TCP-based (e.g. www, e-mail, chat, ftp, p2p file sharing, progressive video, etc.) and any service that can be used over satellite access type with these characteristics
Standardized 5QI values are specified for services that are assumed to be frequently used and thus benefit from optimized signalling by using standardized QoS characteristics. Dynamically assigned 5QI values (which require a signalling of QoS characteristics as part of the QoS profile) can be used for services for which standardized 5QI values are not defined. The one-to-one mapping of standardized 5QI values to 5G QoS characteristics is specified in table

## Slide 11
TS28.541: IOC Configurable5QISet / FiveQICharacteristics
5.3.76 FiveQICharacteristics
This specifies the 5QI value and the corresponding QoS characteristics for a 5QI.
Attribute name | S | isWritable
fiveQIValue | M | T/F (NOTE)
resourceType | M | T/F (NOTE)
priorityLevel | O | T/F (NOTE)
packetDelayBudget | O | T/F (NOTE)
packetErrorRate | O | T/F (NOTE)
averagingWindow | O | T/F (NOTE)
maximumDataBurstVolume | O | T/F (NOTE)
NOTE: The isWritable qualifier is "T" if the attribute 1) describes a 5QI in Configurable5QISet MOI, or 2) describes a 5QI in Dynamic5QISet MOI which is associated to PCFFunction MOI or SMFFunction MOI when the PCF is not deployed; The isWritable qualifier is "F" otherwise. |  | 
5.3.78 FiveQiDscpMappingSet
This IOC specifies the set of mapping between 5QIs and DSCP.
5.3.78.2 Attributes includes attributes inherited from Top IOC and the following attributes:
fiveQiDscpMappingList | M
5.3.79 FiveQiDscpMapping <<dataType>> This data type specifies the mapping between 5QIs to DSCP.
fiveQIValues (Integer: 0-255) | M
dscp (Integer: 0-255) | M
23.5011:
5G QoS Flow or QoS Flow: The finest granularity for QoS forwarding treatment in the 5G System. All traffic mapped to the same 5G QoS Flow receive the same forwarding treatment (e.g. scheduling policy, queue management policy, rate shaping policy, RLC configuration, etc.). Providing different QoS forwarding treatment requires separate 5G QoS Flow.
5G QoS Identifier: A scalar that is used as a reference to a specific QoS forwarding behaviour (e.g. packet loss rate, packet delay budget) to be provided to a 5G QoS Flow. This may be implemented in the access network by the 5QI referencing node specific parameters that control the QoS forwarding treatment (e.g. scheduling weights, admission thresholds, queue management thresholds, link layer protocol configuration, etc.).
Pre-configured 5QI: Pre-defined QoS characteristics configured in the AN and 5GC and referenced via a non-standardized 5QI value.
No child attributes other than inheritance
No child attributes other than inheritance

## Slide 12
FiveQICharacteristics attributes
fiveQIValue | It identifies the 5QI value. allowedValues: 0 – 255 | type: Integer multiplicity: 1
resourceType | It indicates the Resource Type of a 5QI, as specified in TS 23.501 [2]. allowedValues: "GBR", Non-GBR" | type: ENUM multiplicity: 1
priorityLevel | It indicates the Priority Level of a 5QI, as specified in TS 23.501 [2]. allowedValues: 0 - 127 | type: Integer multiplicity: 1
packetDelayBudget | It indicates the Packet Delay Budget (in unit of 0.5ms) of a 5QI, as specified in TS 23.501 [2]. allowedValues: 0 - 1023 | type: Integer multiplicity: 1
packetErrorRate | It indicates the Packet Error Rate of a 5QI, as specified in TS 23.501 [2]. allowedValues: N/A | type: PacketErrorRate multiplicity: 1
averagingWindow | It indicates the Averaging Window (in unit of ms) of a 5QI, as specified in TS 23.501 [2]. allowedValues: 0 - 4095 | type: Integer multiplicity: 1
maximumDataBurstVolume | It indicates the Maximum Data Burst Volume (in unit of Byte) of a 5QI, as specified in TS 23.501 [2]. allowedValues: 0 - 4095 | type: Integer multiplicity: 1
Attribute name | S
fiveQIValue | M
resourceType | M
priorityLevel | O
packetDelayBudget | O
packetErrorRate | O
averagingWindow | O
maximumDataBurstVolume | O
TS 28.541:
5.3.76 FiveQICharacteristics
This specifies the 5QI value and the corresponding QoS characteristics for a 5QI.
5QI Value | Resource Type | Default Priority Level | Packet Delay Budget (NOTE 3) | Packet Error Rate | Default Maximum Data Burst Volume (NOTE 2) | Default Averaging Window | Example Services
1 | GBR | 20 | 100 ms (NOTE 11,NOTE 13) | 10-2 | N/A | 2000 ms | Conversational Voice
2 | (NOTE 1) | 40 | 150 ms (NOTE 11,NOTE 13) | 10-3 | N/A | 2000 ms | Conversational Video (Live Streaming)
Attribute name | S
Scalar (integer 0:9) | M
Exponent (integer 0:9) | M
PacketErrorRate (S 10-2 here S=1 E=2)
Standardized 5QI to QoS characteristics mapping (TS 23.501 5.7.4 table 5.7.4-1)
IOC attributes in TS 28.541 5.4.1