## Slide 1: Clarification on the Session Identifier in the Nchf (SA5 #155)
Chen Shan
Huawei

## Slide 2: Session Identifier in Charging Data Message
  The Session Identifier in the stage 2
The Session Identifier specified in service special charging specifications based on the SCUR, ECUR, IEC and PEC charging scenarios.
The Session Identifier specified in the TS 32.290 clause 7 about the common message contents used for Converged charging or offline only charging which is performed by NF (CTF) consuming service operations exposed by CHF, achieved using Charging Data Request and Charging Data Response.
Take the SMF SCUR Charging as the example:
Take the NEF ECUR/IEC/PEC Charging as the example:
Problem 1 : The Session Identifier can only be present in the Charging Data Request [Termination].
Problem 2 : The Session Identifier can be present in the Charging Data Response [Initial and Event]

## Slide 3: Session Identifier in Open API and CHF CDR
  The Session Identifier in the stage 3
The Session Identifier specified in the TS 32.291 clause 7 and Aabout the Bindings common CDR field, IE and Resource attributes used for Converged charging or offline only charging which is out of Charging Data Request and Charging Data Response.
The Session Identifier specified in the TS 32.298 clause 5.1.5 about the CHF CDR used for Converged charging or offline only charging .
Problem 3 : Mapping relationship of Session Identifier should be aligned in the TSs of Stage 2 and Stage 3.
Stage 2: TS 32.290 and TS 32.2XX/28/2XX
  Session Identifier in the Charging Data Request/Response
Stage 3: TS 32.298
  Session Identifier in CHF CDR (No problem on Mapping )
Stage 3: 32.291 (Problem on Mapping)
  In the Charging Data Request: The session id (ChargingDataRef) is present in the “URI” of the HTPP headers
  In the Charging Data Response: The session id (ChargingDataRef) is present in the “Location” of the HTPP headers.

## Slide 4: Correction Proposal on Session Identifier
Suggested Solution for Problem 1 & Problem 2:
Correction on the Session Identifier in the Stage 2 Charging (TS 32.2xx/28.2xx Charging Specifications 6.x.2 Detailed message format for converged charging).
For SCUR Charging:
  The Session Identifier shall be present in the Charging Data Response [Initial]
  The Session Identifier shall be present in the Charging Data Request [Update/Termination]
For ECUR Charging
  The Session Identifier shall be present in the Charging Data Response [Initial]
  The Session Identifier shall be present in the Charging Data Request [Termination]
For IEC/PEC Charging
  The Session Identifier shall be present in the Charging Data Response [Event]
Suggested Solution for Problem 3:
Clarification on the Session Identifier in the Stage 3 Charging (TS 32.291 Clause 6.1.3)
Clarify the source of session identifier is the ChargingDataRef in the HTTP header specified in the TS 32.291.

## Slide 5: Thank you!