## Slide 1: Brief presentation of SA1 work on RAN Sharing Enhancements (RSE)
Joerg Swetina
NEC Laboratories Europe
S1-135120

## Slide 2: Overview of SA1 activities on RSE
A study (Study on Radio Access Network (RAN) sharing enhancements, TR 22.852) has been conducted in Rel-12
  Contains 13 use cases and a section on potential requirements
  The scenarios illustrate:
    sharing common E-UTRAN resources according to identified RAN sharing scenarios (e.g. pooling of unallocated radio resources).
    verify that the shared network elements provide allocated E-UTRAN resources according to sharing agreements/policies.
    Indication of and potential actions upon overload situation in consideration of sharing agreements/policies.
A first set of requirements has been agreed
  S1-134180 CR to 22.101
Remaining requirements discussed at this meeting
S1-135120

## Slide 3: Main contents
Roles:
  In TS 22.101 the following definitions were introduced
    Hosting E-UTRAN: E-UTRAN that is shared among a number of operators
    Hosting E-UTRAN Operator: The Operator that has operational control of a Hosting E-UTRAN. Note: This operator does not necessarily own a core network. Core NW sharing is out of scope of of RSE.
    Participating Operator: Authorized operator that is sharing E-UTRAN resources provided by a Hosting E-UTRAN Operator
Main difference to previous releases:
  Finer granularity of allocating and controlling shared E-UTRAN resources (Bandwidth, differentiated traffic, cells/sectors)
  Participating Operator has limited OAM Access to the Hosting E-UTRAN (backhaul link test in the base station, obtain fault reports, retrieve RAN resource usage information [non realtime])
S1-135120

## Slide 4: Main contents (II)
Main difference to previous releases (continued):
  Generation and retrieval of usage and accounting information
    Collected events may be delivered to the Participating Operator, including start / end of service for a UE of the Participating Operator in the Hosting E-UTRAN
  Support of PWS in the Hosting E-UTRAN
    Note: Rel-11 design requires a shared PWS core. However, some regulatory obligations require a solution in which no common PWS core network entity is involved
Not yet agreed requirements (discussed at this meeting)
  On-demand capacity negotiation
  Support for load balancing (respecting agreed shares of resources)
  Handover functionality due to E-UTRAN Sharing Agreements
    direct connected and idle UEs towards /away from the Hosting E-UTRAN
    (Home) PLMN selection of a UE if HPLMN is Participating Operator
S1-135120

## Slide 5: Topics to be discussed in joint SA5/SA1 session
Hosting E-UTRAN Operator = Master Operator (MO) without Core Network? Restriction to E-UTRA?
OAM access by Participating Operators?
  SA5: The Master Operator is the only one to have a direct OA&M connection from his DM to the shared network elements
Administration of fine-grained E-UTRAN Sharing
  Static allocation, i.e. guaranteeing a minimum allocation and limiting to a maximum allocation.
  Static allocation for a specified period of time and/or specific cells/sectors
  First UE come first UE served allocation.
  On-demand capacity negotiation
Event collection:
  start / end of service for a UE in the Hosting E-UTRAN
S1-135120

## Slide 6
S1-135120