## Slide 1: Offline Charging Architecture
Discussion for Scenarios and Problem statement on Determination of Completeness of Charging Information (Att of. S5-151177)

## Slide 2: Offline Charging for Multiple Application Servers
IMS enables deployment of new services that can be concatenated. Thus with one call more than one AS can process a call from User A to User B.
An aggregation/correlation of charging data from several IMS elements is required to correctly charge the subscriber. The IMS Charging ID (ICID) is used for this correlation.
Each service used influences the Offline Charging result.

## Slide 3: Examples

## Slide 4: Problem Description
Information collected in a CDR from S-CSCF indicates which Application Servers are involved in an IMS session. Each AS provides charging data required for correct charging of the session in a separate CDR delivered to the BD.
When multiple services are invoked on a single AS, it is common practice for each service generates its own charging data resulting in individual CDR per service in the BD.
When the BD is processing records from multiple IMS nodes, how can it be efficiently guaranteed that it has received all the records necessary to charge the user for the IMS session?

## Slide 5: Scenario 1: MMTel
Vast majority of users Abasic are only subscribed to Multimedia Telephony Service (TS 22.173)
‚Calling Party Pays‘ charging model is applicable (TS 22.115)
MMTel AS CDR provides sufficient accounting information to charge the call
For this scenario, the Application Servers information stored in the S-CSCF CDR is sufficient for the BD to know that there is a CDR required from the MMTel server and that BD could be aware that the MMTel server only hosts one service that can be executed to ensure that it has all the necessary CDRs.

## Slide 6: Scenario 2: TelCo Enterprise Service
Minor group of users Aebs are subscribed to Multimedia Telephony Service (TS 22.173) and additionally to Enterprise Billing Service (EBS).
EBS Service enables:
  Charging of session and service to 3rd party (TS 22.115)
Both MMTel AS and EBS AS provide accounting-relevant information.
For this scenario, the Application Servers information stored in the S-CSCF CDR is sufficient for the BD to know that there is a CDR required from the MMTel server and EBS Server and that BD could be aware that both the MMTel server and EBS server only host one service that can be executed to ensure that it has all the necessary CDRs.

## Slide 7: Scenario 3: Enhanced Multimedia Telephony (EMT)
User Aemt is subscribed to Multimedia Telephony Service (TS 22.173)
Additionally User Aemt is subscribed to EMT Service, which invokes App1.
Two applications resides on same generic service platform SIP-AS
  App1: Filtering/manipulation of customer-specific headers. No CDR is written
  App2: Tailored implementation of call leg manipulation Would write CDRs in case of invocation. But is not invoked in this example.
In case of involvement of App1, MMTel AS provide sufficient accounting information
In case of involvement of App2, accounting information of both services must be correlated
For this scenario, since CDRs may be generated by the SIP AS, the Application Server information stored in the S-CSCF CDR is not sufficient for the BD to know that CDRs may be required from the SIP AS server.

## Slide 8: Scenario 4: Small Business Telephony (SBT)
User Asbt is subscribed to Multimedia Telephony Service (TS 22.173)
Additionally User Asbt is subscribed to SBT Service which invokes App2
At end of call App2 terminates leg towards A-party including MMTel session and connects B-party with an IVR e.g. collecting costumer feedback
In case of involvement of App2, accounting information of both services must be correlated as MMTel CDR provides wrong service delivery end timestamp.
For this scenario, since CDRs may be generated by the SIP AS, the Application Server information stored in the S-CSCF CDR is not sufficient for the BD to know that CDRs are required from the SIP AS server.
For this scenario a correlation of MMTel-AS CDR and App2/SIP-AS CDR is mandatory for a correct service charging.

## Slide 9: Thank You