## Slide 1: Status for solutions in TR 23.779
LG Electronics
Yannick Lair
22 June 2015

## Slide 2: Off-network operations (1/2)
Five solutions in TR 23.779:
  Solution 1-1: Distributed mesh support for MCPTT off-network MCPTT group calls (SA2#104)
    Superseded by solution 1-5.
  Solution 1-2: Off-network MCPTT service using ProSe UE-to-UE relay (SA2#106)
    Should not be pursued further for Rel-13 since SA2 has decided not to specify solution for UE-to-UE relay in Rel-13 and RAN did not consider UE-to-UE relay in the scope of their work in Rel-13.
  Solution 1-3: Application level device to device relay operation for off-network MCPTT (SA6#1)
    Telefonica will not be in a position to pursue this solution further in Rel-13.
  Solution 1-4: Group priority solution for off-network communication when UE in coverage of PLMN network (SA6#3)
    Related to priorities handling, so should better appear in clause 5.7. No group priority handling in SA2.
  Solution 1-5: MCPTT off-network (SA6#4)
    This solution is compromise proposal between solutions 1-1, 4-1-1, 6-1-1 and 6-1-2. Understanding is that this is the agreed solution for Rel-13.

## Slide 3: Off-network operations (2/2)
Remaining work for TR 23.779:
  For solutions 1-2 : capture conclusion that this solution is not pursued further in Rel-13.
  For solutions 1-1, 4-1-1, 6-1-1 and 6-1-2: capture conclusion that these solutions are superseded by agreed solution 1-5.
  For solution 1-5: this solution refers to solutions 1, 2, 3 and 4. It would be better to explicitly refer to solutions 1-1, 4-1-1, 6-1-1 and 6-1-2.
  Evaluation of other solutions and conclusion.

## Slide 4: Group Management – off-network
One solution in TR 23.779:
  Solution 4-1-1: Group Call Participants Discovery by off-network and off-network with ProSe UE-to-UE relay group call setup (SA6#1)
    Included in solution 1-5. UE-to-UE relay parts are not relevant since ProSe UE-to-UE relay is not part of Rel-13 in RAN and SA2.
Remaining work for TR 23.779:
  As per off-network operations : capture conclusion that this solution is included in agreed solution 1-5, except for the UE-to-UE relay part since ProSe UE-to-UE relays will not be provided by RAN and SA2 in Rel-13.

## Slide 5: Call control/signalling - Off-Network
No solution provided, but partly described in solution 1-5.
Also partly described in the following flows:
  7.7.5 (10.7.5 in the TS) ”Private call set up in off-network mode with solicited discovery”
  7.7.6 (10.7.6 in TS) “Private call set up in off-network mode with unsolicited discovery”
Remaining work for TR 23.779:
  No more work needed, subclause 5.5.1 to be kept empty.

## Slide 6: Floor control – off-network
Three solutions in TR 23.779:
  6-1-1: Limited Precedence Based; Off-network Floor Control (SA6#1)
    Included in compromise solution 1-5.
  6-1-2: Options for off-network floor control (SA6#1)
    Included in compromise solution 1-5.
  6-1-3: Floor control off-network and off-network with ProSe UE-to-UE relay (SA6#1)
    The UE-to-UE relay part cannot be pursued further considering that ProSe UE-to-UE relays are not provided in Rel-13. Are the remaining aspects of this solution still needed considering compromise solution 1-5?
Remaining work for TR 23.779:
  As per off-network operations : capture conclusion that solutions 6-1-1 and 6-1-2 are included in agreed solution 1-5.
  Capture conclusions for solution 6-1-3.

## Slide 7: Private calls – off-network
One solution in TR 23.779:
  Solution 9-1-1: Support for MCPTT off-network private calls (SA2#106)
Based on solution 1-1, but no real procedures are described.
Some private call setup sequences are provided in flows in 7.7.5 (10.7.5 in TS) “Private call set up in off-network mode with solicited discovery” and 7.7.6 (10.7.6 in TS) “Private call set up in off-network mode with unsolicited discovery”.
Remaining work for TR 23.779:
  None.

## Slide 8: On-network operations
Four solutions in TR 23.779:
  Solution 2-1: IMS based architecture for MCPTT applications (SA2#105)
  Solution 2-2: NGCN-based architecture (SA2#106)
    Solution 2-2 is not considered further for normative work after introduction of solution 2-4.
  Solution 2-3: Generic high level architecture for MCPTT within a public safety ecosystem with user-based services application sublayer (SA2#106)
  Solution 2-4: Application domain routing over non-trusted SIP core (SA6#4)
Remaining work for TR 23.779:
  Capture conclusion for solution 2-2.
  Evaluation of other solutions and conclusion.

## Slide 9: UE-to-network relay
Two solutions in TR 23.779:
  Solution 3-1: ALG relay for MCPTT UE-to-network relay (SA2#105)
    Solution 3-1 has impact at application layer and would add the ALG relay functionality if:
    From requirements point of view the relay needs to be aware of the type of communication requested by the remote UE,
    For optimizations there would be a need to decide between unicast or multicast delivery on PC5.
  Solution 3-2: Relay for UE-to-network relay MCPTT (SA6#1)
    Solution 3-2 is a pure L3 relay. It is assumed to be already available as per ProSe / eProSe_Ext specifications, no impact at application layer.
Remaining work for TR 23.779:
  Evaluation of solutions and conclusion: decision needed as to whether such ALG relay is needed or if pure L3 relay functionality is enough for UE-to-network relay.

## Slide 10: Group Management – on-network
Three solutions in TR 23.779:
  Solution 4-2-1: Group management – search (SA6#3)
  Solution 4-2-2-1: Group regroup for groups within the same MCPTT system (SA6#3)
  Solution 4-2-2-2: Group regroup for groups from the different MCPTT systems (SA6#3)
    Was accepted for normative phase with approval of information flow 7.4.1 (10.4.1 in TS) “Temporary group formation – group regrouping involving multiple MCPTT systems”
SA6 also agreed on information flow for:
  7-4-2 (10.4.2 in TS) “Temporary group – broadcast group call”
Remaining work for TR 23.779:
  Capture decision for solution 4-2-2-2.
  Evaluation of other solutions and conclusion.

## Slide 11: Call control/signalling - On-network (1/2)
Nine solutions in TR 23.779:
  Solution 5-2-1: MCPTT Group Call resources allocation (alternative #1) (SA6#3)
  Solution 5-2-2: MCPTT Group Call resources allocation (alternative #2) (SA6#3)
  Solution 5-2-3: Solution for On Network Pre-arranged Group Call Set up (SA6#3)
    Solution 5-2-3 was accepted for normative phase with approval of information flows in 7.5.1 (10.5.1 in TS) “Pre-arranged group call”
  Solution 5-2-4: Solution for On Network Late Call Entry (SA6#3)
  Solution 5-2-5: Chat group call with implicit affiliation (SA6#4)
  Solution 5-2-6: MCPTT group call MBMS resources allocation (SA6#4)
  Solution 5-2-7: Associating an MCPTT group call with a multicast bearer (SA6#4)
  Solution 5-2-8: group call procedures based on solution 2-4 (SA6#4)
  Solution 5-2-9: pre-established session (SA6#4)
    Competing with solution 7-2
SA6 also agreed on information flow for:
  7-5-2 (10.5.2 in TS) “Group call involving groups from multiple MCPTT systems”

## Slide 12: Call control/signalling - On-network (2/2)
Remaining work for TR 23.779:
  Capture conclusion for solution 5-2-3 in subclause 5.5.2.3.4.
  Some solutions are for allocation of resources (e.g. 5-2-1, 5-2-2, 5-2-3) and other solutions are to address TS 22.179 requirements (e.g. 5-2-4, 5-2-5) so these solutions are complementary.
  A decision is needed as to which solutions or parts of solutions to pursue for Rel-13.
  Evaluation of other solutions and conclusion.

## Slide 13: Floor control – on-network
Two solutions in TR 23.779:
  Solution 6-2-1: Solution for on-network Floor Control (alternative #1)(SA6#1)
  Solution 6-2-2: Solution for on-network Floor Control (alternative #2) (SA6#3)
    Solution 6-2-2 was accepted for normative phase with approval of several information flows in 7.6 (10.6 in TS) Floor control for on-network MCPTT service:
      Floor request, floor grant and floor taken during an MCPTT session
      Floor revoke, floor rejected during an MCPTT session
      Queue position during an MCPTT session
Remaining work for TR 23.779:
  Capture conclusions in subclause 5.6.2.2.4 for the agreement of solution 6-2-2.
  Capture conclusion in 5.6.2.1.4 that solution 6-2-1 is not pursued further.

## Slide 14: Priority/Pre-emption
Two solutions in TR 23.779:
  Solution 7-1: Messages to be broadcast (SA6#1)
  Solution 7-2: Preliminary setup of unicast media IP connectivity (SA6#1)
    Competing solution in 5-2-9.
Remaining work for TR 23.779:
  Evaluation of solutions and conclusion.

## Slide 15: Service continuity
Two solutions in TR 23.779:
  Solution 8-1: SIP-based service continuity between on-network and UE-to-network relay (SA6#1)
  Solution 8-2: SIP-based service continuity between EPC path and ProSe communication path (SA6#1)
SA2 will not specify solution for service continuity mechanisms at ProSe level in Rel-13. Way forward needs to be defined in SA6.
Solutions 8-1 and 8-2 address a different scenario of service continuity. Solution 8-1 uses well-known SIP-based service continuity mechanisms. Solution 8-2 needs modifications to IMS service continuity.
Remaining work for TR 23.779:
  Evaluation of solutions and conclusion.
  Need to liaise with SA2 in case solution 8-2 is adopted for new requirements on IMS service continuity.

## Slide 16: Private calls – on-network
Two solutions in TR 23.779:
  Solution 9-2-1: Support for MCPTT on-network Private Calls (with Floor Control) (SA6#3)
  Solution 9-2-2: Support for Private Calls without floor control (SA6#3)
These were both accepted for normative phase with approval of information flows
  7.7.1 (10.7.1 in TS) “Call setup – automatic commencement mode”
  7.7.2 (10.7.2 in TS) “Private call using manual commencement mode”
  7.7.3 (10.7.3 in TS) “End private call”
  7.7.4 (10.7.4 in TS) “Call Setup – automatic commencement mode – users in multiple MCPTT system”
Remaining work for TR 23.779:
  Capture the agreement of these two solutions in subclauses 5.9.2.1.4 and 5.9.2.2.4.

## Slide 17: Log on/Authentication
One solution in TR 23.779:
  Solution 10-1: MCPTT UE and MCPTT user single log on (SA6#3)
Some procedures for authentication are also described in solution 2-3.
SA6 also agreed on information flow in 7.1 (10.1 in TS) “Registration and user authentication for MCPTT service”
Remaining work for TR 23.779:
  Evaluation of the solution and conclusion.
  Any dependency on SA3?

## Slide 18: Group affiliation
Two solutions in TR 23.779:
  Solution 11-1: Group affiliation based on OMA XDM (SA6#3)
  Solution 11-2: Group affiliation based on presence (SA6#4)
High level flows agreed for normative phase:
  7.2 (10.2 in TS) “Affiliatîon to an MCPTT group”
  7.3 (10.3 in TS) “Subscription to MCPTT group metadata”
Remaining work for TR 23.779:
  Evaluation of solutions and conclusion.

## Slide 19: MCPTT for IOPS
One solution in TR 23.779:
  Solution 12-1: Local SIP core and local MCPTT server (SA6#4)
IOPS service requirements are listed in TS 22.346
Remaining work for TR 23.779:
  Evaluation of the solution and conclusion.
  Any dependency on SA3?

## Slide 20: Status of candidate solutions in MCPTT TR 23.779 v0.8.0