## Slide 1: Proposal to rename “emergency group call cancel” “group emergency condition” “emergency state cancel” + Other corrections to emergency procedures and information flows TS23.379, TS23.281, TS23.280
Jukka Vialén, Airbus DS SLC

## Slide 2: Background
While drafting emergency call related contributions to MCCI (for SA6#19) we had difficulties to understand some message names and terms used in MCPTT and MCVideo TSs
After checking the stage 3 TSs we noticed that there are also inconsistensies in naming these procedures between stage 2 and stage
Furthermore, some other issues were found - related to emergency procedures in stage 2 TSs - that need to be corrected

## Slide 3: 1. Emergency group call cancel
Name of the procedure “MCPTT/MCVideo emergency group call cancel“ does not reflect the actual purpose of that procedure
  We propose to change this into “In-progress emergency group state cancel“
  With this change the stage2 standards would also be more aligned with their stage3 counterparts
  The detailed changes are covered in the following contributions:
    TS23.379: S6-171542 Renaming of MCPTT emergency group call cancel
    TS23.379: S6-171545 Renaming of MCPTT imminent peril group call cancel
    TS23.281: S6-171548 Renaming of MCVideo emergency group call cancel
  Related CR for off-network:
    TS23.379: S6-171546 Renaming Off-network MCPTT emergency group cancel

## Slide 4: 2. Group emergency condition
“Group emergency condition“ and “In-progress emergency group state“ are used as synonums
  We propose to use only one term - “In-progress emergency group state“ - which is also the term used in stage 3 standards
  The detailed changes are covered in the following CRs:
    TS23.379: S6-171543 Renaming of MCPTT emergency condition
    TS23.281: S6-171550 Renaming of MCVideo emergency condition
    TS23.280: S6-171556 Renaming of emergency condition

## Slide 5: 3. Emergency state cancel
Issues found in TS23.280, 23.379 and 23.281:
  ”Emergency state cancel” procedure is used to cancel the client’s emergency state
  TS 23.281 defines (off-network) ”MCVideo emergency alert cancel announcement”, but that information flow is not used in anywhere in the TS
  TS 23.379 defines (off-network) “MCPTT emergency alert cancel”, but that information flow is not used anywhere in the TS
  in off-network Emergency alert cancellation, there is no support for the following “As part of this process, the MCPTT client may also request the cancellation of the in-progress emergency condition in the group if authorized to do so.”  this text is proposed to be removed. The procedures to cancel in progress emergency condition are explained in See TS23.281, clause 7.1.3.8.1 and TS23.379, clause 10.6.3.9.1.
In stage 3, the procedure is named “Emergency alert cancel”
  TS 24.281 has 1 match for “emergency state cancel” and 61 matches for “emergency alert cancel”
  TS 24.379 has 1 match for “emergency state cancel” and 72 matches for “emergency alert cancel”
We propose to:
  Align stage 2 terminology with that used in stage 3  rename the “emergency state cancel” to “emergency alert cancel”
  Make the above mentioned correction (off-network/cancelling group emergency state)
  The detailed changes are covered in the following CRs:
    TS23.280: S6-171624 Renaming of MCService emergency state cancel and other corrections
    TS23.379: S6-171628 Renaming of MCPTT emergency state cancel and other corrections
    TS23.281: S6-171627 Renaming of MCVideo emergency state cancel and other corrections

## Slide 6: 4. Emergency state cancel, issue 2
Another (separate) issue was found from MCPTT and MCVideo stage 2
  In on-network Emergency state (i.e.alert) cancellation, an authorized user can cancel the local emergency state of another user  but related IE is missing from the information flows.
  This is corrected in the following CRs:
    TS23.379: S6-171544 Correction to MCPTT emergency state cancel information flows
    TS23.281: S6-171617 Correction to MCVideo emergency state cancel information flows