## Slide 1: Discussion on roaming between ECSP
Yanmei Yang, Yajie Hu, Niranth
Source: Huawei, Hisilicon

## Slide 2: Outline
Business relationship
OAM based solution
ECS Publish using CAPIF
ECS Repository

## Slide 3: Business relationship for ECSP roaming
UE subscribe the edge service roaming from Home ECSP
  Home ECSP get payment from the its subscribers for committed edge service roaming for certain application, so that the subscriber can be served by partner ECSP while roaming
  Home ECSP should put the certain application into the roaming service agreement with partner ECSP in advance
  APP#2 in figure-1 should be in the User subscription data and also in the roaming agreement between home ECSP and partner ECSP.
ASP subscribe the edge service roaming from Home ECSP
  Home ECSP get payment from the ASP for committed edge service roaming for its application, so that the subscriber can be served for its application by partner ECSP while roaming
  Home ECSP should put the certain application into the roaming service agreement with partner ECSP in advance
Home ECSP
Partner ECSP
Roaming agreement(APP#2)
App#1
App#2
App#2
App#3
UE
Home ECSP
Partner ECSP
Home ECSP
Partner ECSP
App#1
App#2
App#4
UE
Home ECSP
Partner ECSP
ASP
Service Subscription (App#2)
Obtain service while roaming
App#2
Service Subscription ((APP#2) )
Roaming agreement (APP#2)
Service agreement (APP#2)

## Slide 4: ASP subscribe service from multiple ECSPs (non- ECSP Roaming)
  ASP subscribe the edge service from multiple ECSPs
  Which ECSP(s) could support edge service for application#2 is known to the ASP and should also be provisioned to UE by ASP (the ASP should let UE know the ECSP information including ECS address for receiving service at certain location)
    NOTE: The Federation interface may be used for onboarding App#2 to multiple ECSP system
  One ECSP is not required to be aware of the availability of certain application in another ECSP
ECSP#1
ECSP#2
App#1
App#2
App#4
UE
ECSP#2
ASP
App#2
Service Subscription ((APP#2) )
Roaming agreement (APP#2)
Service agreement (APP#2)
Service agreement (APP#2)
UE
ECSP#1

## Slide 5: OAM based solution for ECSP roaming
Home ECSP
Partner ECSP
Roaming agreement establishment via TMF
App#1
App#2
App#2
App#3
Home ECSP and partner ECSP will sign the roaming agreement for APP#2
Home ECSP
Partner ECSP
App#1
App#2
App#2
App#3
App#4
App#4
Partner ECSP | 
> EAS#2 | Roaming service area#2
Phase#2 OAM system will configure the roaming information in the ECSP
Table-1: ECS information in the Home ECSP
Roaming agreement updated via TMF
Partner ECSP | 
> EAS#2 | Roaming service area#2
> EAS#4 | Roaming service area#4
Table-2: updated ECS information in the Home ECSP
Home ECSP and partner ECSP will update the roaming agreement for APP#4
Phase#2 OAM system will update the roaming information in the ECSP
Phase #1 roaming agreement establishment
Phase #1 roaming agreement updated

## Slide 6: ECS Publish using CAPIF
CAPIF core Function is used for API service but not for roaming service
  The charge mode and charging policy is different between API consuming service and the roaming service
  For Roaming service contains more information ,it should also cover the information about which information is not cover by CAPIF system e.g. service agreement for which applications , valid in which area, and even user type. These type of thing is not in CAPIF’s scope
  Roaming is related to the both roaming consumer between two ECSPs or MNOs

## Slide 7: ECS configuration repository
ECS configuration repository used for maintain information of the partner ECSP
  One ECS amongst the 10 federated ECSs plays the role of a ‘designated ECS’. Address information of the designated ECS is preconfigured in other ECSs of the federation.
  ECSs of the federation register and store information of federated edges at the designated ECS.
  When federation wide EAS discovery is required, the ECS queries the designated ECS.

## Slide 8: Summary
It is important to have common understanding of the business relationships for roaming cases. Suggest to capture the business relationships in the TR.
The OAM based solution for ECS configuration is the most compatible way considering existing ECSP operations to address the roaming cases.

## Slide 9
Thank You!