## Slide 1: Edge Service Delivery Scenarios
Basu
Samsung

## Slide 2: Outline
Example Deployment & Agreements
Scenario 1: Basic
Scenario 2-1/2: Roaming (Home-routed)
Scenario 3: Edge Node Sharing
Scenario 4-1/2/3: Roaming (Local Break-out)
Conclusion

## Slide 3: Example Deployment & Agreements
ECSP Service agreement: For ASP to consume the edge services (e.g., infrastructure, platform) provided by the ECSP.
PLMN Service agreement: For enabling end users to consume edge services (e.g., infrastructure, platform) provided by the ECSP via PLMN provided connectivity.
Roaming agreement: For visited users to join an edge service on the network they are attached to, MNOs need to share a roaming agreement. Local Break-out or Home-routed configuration may exist.
Federation agreement: For deploying and exposing applications on another ECSP’s infrastructure to their subscribers.
An ASP can have agreement with multiple ECSPs.
An ECSP can have agreement with multiple PLMNs.
Multi-device (for single user) is not shown for simplicity.
NOTE: ECS is not shown for simplicity but where applicable it is considered for explaining scenarios in further slides.

## Slide 4: Scenario 1: Basic
UE-1 connects to home PLMN-P for receiving service from EAS-A (of ASP-A)
EAS-A (of ASP-A) is registered to EES-X (of ECSP-X)
EEC-X registers with EES-X (of ECSP-X), and sends service discovery request to discover EAS-A (of ASP-A) on home network
  EES-X provides EAS-A information to EEC-X
AC connects to EAS-A (of ASP-A)
NOTEs:
Roaming agreement with other PLMNs is not required
Federation agreement with other ECSPs is not required
ECSP-X has PLMN service agreement with PLMN-P

## Slide 5: Scenario 2-1: Roaming (Home-routed)
UE-1’ (roaming UE) connects to home PLMN-P via PLMN-Q for receiving service from EAS-A (of ASP-A)
EAS-A (of ASP-A) is registered to EES-X (of ECSP-X)
EEC-X registers with EES-X (of ECSP-X) via PLMN-Q, and sends service discovery request to discover EAS-A (of ASP-A)
  EES-X provides EAS-A information to EEC-X
AC (on UE-1’ - roaming UE) connects to EAS-A (of ASP-A) via PLMN-Q
NOTEs:
Roaming agreement between PLMN-Q and PLMN-P is required
Federation agreement with other ECSPs is not required
ECSP-X has PLMN service agreement with PLMN-P
EAS-A is not available on ECSP-Z and this scenario is considered as Edge Computing on best effort basis.

## Slide 6: Scenario 2-2: Roaming (Home-routed)
UE-1’ (roaming UE) connects to home PLMN-P via PLMN-Q for receiving service from EAS-A (of ASP-A)
EAS-A (of ASP-A) is registered to EES-X (of ECSP-X)
EEC-X registers with EES-X (of ECSP-X) via PLMN-Q, and sends service discovery request to discover EAS-A (of ASP-A)
  EES-X provides EAS-A information to EEC-X
AC (on UE-1’ - roaming UE) connects to EAS-A (of ASP-A) via PLMN-Q and PLMN-P
NOTEs:
Roaming agreement between PLMN-Q and PLMN-P is required
Federation agreement with other ECSPs is not required
ECSP-X has PLMN service agreement with PLMN-P
EAS-A is not available on ECSP-Z and this scenario is considered as Edge Computing on best effort basis.

## Slide 7: Scenario 3: Edge Node Sharing
UE-1 connects to home PLMN-P for receiving service from remote EAS-C (of ASP-C)
EAS-C (of ASP-C) is registered to EES-Z (of ECSP-Z)
Registered EAS information is shared by ECSP-Z to ECSP-X over E/WBI, based on federation agreement
EEC-X registers with EES-X (of ECSP-X), and sends service discovery request to discover EAS-C (of ASP-C)
  EES-X provides EAS-C information to EEC-X, based on shared EAS information between ECSP-X and ECSP-Z
AC connects to EAS-C (of ASP-C)
NOTEs:
Federation agreement between ECSP-X and ECSP-Z is required
Roaming agreement with other PLMNs is not required
ECSP-X and ECSP-Z have PLMN service agreement with PLMN-P
PLMN-P will ensure the IP connectivity towards EAS-C

## Slide 8: Scenario 4-1: Roaming (Local Break-out)
UE-1’ (roaming UE) connects to home PLMN-Q for receiving service from EAS-C (of ASP-C)
EAS-C (of ASP-C) is registered to EES-Z (of ECSP-Z)
EES information is shared between ECS of ECSP-X and ECSP-Z over E/WBI, based on federation agreement
ECS-X redirects UE-1’ to EES-Z (of ECSP-Z)
EEC-X registers with EES-Z (of ECSP-Z) via PLMN-Q, and sends service discovery request to discover EAS-C (of ASP-C)
  EES-Z provides EAS-C information to EEC-X
AC (on UE-1’ - roaming UE) connects with EAS-C
NOTEs:
Roaming agreement between PLMN-Q and PLMN-P is required
Federation agreement between ECSP-X and ECSP-Z is required
ECSP-X and ECSP-Z have PLMN service agreement with PLMN-P and PLMN-Q respectively

## Slide 9: Scenario 4-2: Roaming (Local Break-out)
UE-1’ (roaming UE) connects to visited PLMN-Q for receiving service from EAS-C (of ASP-C)
EAS-C (of ASP-C) is registered to EES-Z (of ECSP-Z)
EEC-X registers with EES-Z (of ECSP-Z), and sends service discovery request to discover EAS-C (of ASP-C)
  EES-Z provides EAS-C information to EEC-X
AC (on UE-1’ - roaming UE) connects with EAS-C
NOTEs:
Federation agreement between ECSP-X and ECSP-Z is required
Roaming agreement between PLMN-Q and PLMN-P is required
EEC-X is aware of ECSP-Z information from previous connection to ECSP-X via (H)PLMN-P
ECSP-X and ECSP-Z have PLMN service agreement with PLMN-P and PLMN-Q respectively

## Slide 10: Scenario 4-3: Roaming (Local Break-out)
UE-1’ (roaming UE) connects to visited PLMN-Q for receiving service from EAS-C (of ASP-C)
EAS-C (of ASP-C) is registered to EES-Z (of ECSP-Z)
EEC-X receives the ECS information from the core network (as defined by SA2)
EEC-X registers with EES-Z (of ECSP-Z), and sends service discovery request to discover EAS-C (of ASP-C)
  EES-Z provides EAS-C information to EEC-X
AC (on UE-1’ - roaming UE) connects with EAS-C
NOTEs:
Roaming agreement between PLMN-Q and PLMN-P is required
Federation agreement between ECSP-X and ECSP-Z is not required
ECSP-Z has PLMN service agreement with PLMN-Q

## Slide 11: Conclusion
Scenarios (1, 3, 4-1, 4-2, 4-3) are valid edge service delivery scenarios and should be considered while developing deployment models
Scenarios 2-1 and 2-2 are not necessarily edge service delivery scenarios.
While UE is roaming, whether the LBO scenario or the home-routed scenario is selected is based on the policy configuration
Scenarios where UE moves from one ECSP serving area to another ECSP serving area is FFS.