## Slide 1: Enhance FFAPP discussion
Shao Weixiang
ZTE Corporation

## Slide 2: FFAPP WID SP-221233 Objective
Develop stage 2 normative technical specification for the application layer enablement capabilities based on identified key issues, solutions and conclusions in TR 23.745, including the following aspects:
  Defining architecture requirements corresponding to the application layer support capabilities.
  The functional architecture of the FF application layer illustrating the application layer support capabilities being utilized by the FF application specific entities (e.g. factory automation system and application residing on AGV, robot).
  Procedures and information flows supporting the related solutions and usage of SEAL procedures.
  Support integration of Operation Technologies (e.g. OPC-UA) with 5G system by utilizing application support layer capabilities (e.g. CAPIF, SEAL).
  Enhancements related to geographic location and positioning information support
  Support for Private slice monitoring
  Support for Edge computing deployment
  Message communication support for non-TSN messaging communications
  Support for TSC services
  Establishing communication with FF application service requirements

## Slide 3: FFAPP WID Objective status
WID Objective | Current status
Defining architecture requirements | Support in TS23.545 Clause 4.1.2
functional architecture of the FF application layer | Support in TS23.545 Clause 5
Procedures and information flows supporting the related solutions and usage of SEAL procedures | No normative solution in TS23.545 Clause 7 Only usage of SEAL IM, KM
Support integration of Operation Technologies (e.g. OPC-UA) | No TR23.745 have no solution, only analysis in annex B
Enhancements related to geographic location and positioning information support | TS 23.434 9.3 location management Guideline TS23.545 annex C.0
Support for Private slice monitoring | Support in TR 23.700-99, TS23.435 Guideline TS23.545 annex C.0
Support for Edge computing deployment | Support in TS23.545 annex A.3
Message communication support for non-TSN messaging communications | Support in TS23.545 annex C.2
Support for TSC services | Support in TS 23.434 14.3.7 & 14.3.8 Guideline TS23.545 annex C.1
Establishing communication with FF application service requirements | Support in TS 23.434 14.3.9 Guideline TS23.545 annex C.0

## Slide 4: FFAPP WI status
FFAPP WI
TS 23.545 FFAPP
functional architecture and Guideline for service enablers usage in the Annex, no normative solution with procedures and information flows
TS 23.434 SEAL
finished
It is needed to have new SID for enhance FFAPP

## Slide 5
Mobile robots / AGVs cooperative carrying use case, from TS 22.104 Annex A.2.2.5
Key issues:
  UE to UE / ProSe communication, PC5 parameters provisioning
  low power high accuracy positioning application level location tracking
  Service Continuity for assisted (network-controlled) sidelink communication and non-assisted sidelink communication
Enhance FFAPP Use case 1
Figure A.2.2.5-1: Mobile robots / AGVs carrying a large work piece cooperatively

## Slide 6
Digital twin based production quality maintenance use case, from TS 22.104 Annex A.2.3.4
Key issues:
  Automatic process with AI/ML, usage Application Data Analytics Enablement Service
  Manual process with AR server, FFAPP supporting for Tactile and multi-modal communication service
Enhance FFAPP Use case 2

## Slide 7
Ranging-based services use case, from TS 22.261 6.37
Key issues:
  UE to UE / ProSe communication
  energy efficient UE ranging operation
  start ranging and stop ranging according to the application layer’s demand
  provision and manage ranging operation and configurations
Enhance FFAPP Use case 3
Figure 6.37.1-1: Illustration of ranging between UEs with or without 5G coverage

## Slide 8
Tactile and multi-modal communication service use case, from TS 22.261 6.43
Key issues:
  3rd party application for the set of UEs and data flows, the expected QoS handling and associated triggering events, other coordination information
Enhance FFAPP Use case 4
Figure 6.43.1-1. Multi-modal interactive system

## Slide 9
Machine vision uses cases in industrial automation, from 5G-ACIA WI 073 “Use Cases and Requirements of Machine Vision in Industrial Applications with 5G”
Key issues:
  Network monitoring by the FF UE
  extended QoS monitoring and reporting
Enhance FFAPP Use case 5

## Slide 10
5G NPN uses cases, from 5G-ACIA WI 075 “5G NPNs for Industrial scenarios”
Key issues:
  support service mobility between the Home SNPN and the SNPN equivalent to the home
  support of localized services provided at specific and limited area for a specific period of time
Enhance FFAPP Use case 6

## Slide 11: Thank You!