## Slide 1: Broadband Callout
Hans Petter Naper
Nkom / TCCA

## Slide 2: Broadband Callout
Hans Petter Naper, DSB, Norway TCCA CCBG Broadband Callout Task Force chair
3GPP SA6, Gothenburg Sweden, 21-25 August 2023

## Slide 3
Background
What is callout?
Mechanism to reliably alert personnel about incidents
Personnel responds to alert (Accept / Standby / Reject)
Used in TETRA networks today
Usage in Norway Nødnett: widely by health and fire, also others
TETRA callout client-server specification:
  Functionality in radio terminals
  Control room functionality
  TCCA TETRA Interoperability Profile (TIP)
  SDS transport for callout messages
  Callout information phase: SDS and PTT
Now being defined for MC broadband

## Slide 4: Callout – basic use case
The control room operator receives e.g. an emergency call from the public
The operator selects personnel to be alerted, formulates a message, and sends a Callout Alert message to the personnel
  Sending can be one-to-one, and/or to a group

## Slide 5: Callout – basic use case
Receiving radio terminals sound an audio signal and display the message
  Each radio terminal can send a delivery ack
  Other services not allowed during callout, except outgoing emergency
The personnel should manually respond to the Alert, by returning a predefined message (Accept, Reject, Standby)
  Each radio terminal enters the callout group (if Accept or Standby)
The operator can send further group text or group voice to callout group
Personnel can respond with text or group voice
Control room sends a Callout End
  Terminals resume to normal operation

## Slide 6
Broadband Callout: Target for the work
Define a BB callout service, interoperable between devices and control rooms
Base broadband callout on TETRA callout
  Simple, to-the-point functionality
  Easier transition when TETRA and BB callout are similar
Few enhancements:
  Longer message texts
  Location of incident sent to device, e.g. for map display
  Users can exit before callout end to attend other device communication
Define in TCCA Service Overview and Service Definition documents (~TIP)

## Slide 7
Broadband Callout over MCX
Use MCData SDS (QCI 69/70), MCPTT for messages and callout group calls
High priority delivery, SDS latency is less important than reliable delivery
SDS length restriction when sent in signalling control plane with QCI 69
Callout SDS messages must be delivered to the callout application
  Assumption: Identify a callout application with the Application ID IE
  TS 24.282: “The value chosen for the Application ID value is decided by the mission critical organization”

## Slide 8: Critical Communications Broadband Group Broadband Callout Task Force