## Slide 1: Discussion on roles and usages of eMMTel Enabler
Yue Liu
China Mobile

## Slide 2: High level architecture of eMMTel enabler

## Slide 3: Use case 1: Application/VAL application as a call party
application providers/VAL service provider may either acts as a UE or a AS in the call.
eMMTel call session is established between UE and eMMTel Enabler. eMMTel Enabler maintains the call session.
eMMTel Enabler acts as a media gateway for the eMMTel audio/video media and acts as HTTP proxy in the Bootstrap/Application data channel
Controlling (e.g. call establish, terminate, etc) and Signalling APIs (e.g. maps SIP signalling to APIs) are needed

## Slide 4: Use case 2: eMMTel 3rd party call
eMMTel call session is established between two UEs but eMMTel Enabler needs to establish temporary session to establish eMMTel call session between two UEs. eMMTel Enabler maintains the temporary session
Only Controlling APIs are needed

## Slide 5: Use case 3: eMMTel application Controller
eMMTel Enabler interacts with DCSF/MF/enhanced MRF via DC3/DC4/MDC2/MDC3 to set the downloading policy/control the downloading of DC applications
Only Controlling APIs are needed

## Slide 6: High level functionalities of eMMTel Enabler
eMMTel Enabler has the following functionalities in different use cases
SIP signalling/media user agent when acts as a call party.
Controller in all three use cases, i.e. acts as a call party, acts as 3rd party call controller, and DC application downloading controller.
HTTP Proxy when acts as a call party and establishes a Bootstrap data channel.
Conclusion: the functionalities listed above are considered as basis of the eMMTel Enabler layer architecture