## Slide 1: DP on some Common EAS use assumptions
Catalina Mladin
Delegate, Convida Wireless LLC.

## Slide 2: Hidden Assumptions 1 and 2
If an AC is to be provided service, its AC Profile would be the same if it needs services stand-alone or as group-member.
AC Profiles of all ACs in the group are the same
If the assumptions above stand, one implication is that EAS services are generally undifferentiated, with no support for asymmetric applications.
  Why are we not doing EAS discovery only based on AC ID and location?
  Why would be more differentiation needed between different types of stand-alone service, than between stand-alone and group-member service?
If the assumptions above do NOT stand->EAS choice changes with more info-> info to make best EAS choice from first group-member AC request needed -> providing Common EAS criteria (e.g. KPIs) in Application Group profile is useful.

## Slide 3: Hidden Assumption 3
The EES knows the scaling of the EAS requirements from 1 AC to max number of group ACs (via non-SA6 signaling from a “group management CAS”), therefore it can make choice of best Common EAS just based on individual AC Profiles and group ID
If the assumption above stands, one implication is that the “group management CAS” knows also where the group will be (it identifies the EESs to give this info to) OR it sends this info to all possible EESs.
  Either way, wouldn’t it more effective to just send all the group info to all (or all identified) EES, and never provision the ACs with Application Group Profile?
  Either way requires strong cooperation between ASP and ESP, so that ESP provides visibility/ access to EESs. This info can be quite dynamic, so semi-static configuration would not work.

## Slide 4: Hidden Assumption 4
The Common EAS for a group can be stored at the CR, as soon as it is determined (at EAS discovery request processing) independent of whether the AC actually uses the Common EAS services or not.
CR storage implies longer and broader use of the information.
If the assumption above stands one implication is that EAS discovery requests are performed only or mainly for the purpose of immediate use of a discovery for connection to EAS. This is inconsistent with our introduction of EAS info provisioning for EEC to EES.
Alternatively, providing Common EAS from EES to CR has only the meaning of “Common EAS has been matched” rather than “Common EAS has been identified and is in use”. This can cause multiple non-functional Common EAS matches to exit in ER and be used incorrectly, delaying group conversion to the same EAS.

## Slide 5: Proposal
Convida’s proposal is to not rely upon these assumptions, especially since they are not clearly spelled out in the spec.
If agreed to the above, the proposal for hidden assumptions 1-3 is to include “Common EAS criteria” as optional IE in the Application Group ID. This also resolves 2 ENs in clause 8.2.11.
If agreed to the above, the proposal for hidden assumption 4 is to query the ECS-ER at discovery and optionally to store new information during discovery. In addition, specify that storage of newly determined information may occur at EAS information provisioning. This also resolves 1 EN in clause 8.5.2.2.

## Slide 6: Summary
SA6 should decide if relying upon hidden assumptions is reasonable. If not, it can choose to either spell them out or adopt other TS fixes.
If agreed to adopt other TS fixes, the proposal is to:
  include “Common EAS criteria” as optional IE in the Application Group ID.
    Optionality allows also for deployments that want to stick with the assumptions to implement current functionality.
    “Common EAS criteria” proposed re-uses Table 8.2.5-1 (EAS Service KPIs), just provided for the group service rather than stand-alone service.
  Change text in 8.5.2.2 to query ECS-ER and optionally store new information during discovery. Specify that storage of newly determined information may occur at EAS information provisioning, in clause 8.15.2.2.