## Slide 1: FS_5GSAT_APP: Study on application enablement for Satellite access enabled 5G Services Supporting discussion paper
03 Oct, 2023
Basu Pattan (Samsung)

## Slide 2: Content
Background
Group communication
Application Service Delivery impacts due to UE Mobility
Application Service Delivery impacts due to Satellite in Motion

## Slide 3: Background
Three area types based on different access coverage:
  Only Satellite Access (NTN)
  Only Terrestrial Access (TN)
  Both TN and NTN
UE-A connects to TN only
UE-C connects to NTN only
Theoretically, UE-B can connect to both TN and NTN, however Rel-18 defines:
  UE-B does not connect to TN and NTN simultaneously, and
  UE-B may connect either to TN or NTN
RAT Type for satellite access in 5GS:
  NR(LEO), NR(MEO), NR(GEO) and NR(OTHERSAT)
RAT Type for satellite access in EPS:
  WB-E-UTRAN(LEO), WB-E-UTRAN(MEO), WB-E-UTRAN(GEO), WB-E-UTRAN(OTHERSAT), NB-IoT(LEO), NB-IoT(MEO), NB-IoT(GEO), NB-IoT(OTHERSAT), LTE-M(LEO), LTE-M(MEO), LTE-M(GEO) and LTE-M(OTHERSAT) for satellite access with WB-E-UTRAN, NB-IoT or LTE-M
Typical two way propagation delay e.g. ~540ms for GEO, ~42ms for LEO at 1200km, and ~26 ms for LEO at 600km
End-to-end Latency: includes latency at access network, backhaul, core network and inter-connected networks

## Slide 4: Group communication
Scenario: Mission Critical (MC) Group Members present across all 3 area types.
TS 23.501 defined 5QIs (related to Mission Critical):
MC KPIs:
To take advantage of coverage enhancement, MC service shall consider all Group Members but added Propagation Delays in Satellite Access impacts communication experience
Typical two way propagation delay:
  ~540ms for GEO, ~42ms for LEO at 1200km, and ~26 ms for LEO at 600km

## Slide 5: Application Service Delivery impacts due to UE Mobility
Scenario: UE-A connected to one RAT type and moves to coverage area of another RAT type
UE can receive service via unicast or multicast or broadcast
When UE is in mobile, access type change might happen and continuing delivery of service via currently selected method may not be efficient

## Slide 6: Application Service Delivery impacts due to Satellite in Motion
Scenario: UE-A is connected to Satellite access for service delivery and Satellite is in motion
When Satellite is in motion and available, UE can receive service via Satellite access i.e. a UE in Satellite access discontinuous coverage cannot receive service
When Satellite is in motion, continuous access may not be available and delivery of service is not ubiquitous

## Slide 7: Objectives (based on Rel-17 and Rel-18)
The SA6 objectives of this study item include the following:
1. Identify the impacts and the necessary changes to the SA6 enabler specifications for supporting satellite access.
a) Develop common approach to support multiple services using satellite access for capabilities identified below (not exhaustive list):
i. Enhancements to Group and Configuration management corresponding to the access the UE is connected to.
ii. Enhancements at the Application enablement layer for the Latency difference between Users/UEs in terrestrial and non-terrestrial networks for better QoE and QoS.
iii. Potential optimizations to the delivery of content from a content caching application by taking advantage of satellites in supporting ubiquitous service.
2. Enable application layer to support the predictable discontinuous /intermittent connectivity patterns between UEs and AS/AFs for IoT services with satellite access e.g. asset tracking, critical infra asset monitoring delivered through low density NGSO satellite constellations, especially in discontinuous satellite coverage.
3. Identify key issues and develop solutions to ensure support of satellite access to SA6 enablers, for capabilities identified in 1 to 2.
4. Identify satellite communication issues, solutions, and conclusions when applicable to Mission Critical services, such as:
a) Analyzing 5G Satellite access to enable large coverage areas for Mission Critical Services.
b) Impacts to Mission Critical Service KPIs (e.g. QoS, latency aspects, and bandwidth limitations) for Satellite access.
c) Resolving MC Service behaviour when MC UEs support both Satellite and 5G Terrestrial network access.
5. Possible deployment models for SA6 enablers and applications in 5G System with satellite access.
NOTE : The study of Mission Critical over Satellite access shall be based on the existing architecture and service features described in the Mission Critical specifications.

## Slide 8: Objectives for future meetings (based on Rel-19)
1. Rel-19 Stage-1 work is in progress for:
- Store and Forward Satellite operation from a data service perspective (when no simultaneous active feeder link connection to the ground segment),
- UE-Satellite-UE communication (unicast, multicast and broadcast),
- Application inputs (e.g. based on Application KPIs) in selection and establishment of suitable satellite access or terrestrial access for delivering user traffic over selected access technology (e.g. for IoT services)
2. Identify potential enabler layer issues for supporting edge computing on-board the satellite.
NOTE : For the above aspects, SA6 depends on progress and decisions made by SA2.

## Slide 9
Thank You!