## Slide 1: SA6: Discussion on removal of permissions in RNAA
Oct, 2023
NTT DOCOMO,INC
S6-232898

## Slide 2: Problem description
If the API invoker used a token once to change state in the network, e.g. change of QoS or subscribe to location information, there can be two types of behavior of the network when the token becomes invalid:
  The changes can be accepted to be permanent (e.g. an application to manage QoS)
  The changes are expected to be transient (e.g. subscription to a location service for an application, QoS change for a particular bearer for a certain time only, or until revocation)
There are two mechanisms by which a token can become invalid
  Expiration
  Revocation
 Further discussion refers to transient changes requiring action on token invalidation

## Slide 3: Possible solutions
Let the API invoker revert the state
  If the token is not valid any more, the API invoker can’t do this
  Not the correct security model for revocation
Let CCF handle state reversal
  CCF is not aware of API invocations, so it can’t call the NFs
Let AEF handle state reversal
  AEF regularly call NFs
  But: what to revert to?
Let the NFs handle state reversal
  Require upgrade of all NFs
Let a new function handle state reversal

## Slide 4: Statefulness?
Reversal to
  Default value, or
  Value before token was first used
Reversal may require knowledge of state
  What was the previous state
  Which exact resource (e.g. which bearer id)
State required for handling token expiration and revocation
Problem is not RNAA specific, but also exists in CAPIF

## Slide 5: Discussion
1. Stateful AEF
The AEF can check the NF state at first use of the token, and store this state in a repository. The AEF will also track when tokens becomes invalid, the AEF can restore the state to the stored value or to a default.
2. Stateless AEF
A separate function is required to track valid tokens and trigger state reversal. That function could either induce the AEF to reset the NF or call the NF directly to reverse the state to the given default.
Note:
Either options above (i.e. 1 or 2), require the API Invoker to indicate what the course of action should be upon token becoming invalid (based on end-users consent captured in the token)
NEF northbound APIs may require to also take in such an enhancement into account.

## Slide 6: Proposed way forward
For R-18, keep state reversal functionality internal to AEF leaving it up to implementation whether to implement separate function or add repository to AEF
For R-19, study whether standardization of a separate state reversal functionality NF is beneficial
  E.g.
    New NE (e.g. Token Invalidation Control- TIC)
    New interface between AEF and TIC
    TIC to AEF interface allows AEF to inform TIC that it needs its services (i.e. track the token invalidation for possible action)
    AEF informs TIC if either CCF (or AEF itself) invalidates a token before its expiry
    TIC takes required action and returns the state of the resource to its original state (i.e. the state before changes took place due to a prior AEF action on the resource using the given token)
    TIC on its own may also take a required action upon the token expiry (as per end- user’s consent captured in the token)

## Slide 7: Thanks