## Slide 1: MC GWUE discussion and way forward
Cuili Ge
Huawei, Hisilicon

## Slide 2: Content
Two cases , requirements
Security aspects
What is addressed in R18 –functional model, procedure
Controversial issues and way forward proposal
Huawei’s view on the MC GW mechanism

## Slide 3: Two cases , requirements
 | Functions of GWUE |  | Functions of Server side (CSC server + MC service server) |  | Author Remarks
Requirements | Case A - host MC client | Case B - NOT host MC client | Case A - host MC client | Case B - NOT host MC client | 
[R-5.15-001] | Provide N3GPP access | Provide MC client (CSC client + MC service client) | Providing MCX service (authentication, authorization…) | Providing MCX service (authentication, authorization…) | 
[R-5.15-001a] | MC system identify the GW – (MC ID, MC service ID) |  |  |  | If new ID, for what ?
[R-5.15-002] | Content unaltered/IP routing Content {CSC-n, MCX-n (signaling & floor control & media} Security: E2E b/w MC client-MC server | Content {CSC-n, MCX-n (signaling & floor control & media} Protocol conversion is required, but the field value in the protocol and payload should be unaltered |  |  | 
[R-5.15-003] | PDU session and QoS management |  |  |  | No SA6 standards impact
[R-5.15-004] | Deployment |  |  |  | No SA6 standards impact
[R-5.15-005] | UE implementation && User behavior | User behavior | UE implementation && User behavior | User behavior | No SA6 standards impact
[R-5.15-006] | identify and prevent the 2nd connection from a user for the same MCX service | Identify and prevent the 2nd connection from a user for the same MCX service | identify and prevent the 2nd connection from a user for the same MCX service | Identify and prevent the 2nd connection from a user for the same MCX service | 1 user, 2 device case is missing !!!
Case A - N3GPP device host MC client
Case B - N3GPP device NOT host MC client
Requirement cl.5.15 from TS 22.280
[R-5.15-001] The MCX Service system shall be accessible via gateway MCX UEs by MCX Users.
[R-5.15-001a] The MCX Service system shall provide a mechanism to uniquely identify a gateway MCX UE.
[R-5.15-002] Gateway MCX UEs shall ensure that the content of communications between the MCX Service System and an MCX User attached to the gateway MCX UEs is unaltered.
[R-5.15-003] Gateway MCX UEs shall handle the communication traffic attributes, e.g. priority and QoS, of an MCX User attached to a gateway MCX UE independently of other MCX Users concurrently attached to the same gateway MCX UE.
[R-5.15-004] Multiple Gateway MCX UEs shall be able to operate within the same area (e.g., site of an incident or, adjacent cells, etc.). accident, overlapping coverage
[R-5.15-005] MCX Users shall be able to select gateway MCX UEs, in case multiple, accessible gateway MCX UEs are available.
[R-5.15-006] An MCX User shall be able to access multiple gateway MCX UEs simultaneously from a single device while restricting a MCX Service to one gateway (e.g., MCPTT on gateway UE 1, MCData and MCVideo on gateway UE 2).

## Slide 4: Security considerations
MC
client
Case A - host MC client
GW conn func
Non-3GPP device
GW conn
control
GW UE
GW conn
control
Server
N3GPP access security (e.g. WiFi WEP)
Authorization of using a gateway UE by a user for MC service(s)
3GPP network
3GPP network security
MC
client
Existing MCX security: 33.180 A, B, C
Case B – not host MC client
Non-3GPP device
GW UE
Server
N3GPP access security
Signalling security:
Not SA6 scope
3GPP network
3GPP network security
Existing MCX security: 33.180 A, B, C for ‘gateway user”
MC
client
Existing MCX security: 33.180 A, B, C for GW UE
Media security: E2E
Whether it exists or not, how it works, outside SA6 scope !!!
Data exchange
Outside SA6 scope !!!
Existing MCX security: 33.180 A, B, C
Media security: E2E: call control, media plane……
MC
client
Mainly related to [R-5.15-006] , [R-5.15-001a] and local-GW
Not essential for IP packet routing for all the users and MC services
GW conn
control
GW conn
control
With this device/network level security, any MC user can use the N3GPP device to communicate with the MC system for all MC service
only specific MC user can use the N3GPP device to communicate with the MC system for specific service.
signaling security is needed.
Authorization of using a gateway UE by a user for MC service(s)
Authorization of using a gateway UE by a user for MC service(s)
Several authentication and authorization levels for different intentions:
a. Non-3GPP device/non-3GPP connection (e.g., WiFi, BT…) authentication and authorization (equivalent concept to the 3GPP UE attach and the AKA)
b. MC service user (using the N3GPP device or the MC gateway UE, let us call it “gateway user”) identity authentication
c. The authorization of using the GW UE by the “gateway user” for MC service(s), i.e., the connection authorization being discussed in SA6
d. MC service authorization to allow the “gateway user” to participate the MC service
e. MC Signalling and Media security (b/t “gateway user” and the servers)
They are NOT well organized in the spec !!!

## Slide 5: What is addressed in R18 –functional model, procedure
Figure 11.2.3-1: Function Model of MC gateway UE media plane
Figure 11.2.1-1: Functional model of MC gateway UE signalling plane
Requirements | Support (Y/N) | How
[R-5.15-001] | Y | Architecture (cl. 11.2) , CSC-n, MCX-n is transparently routed via the GW UE at IP layer. IMS subscription (cl. 11.3 ) and GW UE routing capabilities (11.4) NOTE: The new entities, RPs in the red circle NOT necessary to support 001
[R-5.15-001a] | Y(*) | MC ID and MC service ID of the GW UE NOTE: R-5.15-006 may be related with this requirement.
[R-5.15-002] | Y(*) | Media routing is different from Case A and Case B Case A: E2E, media is terminated MC client at N3GPP device Case B: Hop by Hop, media is terminated MC client at GWUE, and further delivered to the N3GPP device using other ways, e.g., UIC API
[R-5.15-003] | Y | No new work is needed in SA6.
[R-5.15-004] | Y | No SA6 impact: deployment
[R-5.15-005] | Y | No SA6 impact: UE implementation && User behavior
[R-5.15-006] | N(*) | New entities (MC gateway client, MC gateway UE server, MC gateway UE function), new RP (GW-Local, GW-Core) Cl.11.5.1 is trying to address

## Slide 6: Connection restriction is the controversial part now !!!
Way forward #1 – move the [R-5.15-006], [R-5.15-001a] to R19
R18 – support the basic traffic routing without limiting the usage of GW per service per user.
R19 – support the connection restriction per service per user, location interaction, MBMS reception
Pros: No compatible issues, easy to evolve !!!
Cons: No connection control per service per user in R18
Way forward #2 – complete the [R-5.15-006], [R-5.15-001a] in R18
R18 – support the basic traffic routing with the connection restrictions per service per user, location interaction, MBMS reception
Pros: fully support of all requirements in R18
Cons: Can not converge to the final solution, more exceptions is needed, R18 cannot delivered on time.
Even can not give a feasible features/solutions in R18.
[R-5.15-006] An MCX User shall be able to access multiple gateway MCX UEs simultaneously from a single device while restricting a MCX Service to one gateway (e.g., MCPTT on gateway UE 1, MCData and MCVideo on gateway UE 2).
[R-5.15-001a] The MCX Service system shall provide a mechanism to uniquely identify a gateway MCX UE.
LS to SA1 for clarification

## Slide 7: Huawei’s view on the MC GW mechanism

## Slide 8: Work flow
GW conn func
Non-3GPP device
GW conn
control
GW UE
IDM
3.N3GPP link/Conn security
3GPP network
1. 3GPP network security
MC
client
2.Existing MCX security: 33.180 (for GW UE itself)
10. Service authorization with MC service server
11. Other procedures：affiliation, call
MC
client
Case A - host MC client
4. Identity authentication with IDM, get MC service IDs, PTT
MC service server
(MCPTT)
2.Existing MCX security: 33.180 (for GW UE itself)
5. Application layer security:
Authentication & authorization
6. Connection authorization (MC service ID of the user)
6. Connection authorization <MC service ID of the user, + MC service ID of the GW UE>
Initial, Only Open for IDM traffic
7. Check the user is already have a GW for PTT service: Y? or N ?
8. OK
8. OK
9.Then, open the gate for MC service traffic
Without this, no way to prevent the 2nd traffic connection (same user, same service) to the server.
Without this, no need for the whole connection authorization, as the server can different connections, e.g., by IP+MC service ID
The other proposal:
Extend the service authorization to make the MC client at the Non-3GPP device to add the GW UE ID.
Issues:
(1) How and when to provide the ID of the GW to the non-3GPP device is an issue;
(2) The MC client on the non-3GPP device and the normal UE becomes different, a dedicated MC client on the non-3GPP device is needed, increase development and management of the MC client.
The identity authentication should be performed before the connection authorization.
Not service specific
Security consideration
The connection authorization should be finally allowed by the server to cover all the cases.
Why standalone entities and procedures ?
No impact to the existing configuration mechanism. No extra configuration is required by the MC client on the non-3GPP device.
The MC client on any device have the same feature and behavior.
Easy to complete with the existing R18 procedures.

## Slide 9: Work flow
Non-3GPP device
GW conn
control
GW UE
IDM
3.N3GPP link/Conn security
3GPP network
1. 3GPP network security
MC
client
10. Service authorization with MC service server
11. Other procedures：affiliation, call
Case B – NOT host MC client
4. Identity authentication with IDM, get MC service IDs, PTT
MC service server
(MCPTT)
6. Check the user is already have a GW for PTT service: Y? or N ?
7. OK
2.Existing MCX security: 33.180 (for GW UE itself)
2.Existing MCX security: 33.180 (for GW UE itself)
MC
client
Initial, Only Open for IDM traffic
Get a MC ID of a user ( from the API, or from local configuration, or user input…..
Some triggers occurs, e.g., API (non-SA6) invocation
8.Then, open the gate for MC service traffic of the user
……
Repeat for each ‘gateway user’ (non-3GPP device)
6. Connection authorization <MC service ID of the user, + MC service ID of the GW UE>

## Slide 10: Architecture and protocol stack
MC service client
MC service client
MC gateway client
MC gateway UE server
MC service client
CSC client
MC gateway UE function
CSC server(s)
3GPP network
MC service server
Common service core
GW-local
GW-core
MCX-n
CSC--n
MC gateway UE
N3GPP device
MC service client
CSC client
MCX-n
CSC-n
Signalling plane – MC client
Media plane: MCX-4/9/7/8 – MC client
N3GPP low layer
IP
TCP/UDP
SIP/RTP,RTCP/HTTP
3GPP low layer
IP
L2/L1
IP
TCP/UDP
Protocol stack – User plane (GWUE PoV)
Server
GW UE
N3GPP device
N3GPP low layer
SIP/RTP,RTCP/HTTP
MCX-n，CSC-n
3GPP low layer
IP
TCP/UDP
HTTP
3GPP low layer
IP
L2/L1
IP
TCP/UDP
HTTP
TCP/UDP
HTTP
Control plane
GW-Local
GW-core
N3GPP device
MC gateway UE server
CSC client
MC gateway UE
MC gateway UE function
CSC server(s)
3GPP network
MC service server
Common service core
MCX-n
CSC--n
N3GPP stack
3GPP low layer
L2/L1
IP
TCP/UDP
Protocol stack (GWUE PoV)
Server
GW UE
N3GPP device
N3GPP stack
SIP/RTP,RTCP/HTTP
SIP/RTP,RTCP/HTTP
IP
TCP/UDP
APP/content
APP/content
APP/content
APP/content
All the SIP/HTTP/RTP, RTCP has to terminate at the GW UE in this case!
GW-core
GW UE signalling
GW UE signalling
MCX-n，CSC-n

## Slide 11
Common services core
MC service server
MC gateway UE
3GPP network
SIP database
Rx
SIP core
AAA-1
SIP-1
SIP-2
Signalling user agent
HTTP-1
To other SIP core
Registrar finder/
I-CSCF
Local proxy/P-CSCF
Registrar-
AS selection
/S-CSCF
HTTP client
HTTP client
SIP-3
HTTP-1
HTTP server
HTTP Proxy
HTTP-3
HTTP-2
To other HTTP Proxy
MC gateway server
SIP AS
SIP AS
HTTP client
HTTP server
SIP AS
HTTP-1
HTTP-2
HTTP-3
SIP-3
Other MC system
HTTP proxy
SIP core
SIP-2
Diameter proxy
AAA-2
N3GPP device
Signalling user agent
HTTP client
SIP-1
HTTP-1

## Slide 12: Huawei’s contribution plan
Two Options
Option #A:
To R18:
  Add general description in clause 11.1 to clarity that the GWUE can provide basic traffic routing b/w N3GPP device and the MC servers as described in 11.3 and 11.4, and advanced features as described in 11.5 including connection control, location management, MBMS supporting.
  add NOTE in related clauses to clarify that the advanced features is NOT supported in R18.
  (2)Re-draw the functional model figures. Case A and Case B should use different figures to better reflect the concept.
CRs：240125~240132 (R18 CR with R19 mirror)
2. To R19:
  Bring the changes as described in P8, and P9 to R19, mainly fix the connection authorization and the configuration.
CRs：240133/ 0134/135/136 (only R19 CRs)
Option #B：
  1) R18 CRs as described in P8, and P9 to R19, mainly fix the connection authorization and the configuration.
  2) Re-draw the functional model figures. Case A and Case B should use different figures to better reflect the concept.
CRs：no CR proposed, but can create the R18 version of 240133/ 0134/135/136