## Slide 1: Discussion on the exposure of application calling service
Han Wang
Huawei

## Slide 2: IMS capability exposure in SA2(1)
"Study on system architecture for next generation real time communication services phase 2" (FS_NG_RTC_Ph2)
WT-1: Study on the enhancements to framework for exposure of IMS capability in the context of IMS data channel session
WT-1.2: how to expose existing IMS services (e.g. IMS voice/video call, message) in the context of an IMS data channel session, i.e. when DC is established.
Key issue #2: Impact on IMS architecture, interfaces and procedures to support IMS capability exposure in the context of IMS data channel session
This KI will address the following aspects:
- Study enhancements to IMS architecture, interfaces and procedures to expose IMS services in the following IMS data channel related scenarios:
- IMS data channel initiation, update and release. This includes the initiation, update and release of application and bootstrap data channels.

## Slide 3: IMS capability exposure in SA2(2)
The latest progress in SA2 about IMS capability exposure, there are two solution agreed in last meeting:
The IMSEF(a dedicated NEF instance) and DCSF provides the following services to the DC AS via DC3/DC4:
- Control operations of IMS session with data channel media, such as initiating, modifying, terminating and querying an IMS session
With this solution, there are two types of capabilities, which can be exposed via DC3/DC4 interfaces from DCSF to DCAS via Ndcsf services.
- The first type of capabilities are call related events from IMS AS via DC1 interface
- The second type of capabilities are DC related events,
IMS capability exposure architecture (S2-2401600)
Solution for IMS capability exposure via DC3/DC4 (S2-2401601)
SA2 focus on provide the basic capability of establishing an IMS session with data channel media, terminating an IMS session with data channel media, modifying an IMS session to add data channel media, etc via NEF and DCSF

## Slide 4: SA6 key issue 1 focus
NOTE : Whether there are other calling services to be studied in key issue 1 is FFS.
What calling service could SA6 provide in the precondition of SA2 had exposed all basic IMS capabilities ?
SA6‘s calling service could focuses on the scenario of interaction between application and DCMTSI client which the eMMTel enabler is required to perform protocol conversion, eMMtel enabler may has the signaling and media proxy functionality and provides calling service with data channel capability for Application providers/Vertical service providers.
Based on LiuYue’s Use case 1 (S6-232873)

## Slide 5: Summary
The capability of Application calling services provided by eMMTel enabler
May include SIP signaling/media proxy functionality.
HTTP Proxy when establishes a Bootstrap data channel and application data channel.
Summary:
the functionalities listed above are considered as basis of the key issue #1