## Slide 1: Discussion on Modifying Location Reporting Trigger Conditions
Mythri Hunukumbure, Sivasubramaniam Ramanan
UK Home Office

## Slide 2: User Group Requirement
When an emergency crew is responding to an incident, the authorized client (supervisor) would initially set the location reporting trigger parameters to certain values.
As the incident evolves, the supervisor may want to modify these parameters, rather than cancelling the current location reporting trigger and issuing a new one.
  A common example is to change the location report update rate, depending on the severity of the incident.
Currently, there are no provisions to modify an existing location reporting trigger in TS 23.280.

## Slide 3: Reporting Trigger Modify in TS 23.280
The current TS 23.280, section 10.9.1 states:
In the information flows of clause 10.9.2, and procedures of clause 10.9.3:
- the term "requesting MC service user" is used to refer to the MC service user which sends a request to subscribe to location information reports, to trigger a location information report or to modify existing location information triggers from another MC service user;
- the term "requested MC service user" is used to refer to the MC service user whose location information is requested or existing location information triggers are to be modified; and
- the term "reporting MC service user" is used to refer to the MC service user which provides location related information based on on-demand request or trigger criteria.
However, there are no information flows (10.9.2) or procedures (10.9.3) listed to enable modifying location reporting triggers.
  This should be taken up for consideration in SA6 EnhMC.

## Slide 4: Next steps
Discuss and agree the procedures for updating location reporting triggers.
We are happy to follow up with the required change request (CR) to clause 10.9 TS 23.280 to the May 2024 SA6#61 meeting.