## Slide 1: Information update regarding eMMTel
Yue Liu
China Mobile

## Slide 2: SA2 Solutions on capabilities exposure
KI#2 in FS_NG_RTC_Ph2 SI is the impact on IMS architecture, interfaces and procedures to support IMS capability exposure in the context of IMS data channel session.
Up to now, 3 solutions have been proposed in TR23.700-77, i.e. Solution#6, Solution#7 and Solution#18

## Slide 3: Solution #6: IMS capability exposure architecture
Figure 6.6.1.1-1: Architecture of IMS capability exposure
IMSEF: IMS Exposure Function, is supported by the NEF and used for external exposure of IMS capability and service to the 3rd Party DC AS. A dedicated NEF
When CAPIF is supported by the IMSEF, the IMSEF supports the CAPIF API provider domain functions
IMSEF provides:
  Control operations of IMS session with data channel media, such as initiating, modifying, terminating and querying an IMS session.
  Subscribe and unsubscribe to IMS events of the specific subscriber.

## Slide 4: Solution #7: Solution for IMS capability exposure via DC3/DC4
Figure 6.7.1-1: IMS capability exposure architecture
The Solution does not change the architecture of IMS supporting Data Channel
DCSF can return to DCAS the following information on DC3/DC4:
  response code (success or failure);
  other information, e.g. session identifier (session ID), IP address of the UE, location, MDC2 identifier, user identifier (user ID), PVNI, and external DC identifier, Call ID which can be used to determine a DC uniquely;
  notifications to the reported events (DC establishment/termination, downloaded DC application, IMS capability exposure) ; and
  session control status (DC session creation result, DC termination).

## Slide 5: Solution #18: Supporting of network initiated IMS Data Channels
The Solution does not propose a new or enhanced architecture. This Solution applies to DC-AS in the enterprise to trigger the establishment of IMS data channel(s).
NEF impacts:
  Receive data channel request from AFs for establishment, update or release of BDC and ADC.
  Send data channel request to IMS AS.
  Receive notifications of requested IMS events from the IMS AS.
  Send notifications of requested IMS events to the AF.

## Slide 6: Impacts on SA6 eMMTelAPP study
The conclusion on IMS capability exposure has not been made by SA2 yet.
The capabilities of IMS are provided via N33/DC4 references, therefore the eMMTel Enabler architecture model approved in SA6#59 will not be impacted.
The capabilities provided by eMMTel Enabler are needed to be considered based on the capabilities provided by SA2 but are integrated service capabilities rather than reusing the capabilities provided by SA2 directly.
Value added services are needed since lots of service level requirements may not be in scope of SA2.