## Slide 1: Discussion on data channel application related capability provided by SA6
Han Wang
Huawei

## Slide 2: Outline
As specified in 3GPP TS 26.114, the data channel application needs to be uploaded to DCAR before it is intended to be used.
The current discussion in the SA6:
  The upload, upgrade, and delete data channel application procedure are handled by SA2.
  The application policies need to be configured at the enable layer. So, the profile of the application will be uploaded via eMMTel enabler.
  The application and the profile of the application will be handled separately, the data channel application will be uploaded via the interface specified in the SA2, the data channel application profile will be uploaded via the interface specified in SA6.
Problems:
  Option 1: uploading applications and the profile of the application through DSCP in SA2 and eMMTel enabler in SA6
  Option 2: uploading both applications and the profile of the application through eMMTel enabler in SA6:
Solutions:

## Slide 3: Solution 1: upload applications via DSCF and upload the profile of the application via eMMTel enabler

## Slide 4: Solution 2: upload both applications and the profile of the application via eMMTel enabler in SA6

## Slide 5: Solutions Comparison
Solutions | Cons | Pons
Solution 1 : upload applications via DSCF and upload the profile of the application via eMMTel enabler | The application and the profile of the application will be handled separately, and the cooperation between DSCP and eMMTel enabler is complex. The ASP should handle and management two interfaces separately. For ASPs, the application and the profile should be uploaded at the same time, it is unacceptable that the application and the profile of the application be delivered separately. | 
Solution 2: upload both applications and the profile of the application via eMMTel enabler in SA6 |  | ASP friendly, eMMTel enabler layer provides unified interface Fewer steps Less interaction with IMS Core, e.g. the eMMTel enabler layer needs to know whether the application was uploaded before downloading the profile of the application

## Slide 6: Summary
Considering from the holistic perspective of enabling the application layer in SA6 and 5G Core in SA2.
  The application and the profile of the application both need to be uploaded via eMMTel enabler layer, which is benefit for the interaction with ASP and holistic application management.
The solution 2: upload both applications and the profile of the application via eMMTel enabler in SA6 is preferred.