## Slide 1: Discussion on EAS selection for UE group
Huawei, Hisilicon
Yajie

## Slide 2
Concept clarification: Group Delay
For group application , the Group Delay is the initiating UE to group (rest of the UEs):
  For MCPTT call “mouth to ear”, the speaker sends a voice message to the server, then the server sends the voice message to the group (rest of the UE)
  For XR gaming application, the initiating UE execute an action in XR application client, then this action information need to send to the group (rest of the UE) via the application server(s)
Thus, for group service, the group delay contains initiating UE to the server delay, and the server to the group delay, optionally contains the inter-server delay when group connect to multiple servers.
EAS#1
UE#1
UE#2
EAS#1
UE#1
UE#2
EAS#2
Application content synchronization
OPTION#1: common EAS
OPTION#2: multiple EASs

## Slide 3
Whether to select common EAS or multiple EAS
EAS#1
EAS#2
UE#1
UE#2
40ms
Due to the connection between EASs may be a dedicated connection, however the connection between UE and EAS may involve a wireless connection
Thus, the delay of UE-EAS may be longer than the inter-EAS delay
For common EAS case:
  Group delay = UE#1-EAS#1 delay (40ms+20ms) + UE#2-EAS#1 (40ms+20ms) = 120ms
For multiple EASs case:
  Group delay = UE#1-EAS#1 delay (40ms+20ms) + EAS#1-EAS#2 delay (10ms) + UE#2-EAS#1 (20ms+10ms) = 100ms
Thus in such case, selecting multiple EAS can provide a better performance for group of UE
EDN#1
EDN#2
UPF
RAN
40ms
EAS#1
EAS#2
UE#1
UE#2
40ms
20ms
10ms
EDN#1
EDN#2
UPF
RAN

## Slide 4
Whether to select common EAS or multiple EAS
EAS#1
EAS#2
UE#1
UE#2
40ms
For common EAS case:
  Group delay = UE#1-EAS#1 delay (40ms+20ms) + UE#1-EAS#1 (40ms+20ms) = 120ms
For multiple EASs case:
  Group delay = UE#1-EAS#1 delay (40ms+20ms) + EAS#1-EAS#2 delay (10ms) + UE#1-EAS#1 (40ms+20ms) = 130ms
Thus in such case, selecting common EAS can provide a better performance for group of UE
20ms
EDN#1
EDN#2
UPF
RAN
40ms
EAS#1
EAS#2
UE#1
UE#2
40ms
40ms
10ms
20ms
20ms
EDN#1
EDN#2
UPF
RAN

## Slide 5
Clarification on the delay between UE-EAS
The delay between UE-UPF and UPF-EAS is depends on the UPF and EAS deployment.
Thus the delay between UE to different EAS/UPF could be different considering the deployment of the UPF and EAS
Reference: https://www.zte.com.cn/content/dam/zte-site/res-www-zte-com-cn/mediares/zte/files/pdf/white_book/202010140914.pdf
Notes: Observation#1
#2
Way forward

## Slide 6: The end