## Slide 1: MCVideo enhancement with 5G network capabilities
Cuili Ge
Huawei, Hisilicon

## Slide 2: Content
New 5G network capabilities for media streaming service
How MCVideo service can benefit from 5G network capabilities
Potential standard work in SA6, CT1, SA4

## Slide 3
New 5G network capabilities for media streaming service also can be used for MCVideo
Category | Exposure information from Network |  | Network entity being involved and related NBI APIs
Network layer connectivity information exposure （SA2） | UL/DL congestion (QoS monitoring) |  | NBI API Nnef_AFsessionWithQoS_Sub/Noti or Npcf_PolicyAuthorization_Sub/Noti (w/o NEF) Nnef_EventExposure_Sub/Noti or Nupf_EventExposure (w/o NEF)
 | UL/DL Data rate |  | 
 | UL/DL/RT delay |  | 
 | Estimated bandwidth |  | NBI API Nnef_AnalyticsExposure_Sub/Noti or Nnwdaf_AnalyticsSubscription_Sub/Noti (w/o NEF)
 | UL/DL congestion (L4S feedback) |  | NBI API Nnef_AFsessionWithQoS (to set the L4S indication) ECN marking for L4S at UPF or RAN towards UE/AS
Application layer information exposure （SA4） | QoE metrics UE data |  | Data collection AF Naf_EventExposure_Notify Nnwdaf_AnalyticsSubscription_Sub/Noti (w/o NEF)
NOTE: Other capabilities for media streaming not listed in above table are not applicable for MCVideo, e.g., multi-model service ID, data collection for consumption reporting

## Slide 4
How MCVideo can benefit from such capabilities
Network exposure information | MCVideo service work flow | SA6 standard impact
1. UL/CL congestion (QoS monitoring notification) or UL/CL congestion (L4S feedback) | MCVideo server and MCVideo client negotiate L4S capability. MCVideo server obtains the network UL/DL congestion information via the (a) QoS monitoring or (b) RTCP feedback report (per RFC 6679, RFC 8888); MCVideo servers may adapt the RTP packet sending rate | L4S capability negotiation between MCVideo server and MCVideo client Subscribe the QoS monitoring from 5GC/request L4S ECN marking MCVideo client sends the RTCP with L4S feedback report MCVideo behavior general descriptions
2. UL/DL Data rate | MCVideo server subscribes DL/DL data rate from the 5GC MCVideo server triggers the may adapt the RTP packet sending rate | Subscribe the QoS monitoring from 5GC General MCVideo behavior descriptions
3. UL/DL/RT delay | MCVideo server subscribes RT delay from the 5GC MCVideo server may initiate adapt the RTP packet sending rate | Subscribe the QoS monitoring from 5GC General MCVideo behavior descriptions
4. Estimated bandwidth | MCVideo server subscribes Estimated bandwidth from the 5GC MCVideo server adapt the RTP packet sending rate | Subscribe the QoS monitoring from 5GC General MCVideo behavior descriptions
5. QoE metrics UE data | MCVideo subscribe the QoE metrics UE data MCVideo server may adapt the RTP packet sending rate | Subscribe the QoE metrics data from 5GC/Data Collection AF General MCVideo behavior descriptions
Example: Video Push
Application and signaling
Transmission control
MCVideo server
5GC
NG-RAN
MCVideo UE
RTP pkt
Modem
Application and signaling
Media distribution
Media mixer
Transmission control
SIP messages
Transmission control messages
❶ Network exposure information Sub/Noti
❹ DL RTP sending rate control
❷ L4S capability negotiation
❸ UL L4S feedback
Media control messages
Media control
Media control

## Slide 5
Potential standard work in SA6, CT1, SA4
SA4
Codec
FEC
QoE metrics
SA6
Application and signaling plane: MC client/server’s L4S capability negotiation
Media Plane:
  Transmission control
MCVideo codec in TS 26.281:
Default - H.264 (AVC) codec
  encoding and decoding: 240p. ~720P. (~1080P.)
  Tx/Tx: 10fps to 30fps, 240p to 1080p
Optional - H.265 (HEVC) codec
Application and signaling plane: SIP registration enhancement with L4S capability negotiation  TS 24.281
Media Plane:
  MC client L4S feedback using RTCP per RFCs  TS 24.581
  RTP transmit rate adaptation behavior at the  TS 24.581
For simplicity, only one user is shown
Application and signaling
Transmission control
MCVideo server
5GC
NG-RAN
MCVideo UE
RTP pkt
Modem
Application and signaling
Media distribution
Media mixer
Transmission control
SIP messages
Transmission control messages
❶ Network exposure information Sub/Noti
❹ DL RTP sending rate control
❷ L4S capability negotiation
❸ UL L4S feedback
Transmission control messages and MBMS subchannel control messages are defined with RTCP coding
RTCP message
Observation #2a: SA6 and CT1 already extend the RTCP to support transmission control and MBMS
CT1 already define how to forward the RTP media packet, immediately forward, discard, buffer…..
Observation #2b: SA6 and CT1 already define how the RTP packet is forwarded, immediately forward, discard, buffer…..
Observation #3: SA4 may has work on the codec adaptation (e.g., resolution, framerate)
Media control messages
Media control
Media control
Codec
Codec
New work area
Media Plane control:
  MC client L4S feedback per L4S ECN marking (DL congestion)
  RTP transmit rate adaptation
Observation #4: Both SA4 (common) or SA6(MCVideo specific) may work on the new area
CT1
Observation #1: The application and signaling and interaction with 5GC is inSA6 scope

## Slide 6
SA6 MCVideo standards potential changes
1. MCVideo server and MCVideo client negotiate L4S capability
2. MCVideo server subscribe the network exposure information via QoS monitoring or activate the L4S, use the QoE metrics mechanism from SA4 to get the QoE metrics.
3. The media control aspects as a) and b) are FFS.
  a). MCVideo client sends L4S feedback report via RTCP message
  b). MCVideo server subscribes the network information/QoE information for the 5GC, and may adapt the RTP packet sending rate