## Slide 1: MC GWUE discussion and way forward
Cuili Ge
Huawei, Hisilicon

## Slide 2: Content
R18 clean up
R19 clean up and enhancements

## Slide 3: R18 clear up
TS 23.280
  (1) Cl.3 - Definitions related with the function entities designed for the conneciton authorization (MC gateway client, MC gateway UE server, MC gateway UE function)
  (2)Cl.8.1.7 - GW MC service ID should be voided and its coressponding usage in other clauses i.e., 11.4.3 and clause 11.5
  (3)Cl.11
    11.1 – functionalities clear up to remove the functions cannot be supported in R18.
    11.2 –
      Functional model update to remove the MC gateway client, MC gateway UE server, MC gateway UE function, related reference points,
      connection authorization of the association b/t MC client on the non-3GPP device and the MC gateway UE,
      media plane aspect clean up (only unicast delivery from the MC server to the MC client in the non-3GPP device is supported)
    11.5 – The whole 11.5 should be voided.
  (4)Annex A.7 – The whole A.7 should be voided.
  (5)Annex D – should be updated to clean the conneciton authorization related aspects.
TS 23.379, TS 23.281, TS 23.282
  Removal of the GW MC service ID in the annex A.5

## Slide 4: R19 clean up and enhancement
TS 23.280 - Main difference
  (1) Function model update with new application layer function entities in non-3GPP device, MC gateway UE and the MC service server, and the corresponding reference points. They are needed as to:
    Support the 3GPP specific location reporting configuration and location report
    MBMS signaling handlings to instruct the MC gateway UE to receive the MBMS traffic from the MC service server
  (2) the location management procedure is corrected:
    The new application layer function entities are used to handle such location signallings between the non-3GPP device and the MC gateway UE
    The identity used in the signallings between the non-3GPP device and the MC gateway UE is the MC service ID of the MC service user
  (3) the MBMS signaling and media receiving procedure is corrected:
    The new application layer function entities are used to handle such MBMS signallings between the non-3GPP device and the MC gateway UE
    The MapGroupToBearer and UnMapGroupToBearer message dose not to be handled by the MC gateway UE
  (4) the connection authorization of the use of MC gateway UE for one or more service(s) is optionally required due to:
    Early packet/traffic dropping at the MC gateway UE in order to efficiently make use of the limited Uu resource of the MC gateway UE (compared with forwarded the traffic to the MC service server and the MC service server reject such traffic, the Uu transmission resource is wasted in DL/UL directions)
    The conditions of MC gateway UE changes, early disconnection notification to the non-3GPP device for better user experience (compared with re-try several times after the link between non-3GPP device and the MC gateway UE is broken.
    How the connection authorization procedure is look like to satisfy the above requirements? The new application layer function entities are used (next page)

## Slide 5: Work flow
Conn Ctrl client
Non-3GPP device
Conn Ctrol GW
GW UE
IDM
2.N3GPP link/Conn security
3GPP network
1. 3GPP network security
IDM client
3.Existing MCX security: 33.180 (for GW UE itself)
10. Service authorization with MC service server
11. Other procedures: affiliation, call……
MC
client
Case A - host MC client
4. Identity authentication with IDM, get MC service IDs, PTT
MC service server
(MCPTT)
5. Connection authorization (MC service ID of the user)
6. Connection authorization <MC service ID of the user, + MC service ID of the GW UE>
Initial, Only Open for IDM traffic
7. Check the user is already have a GW for PTT service: Y? or N ?
8. OK
8. OK
9.Then, open the gate for MC service traffic
Conn Ctrol GW
This is to control the routing of certain MC service(s) traffic of the MC service user at the MC gateway UE to be open/close.
i.e., the MC service user is authenticated, but it does not mean all the traffic/content from this MC service user is allowed to be routed via the MC gateway UE.

## Slide 6: Work flow
Non-3GPP device
GW conn
control
GW UE
IDM
2.N3GPP link/Conn security
3GPP network
1. 3GPP network security
MC
client
10. Service authorization with MC service server
11. Other procedures：affiliation, call
Case B – NOT host MC client
4. Identity authentication with IDM, get MC service IDs, PTT
6. Check the user is already have a GW for PTT service: Y? or N ?
7. OK
3.Existing MCX security: 33.180 (for GW UE itself)
MC
client
Initial, Only Open for IDM traffic
Get a MC ID of a user ( from the API, or from local configuration, or user input…..
Some triggers occurs, e.g., API (non-SA6) invocation
8.Then, open the gate for MC service traffic of the user
……
Repeat for each ‘gateway user’ (non-3GPP device)
6. Connection authorization <MC service ID of the user, + MC service ID of the GW UE>
MC service server
(MCPTT)
Conn Ctrol GW
This is to control the routing of certain MC service(s) traffic of the MC service user at the MC gateway UE to be open/close.
i.e., the MC service user is authenticated, but it does not mean all the traffic/content from this MC service user is allowed to be routed via the MC gateway UE.