## Slide 1: Discussion on multi-flow sync for multi-modal XR application
Jian Zhang
Huawei, Hisilicon

## Slide 2: The multi-flow sync for multi-modal application in SA2 (AF is requested to provide the service requirement)
Reference: Clause 5.37.2 in TS 23.501
Reference: Clause 6.1.3.27.3 in TS 23.503
As specified in TS 23.501 and TS 23.502 (as highlighted by red line in left figures), the multi-modal flow sync provides the request to application server/AF to provide the data flow description and the corresponding QoS requirements.
Therefore, application server/AF should determine the multi-modal flow information and the QoS requirements to request 5G network to perform the multi-modal flow sync.
This paper focuses on how to determine the multi-modal flow information and the QoS requirements by SEALDD server based on E2E transmission measurement result.

## Slide 3: The E2E transmission delay components and flow sync in SEALDD architecture
RAN
UPF
SEALDD client
XR server
XR client
5G CP
N33/N5
UE
SEALDD server
The E2E transmission delay
5G network transmission delay
N6
N3
Uu
N6 transmission delay
For the application data transmit via SEALDD architecture, the E2E transmission delay includes two parts, i.e., the network delay between UE and UPF, and the N6 transmission delay between UPF and SEALDD server.
For multi-modal application data, the multi-flow sync depends on whether the E2E transmission delay of SEALDD traffic for different media data (e.g. video, haptic, etc) can satisfy the required delay difference threshold (e.g. 2ms).
  Case#1 (flow sync is satisfied): E2E transmission delay for video - E2E transmission delay for haptic <= 2ms
  Case#2(flow sync is not satisfied): E2E transmission delay for video - E2E transmission delay for haptic > 2ms
SEALDD traffic#1 for video
SEALDD traffic#2 for haptic

## Slide 4: The multi-flow sync for multi-modal application in SA2 (without N6 knowledge)
RAN
UPF
SEALDD client
XR server
XR client
5G CP
N33/N5
UE
SEALDD server
5G network transmission delay
N6
N3
Uu
SEALDD traffic#1 for video
SEALDD traffic#2 for haptic
5G network transmission delay
20ms
18ms
SA2 focuses on the 5G network transmission delay, the application server/AF can send the request to 5GC to satisfy the required delay between UE and UPF.
  The multi-modal application/AF may request the 5GC with QoS requirements for video (e.g. 20ms) and QoS requirements for haptic (e.g. 18ms) to satisfy the delay difference threshold (e.g. 2ms) without the knowledge of N6 traffic.
SEALDD traffic#1 for video
SEALDD traffic#2 for haptic

## Slide 5: The multi-flow sync for multi-modal application in SA6 (with N6 knowledge)
RAN
UPF
SEALDD client
XR server
XR client
5G CP
N33/N5
UE
SEALDD server
5G network transmission delay
N6
N3
Uu
SEALDD traffic#1 for video
SEALDD traffic#2 for haptic
5G network transmission delay
20ms
18ms
The SEALDD server can obtain the E2E transmission delay including N6 transmission by using the measurements mechanism:
  For example, the E2E transmission delay for video is 22ms, where the 5G network transmission delay and N6 transmission delay are 20ms, and 2ms, respectively. And the E2E transmission for haptic is 19ms. The multi-flow sync is not satisfied due to the delay difference (e.g. 2ms) is exceeded.
Based on the E2E transmission measurement results (with the knowledge of N6 traffic), the SEALDD server can determine/update the QoS requirements to 5GC.
  For example, the SEALDD server can update the QoS requirements (i.e. 5G network transmission delay) for video from 20ms to 19ms. Then the E2E transmission delay for video and audio are 21ms and 19ms, respectively. The multi-flow sync is satisfied due to the delay difference (e.g. 2ms) is not exceeded.
SEALDD traffic#1 for video
SEALDD traffic#2 for haptic
5G network transmission delay
5G network transmission delay
19ms
18ms
N6 transmission delay
N6 transmission delay
SEALDD traffic#1 for video
SEALDD traffic#2 for haptic
2ms
1ms
1. Initial configuration (without N6 knowledge)
3. Configuration update (with N6 knowledge)
2. Running phase
5G network transmission delay
5G network transmission delay
20ms
18ms
N6 transmission delay
N6 transmission delay
2ms
1ms
SEALDD traffic#1 for video
SEALDD traffic#2 for haptic