## Slide 1: Discussion on Updating Location Reporting Configuration
Mythri Hunukumbure, Sivasubramaniam Ramanan
UK Home Office

## Slide 2: Emergency Services Requirement
When an emergency crew is responding to an incident, the authorized client (supervisor) would initially set the location reporting trigger parameters to certain values.
As the incident evolves, the supervisor may want to modify these tiggers, rather than cancelling the current location reporting configuration and issuing a new one.
  A common example is to change the location report update rate, depending on the severity of the incident.
Currently, there is no text in TS 23.280 to clarify how an existing location reporting configuration can be modified/updated.

## Slide 3: Reporting Trigger Modify in TS 23.280
SA1 requirements spec (TS 22.280, section 5.11) states:
[R-5.11-008] The MCX Service shall be able to modify Location information update triggers of an MCX User while the MCX User is on the network.
The current TS 23.280, section 10.9.1 states:
In the information flows of clause 10.9.2, and procedures of clause 10.9.3:
- the term "requesting MC service user" is used to refer to the MC service user which sends a request to subscribe to location information reports, to trigger a location information report or to modify existing location information triggers from another MC service user;
- the term "requested MC service user" is used to refer to the MC service user whose location information is requested or existing location information triggers are to be modified; and
- the term "reporting MC service user" is used to refer to the MC service user which provides location related information based on on-demand request or trigger criteria.
To modify a trigger, the location reporting configuration should be updated. How and where this is done is not clarified in TS 23.280.
  This should be taken up for consideration in SA6 EnhMC.

## Slide 4: Event triggered location reporting
This procedure (10.9.3.1) mentions (in step 1):
1. The location management server sends location reporting configuration message to the location management client(s) containing the initial configuration (or a subsequent update) for reporting the location of the MC service UE. This message can be sent over a unicast bearer to a specific location management client or as a group message over an MBMS bearer to update the location reporting configuration for multiple location management clients at the same time.
NOTE 2: The location reporting configuration information can be made part of the user profile, in which case the sending of the message is not necessary.
NOTE 3: Different location management clients may be given different location reporting criteria.
How a ‘subsequent update’ to the initial configuration can be achieved is not specified here. How a cancellation can be done is specified in the Notes of the Table 10.9.2.1-1.
  Having a Note 4 in TS 23.280 section 10.9.3.1, mentioning the same configuration Table as in 10.9.2.1-1. can be with only the updating parameters, is suggested.

## Slide 5: Stage 3 spec. for configuration updates
TS 24.379, Annex F: XML schema for MCPTT location information
F.3.3 Semantic
The <location-info> element is the root element of the XML document. The <location-info> element contains the <Configuration>, <Request> and <Report> subelements, of which only one can be present.
<Configuration> element has a <ConfigScope> attribute that can assume the values "Full" and "Update". The value "Full" means that the Configuration> element contains the full location configuration which replaces any previous location configuration. The value "Update" means that the location configuration is in addition to any previous location configuration. To remove configuration elements a "Full" configuration is needed.