## Slide 1: Spatial Anchors Enhancement
Michel Roy
InterDigital

## Slide 2: Outline
Spatial Anchor principles
Spatial Anchor limitation
Proposed principle to solve limitation
Summary

## Slide 3: Spatial Anchor Principles
Spatial Anchor: an association between a location and a service
A spatial anchor producer needs to:
  Read the position of a spatial anchor
  Provision the spatial anchor and associated service/metaverse media
A spatial anchor consumer needs to:
  obtains Spatial Anchor metaverse media from the service
  positions the metaverse media at the location
Spatial Anchor Location: GPS coordinates, civic address, etc.

## Slide 4: Spatial Anchor Limitation
GPS coordinates precision is “coarse”
  Lat: 40.123456 – 5th decimal is ~ 1.1m
  Long: 40.123456 – 5th decimal is ~ 1.1m @ equator
  5+ decimal measurement is complex
Some use cases…
  require precise coordinate measurement
  require presence of an object
Lat./long. Is not sufficient

## Slide 5: Proposed principle to solve limitation
AIML model for object recognition (e.g. a class of AIML model)
  Input: an image/video stream
  Output: label(s) & bounding box for recognized objects
  Labels may be used for retrieving metaverse media
  Bounding box may be used to position metaverse media
AIML
Object Recognition
bounding boxes
& labels
Position fetched
MetaverseMedia

## Slide 6: Summary
The following enhancement is proposed:
  Associate an AIML model or AIML model identifier with a Spatial anchor
    Consumer uses AIML model output to assist with Metaverse Media fetching & placement
  Provide an AIML range with the AIML Spatial Anchor
    Indicates the range (e.g., closeness) at which the AIML model can be used
    If the user is far, use the coarse location (e.g., “cheese display”)
    If the user is close, use the AIML model (e.g., “detect available cheese(s)”)
The proposal is detailed in S6-242047