## Slide 1: R19 MC GWUE traffic control
Cuili Ge
Huawei, Hisilicon

## Slide 2: Content
Why traffic control at the MC gateway UE is beneficial ?
How to design the traffic control at the MC gateway UE ?

## Slide 3: Why traffic control at the MC gateway UE is beneficial ?
Benefit of traffic control at the GW UE
  Stop the unauthorized traffic at the MC gateway UE to protect the Uu resource from being wasted.
  The MC gateway UE can be well managed to serve e.g., as many as users based on the MC organization’s different requirements.
  Stop the second usage of MC gateway UE for a single MC service from a device.
Issues - Currently, the MC gateway UE only provide the transparently traffic forwarding without any information of the “traffic”, several issues may occur due to its capability and the Uu resource is limited:
Unauthorized traffic may congest the Uu link of the MC gateway UE which results the MC gateway UE is unable to serve other MC service users. The traffic may be rejected by the MC servers but the UL/DL Uu transmission resource of the gateway UE is wasted.
The MC gateway UE may be congested by big traffic volume (e.g., Video call) from fewer users.
One service from a single device may simultaneously use multiple MC gateway UEs
Uu
Non-3GPP
Uplink traffic (SIP/HTTP message, RTP packet, RTCP packet)
Reject！！
Reject response
Uu
Non-3GPP
Uplink traffic (MCPTT/MCVideo/MCData of user X,Y,Z)
Reject！！
Reject response

## Slide 4: How to design the traffic control at the MC gateway UE ? (1)
New capabilities are needed at the MC gateway UE:
Make the MC gateway UE be aware of the “user” and “traffic” information
Make the MC gateway UE control the “traffic” to be forwarded, rejected/dropped.
New capabilities are needed at the MC service server
Check if the service (MCPTT, MCVideo, MCData) is already using another MC gateway UE
GW-local-X
MC traffic control
1. Before sending service traffic, request the permit of using the gateway UE for certain traffic
New functional entities are needed
GW-local-Y
2. Confirm the user’s certain traffic is allowed to use the gateway UE
3. Be aware of the user, and its allowed traffic (e.g., destination IP and port, 5-tuples
4. Service traffic access control, forward, reject/drop
GW UE control
MC traffic control
GW-local-Y
GW UE control
2. Confirm the user’s certain traffic is allowed to use the gateway UE
3. Be aware of the user, and its allowed traffic (e.g., destination IP and port, 5-tuples
4. Service traffic access control, forward, reject/drop
1. Internal trigger
考虑是否Non-3GPP device上的MC service client自己就不会发起第二条路径。

## Slide 5: How to design the traffic control at the MC gateway UE ? (2)
New procedures are needed.
Non-3GPP device
MC traffic
control
GW UE
IDM
N3GPP link/Conn security
3GPP network
3GPP network security
7. Service authorization with MC service server, Other procedures：affiliation, call
MC
client
Case A - host MC client
3.Identity authentication with IDM, get MC service IDs
MC service server
(MCPTT)
4a. Connection request
(MC service ID of the user)
4b. Connection request <MC service ID of the user, MC service ID of the GW UE>
2. Initial, Only Open for IDM traffic
4c. Check the user is already have a GW for PTT service: Y? or N ?
4d. Connection response
6.Then, open the gate for MC service traffic
IDM
client
1. Identity authentication with IDM, get MC service IDs
New - an ID is needed to identify the MC gateway UE
4e. Connection response
5. Cache the user/traffic for next connection if temporary disconnection occur.

## Slide 6: How to design the traffic control at the MC gateway UE ? (3)
New procedures are needed.
Non-3GPP device
GW conn
control
GW UE
IDM
N3GPP link/Conn security
3GPP network
3GPP network security
IDM client
6. Service authorization with MC service server, Other procedures：affiliation, call
3. Identity authentication with IDM, get MC service IDs, PTT
MC service server
(MCPTT)
4b. Check the user is already have a GW for PTT service: Y? or N ?
4c. OK
MC
client
2.Initial, Only Open for IDM traffic
Get a MC ID of a user ( from the API, or from local configuration, or user input…..
Some triggers occurs, e.g., API (non-SA6) invocation
5.Then, open the gate for MC service traffic of the user
……
Repeat for each ‘gateway user’ (non-3GPP device)
4a. Connection authorization <MC service ID of the user, + MC service ID of the GW UE>
Case B – NOT host MC client
1. Identity authentication with IDM, get MC service IDs, PTT
New- an ID is needed to identify the MC gateway UE

## Slide 7: 明确的建议