## Slide 1: Discussion on common EAS discovery for roaming and federation
Huawei, Hisilicon
Yajie

## Slide 2
Scenario description
Scenario clarification
  For Roaming and federation, several kind of EAS may be deployed in the PLMN/ECSP’ service area
  EAS#1, EAS#2 share the same EASID, however provide service to different PLMN/ECSP’ user
Consider that different PLMN/ECSP’s User can be in same group for certain application service, thus the following issue may happen:
  If only using UE’s serving PLMN information to select the EAS, for UE#1 may connect to the EAS#1, however for UE#2, the EAS#2 may be selected for UE#2
  However, the EAS#2 can be selected for group#1 to avoid the inter-EAS content synchronization if using EAS#2 can provide optimal performance for group#1
PLMN#A
PLMN#B
EES
EAS#2
EAS#1: can only provide service to PLMN#A’s User
EAS#2: can provide service to both PLMN#A and PLMN#B’s User
UE#1 and UE#2 are in the same group
UE#1
UE#2
Group#1
PLMN#B
EAS#1
PLMN#A
UPF
UPF
UPF#1
OPTION#1
OPTION#2
RAN
RAN
Notes: https://aws.amazon.com/ec2/autoscaling/faqs/?nc1=h_ls

## Slide 3
Way Forward
The service provisioning procedure and the EAS discovery procedure should be enhanced:
  The service provisioning procedure should be enhanced with group PLMN/ECSP information, so that the EES determination can be based on EAS allowed PLMN/ECSP information and group PLMN/ECSP information
  Similarly, the EAS discovery procedure should also be enhanced with group PLMN/ECSP information, so that the EAS determination can be based on EAS allowed PLMN/ECSP information and group PLMN/ECSP information
Notes: Observation#1
#2
Way forward

## Slide 4: The end