## Slide 1: Discussion on common EAS determination
Huawei, Hisilicon
Yajie

## Slide 2
Concept clarification: Group connection information
Considering group UEs may connect to multiple EASs, thus the group connection information should reflect each UE’s connection information (e.g. EES, EAS)
  For example, UE#1, UE#2 and UE#3 are in same group, however, UE#1, UE#3 connect to EAS#1 and EES#1, UE#3 connect to the EAS#2, EES#2
  Thus, the group connection information is as following table.
EAS#1
EAS#2
UE#1
EDN#1
EDN#2
EES#1
EES#2
UE#3
UE#2
Group connection info |  | 
UE#1 connection info | EES#1 | EAS#1
UE#2 connection info | EES#1 | EAS#1
UE#3 connection info | EES#2 | EAS#2

## Slide 3
The group connection information should be remained in EES
when UE connect to the T-EAS, T-EES, the rest of UEs in the group should also be aware of the T-EAS, T-EES information, since the rest of UE may also need to relocate to the T-EES and T-EAS.
  For example, the UE#1 relocates to the T-EAS#3, T-EES#3, then the EAS#1, EAS#2, EAS#3 need to synchronize the application content with each other
  However, the UE#2 is in the overlapping area between EDN#2 and EDN#3, the UE#2 can connect to T-EAS#3 if the E2E response time is shorter then UE#2 connect to the EAS#2, in such case only EAS#1 and T-EAS#3 need to synchronize the application content with each other
EAS#1
EAS#2
UE#1
EDN#1
EDN#2
EES#1
EES#2
UE#3
UE#2
UE#1
T-EAS#3
T-EES#3
EDN#3
EAS#1
EAS#2
UE#1
EDN#1
EDN#2
EES#1
EES#2
UE#3
UE#2
UE#1
T-EAS#3
T-EES#3
EDN#3
OPTION#1
OPTION#2

## Slide 4
Way forward
The EES should maintain group connection information
When ACR happen, the UEs in the group should be notified with T-EAS information to determine whether to connect to the T-EAS

## Slide 5: The end