## Slide 1: Architecture Options
Sapan Shah
Samsung

## Slide 2: Contents
Current Architecture Options
Architecture options comparisons
Summary and proposal

## Slide 3: Architecture Options
Solution analysis:
Solution # | Title | Mapping KI # | Architecture Option
1 | Spatial anchor discovery | 1 | Application enablement architecture
2 | Support for spatial anchor management | 1 | Enhancement to SEAL LM
3 | Spatial anchor subscription | 1 | Application enablement architecture
4 | Support for spatial anchor analytics information | 1, 8 | Application enablement architecture
5 | Support for digital avatars | 3 | Enhancement to SEAL CM
6 | Avatar support using Metaverse Digital Representation Block (MDRB) | 3 | Application enablement architecture
7 | Digital avatar support by A-DACM | 3 | A-DACM (A separate server)
8 | Support for spatial map management | 4 | Enhancement to SEAL LM
There are 3 options discussed till now
  To define new application enablement architecture
  To enhance existing enabler server (like SEAL LM, SEAL CM)
  To define new server for the specific management

## Slide 4: Architecture Options - Comparison
Criteria | Meaning | New Application Enabler Architecture | Enhancing existing enabler server | New Server/Function
modularity | architecutre can be divided into separate individual modules per feature | Less (all features are within a single server) | Moderate to High (all features with within different SEAL servers) | High (all features are separate SEAL servers)
scalability | How easy to add or remove resources from the system | High | High | High
security | To authenticate and authorize the access for interface level security | Can be done by 3GPP SA3 | Already in-place | Can be done by 3GPP SA3
usability | User interactions | Easy | Easy | Easy
Cost effective | Cost of development and deployment | High | Low | High
Pros | General | - All metaverse application enablement features can be made available at one server. - Follows client-server architecture model. | - Easy to deploy by adding new feature - Location can be available by the same server - Does not crete a new layer - Follows client-server architecture model | - Does not create new layer - May follow client-server model
Cons | General | - Create a new layer - May need to rely on other servers for more information (like location information from SEAL LM server) | - Metaverse features are on different servers (*) | - Metaverse features are on different servers (*) - May need to rely on other servers for more information (like location information from SEAL LM server)
TS Modification |  | New TS | Existing TS (23.434) | New TS
Reliability is unknown for all architecture options.

## Slide 5: Architecture Options
Other points
  For KI#6 and #7 – existing enabler architecture will be enhanced (either procedure enhancement or architecture enhancement or both)
  Metaverse service can be used by different verticals – like V2X vertical for traffic simulation and automated driving, Gaming industries, Smart home, Health care industries, etc.
Summary
  All architecture options are feasible and deployable
  Considering the comparison and direction towards other KIs, it is suggested to enhance existing SEAL service for Avatar management and define new SEAL server for spatial mapping and spatial anchor management.