## Slide 1: Discussion on Remote Device Control
Mythri Hunukumbure, Sivasubramaniam Ramanan –
UK Home Office

## Slide 2: SA1 Requirements in TS 22.280
6.13.4 Access control
[R-6.13.4-001] The MCX Service shall support suspending or disabling of access from an MCX UE or an MCX User to the MCX Service.
[R-6.13.4-002] An MCX User who has a profile that has been deleted or suspended shall be prevented from using that MCX Service User Profile to access the MCX Service.
[R-6.13.4-003] The MCX Service shall provide a mechanism to temporarily disable an MCX UE remotely by the MCX Service Administrator or an authorized MCX User.
[R-6.13.4-004] The MCX Service shall only allow a user to affiliate to or select an enabled MCX Service Group (i.e., not disabled).
[R-6.13.4-005] A temporarily disabled MCX UE, which has limited access capability per Mission Critical Organization policy, shall be able to be re-enabled by the MCX Service Administrator or an authorized MCX User.

## Slide 3: SA1 Requirements in TS 22.280
[R-6.13.4-006] The MCX Service shall provide a mechanism to re-enable a temporarily disabled MCX UE by the MCX Service Administrator or an authorized MCX User.
[R-6.13.4-007] The MCX Service shall provide a mechanism to permanently disable an MCX UE by the MCX Service Administrator or an authorized MCX User.
[R-6.13.4-008] The permanently disabled MCX UE shall remove all MCX Service User Profiles stored in the MCX UE.
[R-6.13.4-009] The permanently disabled MCX UE shall have no access to MCX Services.
[R-6.13.4-010] The security solution for the MCX Service shall minimize the impact of a compromised MCX UE on other MCX UEs.

## Slide 4: Limitations in current options
It is possible to disable the MC user profile, such that the user cannot use the UE anymore for any MCX service.
  However, this does not allow the [6.13.4-005] requirement, i.e. to allow limited access to services for a temporarily disabled UE.
Temporary or permanent disabling of a device could be done with existing Mobile Device Management (MDM) and EMM solutions.
  This EMM/MDM solution can be operated outside of the MCX system by an administrator. This may not be a 24/7 role in user organisations (UO’s) and can cause delays to execute the access control in the field. Also, different UO’s can have their own EMM/MDM solutions.
  To enable specific services to be active during temporary disabling (eg: Location), these servers (and clients) will have to be exposed to the EMM/MDM solution. This can compromise the end-to-end security that is provisioned through MCX encryption keys.

## Slide 5: Possible Architecture w.r.t. EMM/MDM
EMM/MDM is orchestrated through the OSS/BSS by a system administrator.
Control room interface
OSS/BSS
HTTP Proxy
MCX Servers
SIP core
Core network (EPC/ 5GC) functions
IP Routing Function
EMM/
MDM

## Slide 6: Our proposals
Develop the architectural framework in SA6 to meet the SA1 requirements of access control in TS 22.280, clause 6.13.4.
  How to achieve the two-state disablement (temporary and permanent) of identified MCX UEs?
  What level of limited access (or services) to be allowed in temporary disablement and how to orchestrate this?
To include this topic in the generic enhMC_Ph2 work item for Release 20.
There will be some SA3 security impact and we propose to work closely with SA3 (through LS etc.) in defining this framework.