## Slide 1: Dynamic Generation of AF-Specific UEID
Shahram Mohajeri
AT&T

## Slide 2: Background
23.558 clause 8.6.5 defined “UE Identifier API” which resulted in having SA2 specify “AF specific UE ID retrieval” procedure (23.502 clause 4.15.10) and the associated Nnef_UEId_Get operation
AF specific UE ID is a GPSI in External ID format to protect user’s privacy
UEID (i.e. AF specific UE ID) is defined in 23.558 clause 7.2.6 and is used by external AFs for invoking APIs (via EES or NEF) targeting a given UE

## Slide 3: AF Specific UE ID Retrieval (Stage2 & Stage3)
Stage2- “AF specific UE ID retrieval” procedure in 23.502 clause 4.15.10, step 10 doesn’t specify the case where UDM may not be able to find the AF specific UE ID
  Step 10.“The UDM responds to the NEF with an AF specific UE Identifier represented as an External Identifier for the UE which is uniquely associated with the Application Port ID, MTC Provider Information or AF Identifier
Stage3- 29.522 (clause 4.4.32.2) “Retrieve AF specific UE ID service operation” however states that UDM would reply to NEF with a "404 Not Found" error status code
  “If the UDM indicates that the requested UE Identifier is not available in the subscription data, the NEF shall respond to the AF with a "404 Not Found" error status code.”
23.502- Figure 4.15.10-1: AF specific UE ID retrieval

## Slide 4: Problem Statement
Stage2 doesn’t specify how “AF Specific UEIDs” are created and stored in the subscriber’s record in UDM/UDR
Lack of clarity in Stage2 spec, may lead one to assume that the subscription data in UDR are expected to be preloaded with “AF Specific UEIDs”
  For an MNO with over 100 million subscribers and say 200 AFs, bulk-load doesn’t make sense as not every subscriber is going to use every AF’s service…waste of resources
  Additionally, new AFs are onboarded and new subscribers are added on ongoing basis, keep running bulk-load process is not practical
  There are use cases where the user may wish renewal of the “AF Specific UEIDs”, hence enabling “forget me” feature upon the next visit to the AF service
Leaving it unspecified, doesn’t help the industry which needs a consistent and reliable method of retrieving such an opaque UEID which on one hand avoids user privacy issues (vs MSISDN) and on the other can reliably be used by the AF to identify the UE across PDU sessions (vs UE IP address which changes)
  App developers need a consistent behavior from NEF APIs across MNOs. Hence, leaving it unspecified leads to inconsistency in NEF API implementations and in turn diminishes the AF Specific UEID’s usefulness
Bottom line: The nature of “AF Specific UEIDs” availability is dynamic and currently a mechanism enabling its creation dynamically is missing from stage2 spec.

## Slide 5: Needed Enhancement
Given the importance the “AF Specific UEID” for AF’s invocation of NEF northbound APIs, there needs to be an enhancement to the existing stage2 “AF specific UE ID retrieval” procedure (23.502) whereby in the absence of the “AF Specific UEIDs” in the subscription data (upon UDM query), an “AF Specific UEIDs” is created dynamically, stored in subscription data and returned to the NEF in reply to the Nnef_UEId_Get operation.
  Note : Avoiding UDM return “404 Not Found" increases the success rate of NEF northbound API usage by AFs which rely on “AF Specific UEID”

## Slide 6: Way Forward Proposal
Send an LS to SA2 (CC CT3) and ask for an enhancement to the “AF specific UE ID retrieval” procedure
A draft LS is proposed in S6-250070