## Slide 1: Discussion Paper on SID proposal of application enablement for Ambient IoT services
CATT

## Slide 2: Outline
Background
SID proposal

## Slide 3
SA1(TS 22.369) has identified the functional service requirements of Ambient IoT and includes 6 aspects:
  Communication;
  Positioning/location;
  Management;
  Collected information and network capability exposure;
  Charging;
  Security and privacy
Potential SA6 work based on above SA1 functional service requirements：
  Communication: The 5G system shall provide suitable mechanisms to support communication between a trusted and authorized 3rd party and an Ambient IoT device or group of Ambient devices.
  Management: The 5G network shall support suitable management (e.g. enable, disable, permanently disable) mechanisms for an Ambient IoT device or a group of Ambient IoT devices.
  Collected information and network capability exposure:
    Subject to user consent, operator policy and 3rd party request, the 5G system shall be able to obtain data from Ambient IoT devices (e.g. sensor data) and provide it to a trusted 3rd party via the 5G network.
    Subject to user consent, operator’s policy and 3rd party request, the 5G system shall provide information about an Ambient IoT device or a group of Ambient IoT devices (e.g. position) to the trusted 3rd party via the 5G network.
    The 5G system shall enable an authorized 3rd party to instruct the 5G network to trigger a group of Ambient IoT devices in an specific area and which action the Ambient IoT devices need to perform when triggered (e.g. send ID, receive further information, send measurement value).
Potential SA6 work based on SA1 requirements
Notes: 周期管理、数据采集、不同组管理及操作、复杂任务的管理、签约归属权的转移、终端区域数量TR 22840：
    [PR 5.3.6-003] The 5G system shall support a mechanism to interface a 3rd party application to manage and operate on the Ambient IoT devices.
    [PR 5.29.6-1] Based on operator policy, the 5G system shall provide means for a trusted third party to request the permanent disabling of an Ambient IoT device to communicate with the 5G system.
    [PR 5.29.6-2] Based on operator policy, the 5G system shall provide means for a trusted third party to request the deletion of any digitally stored information of an Ambient IoT device.
    [PR.5.27-003] The 5G network shall be able to trigger Ambient IoT devices. The 5G system shall enable an authorized 3rd party to instruct the 5G network in which area, which group of Ambient IoT devices needs to be triggered and which action the Ambient IoT devices need to perform when triggered (e.g. send ID, receive further information, send measurement value).
    [P.R.5.1.6-002] The 5G system shall support to provide collected information from Ambient IoT devices to the trusted 3rd party.
    [PR.5.21.6-004] The 5G system shall be able to expose the identities and relative positioning results of Ambient IoT devices to a trusted third party. The 5G system shall be able to provide a mechanism to expose the information collected from an Ambient-IoT device to a trusted 3rd party.
    NOTE: The request from 3rd party can include the requested Ambient IoT device identity, the requested service area to find the Ambient IoT device, the requested information of an Ambient IoT device includes position information.
    [P.R.5.12.6-003] The 5G system shall be able to provide information of a specific Ambient IoT device to the trusted 3rd party.
    [P.R 5.13.6-005] The 5G system shall support transferring data collected from Ambient IoT devices to a trusted 3rd party.
    [PR.5.20.6-001] The 5G system shall support communication with Ambient IoT device with 3rd party application server.
    [PR 5.22.6-2] The 5G system shall provide a mechanism for a 3rd party application to write user data to and to read user data from an Ambient IoT device.

## Slide 4
SA2 (TR 23.700-13) has studied the following key issues of Ambient IoT and summarized some conclusions.
  KI#1: Architecture support of Ambient IoT Devices;
    Topology 1 and Topology 2
  KI#2: Identification, Subscription, Registration and Connection management;
    Identifier and Identification Management
  KI#3: Support of Ambient IoT Services
    Ambient IoT services supported: Inventory, Read, Write, Disable (permanently in Rel-19)
    NEF exposure: New NEF services to support the above AIoT services will be defined.
    Information provided by the AF: AIoT service type, Information for AIoT reader selection, Information about the target AIoT device(s) or Information to be used for resource allocation
Potential SA6 work based on SA2 TR/TS conclusion
The WID for Ambient IoT in SA2 in Rel-19 has been endorsed and the normative work is ongoing：
  The work item is focusing on Device 1 in Topology 1 and the architecture supports Device 1 in Topology 1
  The WT#1,#2,#3 related to KI#1,#2,#3 will be specified in the TS
Potential SA6 work based on above SA2 TR/TS conclusions：
  The WT#3 Ambient IoT Service enabler for Inventory and Command is related to SA6 work, especially for:
    Exposure for AIoT services to AF
    Information provided by the AF
Notes: And some potential SA6 work based on SA2 related normative work is as follows:
Exposure for AIoT services to AF: How AF utilizes the exposure of AIoT device information and exposes to the application server;
Information provided by the AF: AIoT service type, Information for AIoT reader selection, Information about the target AIoT device(s) or Information to be used for resource allocation.

## Slide 5
SA2 may study the following work tasks of Ambient IoT since Rel-20 (captured from SP-241972).
  Key Work Tasks include defining:
    WT#1 Ambient IoT device and reader association.
    WT#2 Architecture to support Ambient IoT device reachability and communication in roaming scenarios.
    WT#3 Architecture to support AIoT device management C2 and configuration.
    WT#4 Architecture to support AIoT device positioning.
    WT#5 Support Ambient IoT services based on energy availability.
  Key Work Tasks include defining:
    The work postponed from R19, including the support of Topology2.
  Potential 5GA features:
    Outdoor scenarios supporting of Ambient IoT service
    DO-A supporting, e.g. access and mobility management of Device 2b.
    Architecture and procedures enhancement to support topology 3 and 4.
    Density control of the AIoT service
SA2 petechial work tasks in Rel-20
The SA6 work of Ambient IoT in Rel-20 should consider the work tasks of Rel-20 SA2 when its scope is available.
Notes: And some potential SA6 work based on SA2 related normative work is as follows:
Exposure for AIoT services to AF: How AF utilizes the exposure of AIoT device information and exposes to the application server;
Information provided by the AF: AIoT service type, Information for AIoT reader selection, Information about the target AIoT device(s) or Information to be used for resource allocation.

## Slide 6: Outline
Background
SID proposal

## Slide 7: SA6 Rel-20 5GA Proposal Overview: Application enablement for Ambient IoT services
Background/Motivation
  New requirements from SA1 (TS 22.369) including overview of Ambient IoT service, functional service requirements, Performance service requirements, etc.
  Architecture definition and Exposure information from SA2 (TR 23.700-13).
<<SI+WI or WI>>
  SI+WI
<<Continuation or New topic>>
  New topic
Objectives
  Management for AIoT devices
  Support of the AIoT services
  Expose the collected information of Ambient IoT devices
TUs required
  SID: 5 WID: 4
Dependency on other WGs
  SA2

## Slide 8: Detailed 5GA Proposal Objectives: Application enablement for AIoT services
Study Scope:
  align with the scope of Rel-19 SA2 AIoT WI and also consider the objectives of Rel-20 SA2 AIoT SI
    Topology: Topology 1(Rel-19); Topology 2(Rel-20)
    Device type: Type 1(Rel-19); Type 2a and 2b(Rel-20)
    Traffic type: DT and DO-DTT(Rel-19); DO-A(Rel-20)
    Use case: Inventory and Command (Rel-19); Location and Sensor data reporting(Rel-20)
      Management for AIoT devices
  Study how the AIoT enabler managers the identifier for AIoT devices (e.g. associate the device ID with reader ID).
      Support of the AIoT services
  Study how the AIoT enabler support the VAL server’s requests (e.g. inventory, command) for the AIoT devices
  Study how the AIoT enabler discovers the related reader and obtains the AIoT devices related information as requested.
  Study how the AIoT enabler provisioning the configuration for the e.g. inventory, command operations.
      Expose the collected information of Ambient IoT devices
  Analyze and manage the AIoT device Data (e.g. classification, duplication removal, aggregation, format unification)
  Expose the value-added AIoT devices information to the consumer (e.g. VAL server).
      NOTE: The SA6 AIoT SI will start based on the scope of Rel-19 SA2 AIoT WI first, and may update the objectives after the Rel-20 SA2 AIoT SI is ready.