MCC Task Force 160

Description and Terms of Reference for 2012

# 1.	Background

1.1   The MCC TF160 was setup in June 2000 and is currently under the responsibility of 3GPP TSG-RAN WG5 (RAN5) for the development, maintenance and deliveries of TTCN test cases. Following a decision at PCG#17 MCC TF160 became the 3GPP TTCN expertise pool for both TSG RAN and TSG GERAN. The task force (TF) consists of the skilled protocol / TTCN experts coming from various companies of the 3GPP partners. Nearly 1200 TTCN test cases in UTRA FDD and LCR TDD, and 600 E-UTRA (LTE) FDD and TDD test cases have been verified and approved for UE conformance testing and certification purposes.

1.2   The funding of an expert team as a task force at the MCC has proved to be the most efficient and cost-effective way to develop the test specifications found in TS 34.123-3, 34.229-3, 36.523-3, 37.571-4 and 51.010-5. In order to stabilise and to maintain all the currently available TTCN Abstract Test Suites (ATS) and to continue developing new TTCN test cases for the different 3GPP Releases, MCC TF160 has been resourced, in part, by the PCG/OP. 58 man months (mm) have been allocated at OP#26 in Oct 2011, to cover the RAN 2012 task requirement list. Voluntary funding of 39 mm will also be sought from various external organisations as well as individual companies, in the form of both manpower and cash. Responsibility for ensuring that the TF is resourced to meet the test development requirements rests jointly with RAN and GERAN.

1.3   MCC TF160 continues to work in accordance with the priorities identified by the Global Certification Forum (GCF) but increasingly it is fulfilling requirements set by the TD-SCDMA Industry Alliance (TDIA),  the PCS Testing Certification Review Board (PTCRB) and the Global TD-LTE Initiative (GTI) .

1.4   To meet the HSPA market demand for a number of Rel-8 / Rel-9 features, LCR TDD enhanced FACH, multi-freq / multi-band, IMS emergency call and VoLTE test, UTRA FDD enhanced HNB mobility, SSAC, DC-HSUPA and MIMO / non MIMO coexistence, MDT, etc. among others, have been introduced. The conformance tests for these have been or are being specified in prose at RAN5, and it is necessary to implement these in TTCN, as the reference test specification, for UE conformance certification purposes.

1.5    The target and schedule of the LTE conformance test is, as ever, very demanding. MCC TF160 will provide all the prioritised LTE/SAE TTCN3 test cases in Rel-8 and later Releases for the certification of the evolved UE, as well as the support of emergency call over LTE, LTE MBMS, PWS, LTE MDT and LTE positioning tests.

1.6      With the introduction of LTE/SAE, a seamless inter-system HO of the evolved UE between GERAN - evolved UTRAN is needed. MCC TF160 will continue to develop the corresponding ATS for GERAN.

# 2.     Consequences if not resourced

All test cases produced by MCC TF160 are used to prepare UE and evolved UE for worldwide roaming and interoperability within 3GPP networks. Without such tests the UE and evolved UE interoperability cannot be guaranteed. Should MCC TF160 be discontinued, then the cohesive and unified approach to develop common TTCN modules will be lost. The system simulator manufacturers will inevitably deliver test platforms with different interpretations of the core specifications which will, in turn, lead to variable results and general confusion as to what constitutes a conformant handset. Furthermore the broader implementation of 3GPP networks could be delayed as potential issues, such as interoperability of handsets, may not resolved.

# 3.     Detailed description

3.1     Subject title: 3GPP TTCN specifications for UE and evolved UE of different Releases

3.2     Reference Technical Body: 3GPP TSG RAN WG5, TSG GERAN WG3

3.3    Other interested Technical Bodies: 3GPP TSG RAN WG 2, TSG CT WG 1,TSG GERAN WG 2

3.4     Target dates for the start of work: Jan 2012

3.5     Target dates for the conclusion of the work: Dec 2012

3.6     Resource requirement

3.6.1  Estimated man month requirement in 2012

It was estimated that the resource requirement, in terms of TTCN experts, for 2012 will be 97 man months. A review of the funding requirement for 2012 was undertaken by RAN5 in Aug 2012 and later endorsed by TSG RAN.

3.6.2  Additional tasks requiring resources

In addition to the TTCN development ETSI needs to host MCC TF160, as well as provide the task force’s overall leadership, management, logistical and IT support.

3.6.3  Qualification required, mix of skills

The experts should have deep 3GPP protocol knowledge at the Uu, LTE-Uu, Um or Gm reference points and good skills for writing TTCN test cases to cover FDD, LCR TDD as appropriate.

  - Release and Configuration Manager (RCM)

In Jan 04, the RCM was appointed with specific duties to control the release of TTCN ATS (in TTCN2 or TTCN3) as well as coordinate the verification activity between the test industry (verification teams) and MCC TF160. The continuation of the RCM in 2012 is to provide great benefits to the test industry and now the RCM is an integral part of MCC TF160. Furthermore, LCR TDD verification has been started. The RCM task is shared by FDD and TDD test industries.

  - Scope of Terms of Reference

3.8.1 The technical areas of MCC TF160 cover the conformance test specifications for UE signalling, protocols and radio access bearer interoperability in FDD and TDD radio technologies in UTRA and E-UTRA. The UE handover and interoperability between E-UTRA and UTRA, GERAN or non-3GPP technologies also belongs to the area.

3.8.2  The task force is responsible for the development, maintenance and deliveries of NAS, SMS, RRC, MAC, RLC, RAB, PDCP, A-GPS, AGNSS, HSPA /HSPA+, IMS-CC, MTSI, interRAT HO, as well as LTE/SAE and LTE positioning test suites in the different Releases according to the relevant 3GPP prose test specifications. For the purposes of enabling GCF/PTCRB certification of handsets, priority is given to the completion and maintenance of the high priority test cases.

3.8.3   The task force is also responsible to implement the prose and TTCN CRs in TTCN, to integrate the verified TTCN test cases into the existing ATS and to deliver the 3GPP formally approved ATS releases and interim working ATS releases.

3.8.4   MCC TF160 consists of three teams; a UTRA FDD team, a LCR TDD team and an LTE/SAE team. The FDD team concentrates on the FDD Abstract Test Suite (ATS) for R99, and the later releases. The LCR TDD team concentrates on the LCR TDD ATS for Rel-4 and the later releases. The LTE/SAE team contributes to the LTE/SAE test suites in Rel-8 and the later Releases. The split of ATS according to the access technologies of FDD and TDD will continue for UTRA HSPA test. However, the LTE/SAE test suites will be shared by the technologies of FDD and TDD.

3.8.5   MCC TF160 will provide assistance to those parties interested in developing HCR/VHCR TDD on the condition that there are no resource implications to that approved by PCG.

  - Context of the tasks in relation to TS 34.123, TS 34.229, TS 36.523, TS 37.571 and TS 51.010

    - Part One. The first part of TS 34.123, TS 34.229, TS 36.523 and TS 51.010, as well as TS 37.571-2 specifies the test structure, test purposes and give each test case a prose description.

3.9.2    Part Two. The second part specifies necessary ICS questions for UE manufacturers on the UE 
           capabilities and the test case applicability.

3.9.3   TTCN Parts (34.123-3, 34.229-3, 36.523-3, 37.571-4 and 51.010-5). These parts contain the test suites themselves and are considered as 3GPP formal test specifications; they are among the formal deliveries of MCC TF160.

  - Related activity in other bodies and necessary co-ordination of schedules

Changes on interRAT test in TS 34.123, TS 36.523 of RAN5 or TS 51.010 of GERAN 3 can have interactive impact. The stability of the relevant core specifications of CT1, RAN2 and GERAN2, as well as backwards compatibility between the Releases, will have an impact on the progress of the Task.

3.11   Base documents used

TS 24.008: Mobile radio interface layer 3 specification, Core Network Protocols - Stage 3

TS 24.229: IMS CC protocol based on SIP and SDP - Stage 3

TS 24.301: NAS protocol for EPS - Stage 3

TS 25.321: MAC protocol specification

TS 25.322: RLC protocol specification

TS 25.331: RRC protocol specification

TS 25.346: Introduction of MBMS in the Radio Access Network (RAN)

TS 36.321: E-UTRA MAC protocol specification

TS 36.322: E-UTRA RLC protocol specification

TS 36.323: E-UTRA PDCP specification

TS 36.331: E-UTRA RRC protocol specification

TS 34.108: Common test environment for UE conformance testing

TS 34.123-1: UE conformance specification, part 1: protocol conformance specification

TS 34.123-2: UE conformance specification, part 2: ICS Proforma specification

TS 51.010-1: Mobile station conformance specification, part 1: protocol conformance specification

TS 51.010-2: Mobile station conformance specification, part 2: ICS Proforma specification

TS 34.229-1: IMS CC UE conformance specification part 1: protocol conformance specification

TS 34.229-2: IMS CC UE conformance specification, part 2: ICS Proforma specification

TS 36.508: Common test environment for evolved UE conformance testing

TS 36.523-1: UE conformance specification, part 1: protocol conformance specification

TS 36.523-2: UE conformance specification, part 2: ICS Proforma specification

TS 37.571-2: E-UTRA and EPC UE conformance specification for UE positioning; Part 2: Protocol conformance

TS 37.571-3: E-UTRA and EPC UE conformance specification for UE positioning; Part 3: ICS

3.12   Relevant RAN and GERAN Work items

RAN WIs:

All TEIx_Test, LTE-UEConTest_SIG, , LCS_LTE_UEConTest, EHNB-LTE-UEConTest, SSAC-UEConTest, MBMS_LTE-UEConTest, MDT_UMTSLTE-UEConTest, LTE_PWS-UEConTest, MIMO_HSDPA-UEConTest,  IMS_EMER_GPRS_EPS_UEConTest, LCRTDD_MB_MF_UEConTest, EHNB-UTRA_FDD_UEConTest,  RANimp-MultiBand_DC_HSDPA-UEConTest, RANimp-DC_HSUPA-UEConTest, ANR_UTRAN-UEConTest,

GERAN WIs: All TEIx,

3.13   Expected Output

TS 34.123-3: UTRA UE conformance specification, part 3: Abstract Test Suite (ATS)

TS 51.010-5: GERAN Mobile station conformance specification, part 5: Abstract Test Suite (ATS)

TS 34.229-3: IMS CC UE conformance specification, part 3: Abstract Test Suite (ATS)

TS 36.523-3: E-UTRA UE conformance specification, part 3: Test Suites

TS 37.571-4: E-UTRA and EPC UE conformance specification for UE positioning; Part 4: Test Suites

In addition, the outputs will be in the form of Abstract Test Suites (ATS) and will be delivered in accordance with the RAN5 and GERAN3 approved programme. In essence, MCC TF160 will deliver 4 formal releases (at quarterly intervals) of the ATS containing those test cases which have been verified according to R5 PRD-12. In between these releases, MCC TF160 will deliver a series of RAN5 and GERAN3 interim working documents that contain the entire suite of test cases i.e. including those that have yet to be verified. This enables the test industry to verify the outstanding test cases within the framework of the extant working ATS.