## Slide 1: LTE – Rel-12 and Beyond
Considerations for LTE Enhancements and Evolution

## Slide 2: Background
Smartphones and tablets are driving increased mobile usage
Mobile adoption of the internet is still in early stages
In Next 5 years:
  10x Mobile data traffic increase
  Video (rich multimedia) will drive increase
  1 billion  5 billion mobile broadband subscriptions – but M2M also growing
Subscribers will expect to pay less even with longer battery life and faster/more services

## Slide 3: Rel-10 + Rel-11  Rel-12
Rel-10 addressed some core requirements in terms of cell edge throughput, capacity improvements, small cell support
  Carrier Aggregation
  CoMP
  MIMO (Two component codebooks, TM9 – MU-MIMO, 8x8 DL, 4x4 UL)
  eICIC
But challenges remain
  Cell edge performance
  Backhaul
  Support for proliferation of Machine to Machine communication
  Spectrum availability
  Continued need for increased capacity while constrained in spectrum availability
Current Rel-11 WIs and SIs are addressing some of these challenges
  Need for continued progress in these topics

## Slide 4: Rel-12 Issues
  Lower overhead
    E.g. reduced CRS and SIB transmissions
  Improved small packet transaction handling
    For both MTC & non-MTC
  Link Enhancements
    Advanced Receivers, enhanced MIMO, …
  Small Cell support/integration
    Evolve cell coordination techniques
    Unlicensed spectrum use
Latency, Power
  Application aware RRM (less power usage)
    Includes enhanced sleep modes
  Address overall energy usage across system (e.g. green TP)
  On demand connection (low overhead/fast)
Improved Spectral Efficiency & Lower Cost per bit

## Slide 5: Rel-12 Issues
New opportunities
  Tighter integration with other RATs (WiFi offloading, handovers, …)
    WiFi-LTE simultaneous transmission
    WiFi replacement long term ?
  Cognitive (LTE) Radio (e.g. with TVWS spectrum)
  Adhoc (D2D e.g.) and M2M/MTC services/support

## Slide 6: Link Enhancement Considerations
256 QAM – Higher Order Modulation (M=8)
  Unicast Downlink and Wireless Backhaul
  EVM consideration e.g. DL (eNB Tx, UE Rx)
    R=3/4, M=8 SNR ~ 22 dB
Further Enhanced MIMO
  Improved 4xn code book with dual structure
Control Channel soft combining across TTIs
  MTC control channel coverage with reduced
  bandwidth, e.g.
Dynamic TDD UL/DL configuration
  e.g. Indoor (femto) cell
Advanced Receivers (e.g. MMSE-IRC)
Enhanced CoMP with enhanced feedback
  Further improved cell edge throughput

## Slide 7: Spectrum
Spectrum availability continues to be a challenge
  Multi-mode carrier aggregation could be useful in some deployments where operators have access to TDD spectrum
  Not all spectrum is being used all the time
    Opportunistic use of spectrum is desirable
      TV white space, unlicensed spectrum used for WiFi
      Might be useful to consider cognitive radio approaches combined with aggregation (LTE + WiFi or LTE + LTE over unlicensed) and offloading techniques to increase throughput
  Potential opportunity with 3.5 GHz TDD

## Slide 8: Efficient Transactions
Small Data transmissions
  Increased data usage is fuelled by both increased streaming traffic as well as large amounts of small data transactions
  Need to address
    Better signaling techniques for radio resource allocation
      SPS enhancements, Efficient CCHs for small packets

## Slide 9: Machine Type Communications
Significant attention being given to MTC in various forums
  Focus is primarily on the higher level systems aspects
  3GPP should focus on making MTC more efficient from a radio perspective
Low cost devices
  Work is ongoing in RAN WG1
    Work should enable: Smaller, power efficient, low cost devices
      But maintain network efficiency (backwards compatibility, spectral efficiency, coverage)
    Lower Peak Rate, Single RAT, Single Carrier, BW reduction if necessary, Reduced Tx power
More work is needed on:
  Group based MTC
  Future-proof design (e.g. delay sensitive MTC)
  Improved small transaction handling (leverage work for non-MTC devices)

## Slide 10: New Carrier Types
Current status for New Carrier Type
  Non-backwards compatible and legacy(Rel8/9/10) portions mapped to different carriers or carrier segments
    Non-backwards compatible portion used for enhanced PHY scheduling (smaller pilot overhead, beam-formed control using ePDCCH)
Potential Options for Rel-12 and beyond
  Standalone carrier with no legacy portion – legacy UE penalty
    Incremental performance gain compared to Rel10 does not justify the penalty
      Gains should be similar to those seen for UMTS vs. LTE, otherwise unlikely to be deployed
    Focus should be on small cell operation only
      No need to meet all requirements of TR 25.913
      Allows greater design flexibility and hence more potential for significant gains

## Slide 11: AdHoc Networks
Small Cells enable increased capacity
  But also add complexity
    Backhaul
      Relays, Wireless backhaul
    Increased Handovers
beneficial to consider proximal communications, other approaches

## Slide 12: AdHoc Networks – potential candidates
Device-to-device communications
  Work already underway in SA WG1 to address use cases
    Some potential use cases are public safety and proximity based communications
  RAN will need to address
    Range for device-to-device (potential advantage over WiFi)
    Support of discovery
    Interference management
    Radio Resource Allocation
  Overall benefit is dependent on percentage of traffic that is proximal
  (< 500m)
Other Approaches
  Support of Mesh topologies

## Slide 13: Potential MIMO Enhancements
DL MIMO Enhancements
  Enhancements for improved single transmission point (single-TP) MIMO performance with new deployment scenarios
    Geographically separated (non-quasi collocated) antenna deployments with power imbalance
    Closely- and widely-spaced cross-polarized antenna configurations
    Different antenna configurations for macro and small cells
  CSI feedback enhancements
    4-Tx codebook enhancements (e.g., dual codebook, SVD bound) with finer spatial domain granularity
    Finer granularity sub-band CQI and sub-band PMI feedback
    MU-MIMO CSI feedback enhancements
  Vertical beam-forming (steerable antenna down-tilt)
    Codebook enhancements possible for 2D planar array of cross-polarized elements
UL MIMO Enhancements
  Multi-antenna transmission enhancements for new deployment scenarios
    Heterogeneous network deployments with low-power nodes
    Geographically separated (non-quasi collocated) antenna deployments
  Improved robustness to implementation issues with real-world UE multi-antenna designs
    Relative phase discontinuity between transmit antennas
    Antenna gain imbalance
    MIMO schemes with relaxed RF requirements
  Open-loop (channel-independent) uplink MIMO transmission schemes
    Robustness for higher mobility scenarios
  MIMO transmission for uplink control information
    Efficient transmission of higher control payload to support DL CoMP/CA feedback

## Slide 14: Potential CoMP Enhancements
DL Coordinated Multipoint (CoMP)
  CSI feedback enhancements with non-quasi collocated antenna ports
    Accommodate power imbalance and phase differences
    Aggregated feedback across multiple CSI-RS resources
    Inter-CSI-RS-resource phase indicator feedback
  Mobility enhancements with CoMP
UL CoMP Enhancements
  Uplink power control enhancements for PUSCH/PUCCH/SRS
    CSI-RS based path loss estimation, increased parameter range
  Sounding RS enhancements
    Aperiodic SRS and frequency hopping
    Non-precoded SRS
  PUSCH/PUCCH/SRS sequence enhancements

## Slide 15: Advanced Antenna Technology
Electronically Steerable Down-tilt Antennas
  Minimize intra and inter-cell interference
  Down-tilt can be adjusted to a single UE or a group of UEs
  Elevation determination based on either UE feedback or angle of arrival (AOA) of uplink signals
  However, array calibration may be required in active antenna systems and RF and EMC Requirements can be challenging
  Worthwhile to evaluate expected performance gains
    Related areas to address
      Codebook design
      Control signaling
      UE feedback
      eNB RF requirements

## Slide 16: Summary
3GPP RAN should continue work that has been partly addressed earlier
  Improved Latency and energy usage
  MTC support
  MIMO and CoMP
Significant benefit can accrue from focusing on ways to improve support for small data transactions
New Carrier Types
  Support for standalone new carriers focusing only on small cells
AdHoc network Investigation
  Simple approaches for device-to-device communications
Tighter integration with other RATs
LTE over un-licensed spectrum