## Slide 1: A look at the requirements for LTE in the Unlicensed Bands
June 13, 2014
RWS-140006
Sophia Antipolis, France

## Slide 2: Introduction
LTE in the unlicensed band has the possibility to greatly complement the services provided by LTE.
Since this will be deployed in various unlicensed band/sub-bands and in different regions, we believe that there is a need to agree on a single set of coexistence requirements and methodology to inter-operate in shared unlicensed spectrum.
We expect the initial focus to be on prioritized targeted sub-bands, however we should ensure that LTE-U design is forward compatible so further extensions only require additional RAN4 spectrum related discussions (similar to existing process).

## Slide 3: Coexistence ISSUES

## Slide 4: Unlicensed spectrum under consideration
  Focus on new additions to 5GHz band: middle (5.4GHz) or upper (5.8GHz)
  New additions have lesser restrictions, and at this time are less crowded
  Useable for both outdoor/Indoor deployments
  Better path loss than 60GHz band
5GHz regulations are very fragmented
  Significant geographical regulations differences exist within each sub-band.
  For example, 5.725 to 5.875 GHz preferred, but not available in Japan.
FCC Revision of Part 15 for Operation of Devices in 5GHz, NPRM, April 2014

## Slide 5: Highly Fragmented Regulatory Requirements Across the Regions in 5GHz Spectrum
 | US1 | Europe2 | Japan | China | Korea
5.15GHz-5.25GHz (100MHz) | Indoor/Outdoor(U-NII-1) | Indoor (Band A) | Indoor/Satellite | Indoor/DFS/TPC | Indoor
5.25GHz-5.35GHz (100 MHz) | DFS/TPC (U-NII-2A) | ACA/DFS/TPC (Band A) | Indoor/DFS/TPC | Indoor/DFS/TPC | DFS/TPC
5.35GHz-5.470GHz (120 MHz) | (U-NII-2B) | under study | No | under study | under study
5.470GHz-5.650GHz (180 MHz) | DFS/TPC(UNII-2C) | ACA/DFS/TPC (Band B) | DFS/TPC | In consideration | DFS/TPC
5.650GHz-5.725GHz (75 MHz) | DFS/TPC/RADAR (UNII-2C) | ACA/DFS/TPC (Band B) | DFS/TPC | In consideration | Bcast Relay Service
5.725GHz-5.825GHz (100MHz) | Yes (UNII-3) | DFS/RADAR (Band C) | No | Licensed (3 operators) | EIRP 10 mW, Center Freq 5.775GHz (allocated for WDCS)
5.825GHz - 5.850GHz (25MHz) | Yes (UNII-3) | DFS/RADAR (Band C) | No | Yes | Under Study
5.850GHz - 5.875GHz (25MHz) | UNII-4 | RADAR (Band C) | No | under study | under study
5.875GHz-5.925GHz (75MHz) | U-NII-4 | under study | No | under study | under study
Under discussion
1 FCC Revision of Part 15 for Operation of Devices in 5GHz, NPRM, April 2014
2 ETSI BRAN

## Slide 6: Example Regulatory Requirements (1 of 2)
Transmit Power Control (TPC) requirements – US (FCC)
  TPC feature adjusts a transmitter’s output power based on the signal level present at the receiver. As the signal level at the receiver rises or falls, the transmit power will decrease or increase as needed1.
Dynamic Frequency Selection (DFS) – US (FCC)
  Detects the presence of radar signals and dynamically guides a transmitter to switch to another channel whenever a particular condition (indicating a conflict with an active radar operation) is met. Prior to the start of any transmission, a U-NII device equipped with DFS capability must continually monitor the radio1.
1 FCC Revision of Part 15 for Operation of Devices in 5GHz, NPRM, April 2014

## Slide 7: Example Regulatory Requirements (2 of 2)
Automatic Channel Access – Europe
  ETSI BRAN 301 893: Before starting transmissions, the equipment will perform Clear Channel Assessment (CCA) …not less than 20usecs…Channel is considered occupied if energy level exceeds threshold. If channel is free, the Channel Occupancy Time shall be in the range 1 ms to 10 ms and minimum Idle Period shall be at least 5% of Channel Occupancy Time.
=> There is a need to determine “greatest common denominator” of all regulatory requirements for a particular sub-band

## Slide 8: Coexistence with IEEE 802
The discussion in RAN on LTE in Unlicensed has generated discussion in IEEE 802 and the Wi-Fi Alliance.
  802.19 (Wireless Coexistence Technical Advisory Group) has had discussions on how LTE in the unlicensed band would effect coexistence for 802 protocols and Bluetooth.
  A good deal of offline discussion around the meetings about a more formal response involving regulatory issues, but most are waiting to see what 3GPP proposes.
  We anticipate an effort to put 802.11 in the newly freed-up 5.8GHz, so probably putting LTE in any feasible part of 5 GHz will need to coexist with 802.
    802 enjoys significant penetration and social/political support
=> Wireless access fairness will need to be supported between LTE-U and 802 radio access technologies

## Slide 9: Examples of Issues with Coexistence with 802
Operation in shared spectrum requires solutions to coexistence problems in presence of unpredictable deployments (example: hidden node problem).
802.11 has much more relaxed ACLR requirements than LTE so an 802.11 STA near a LTE UE may cause RF receiver issues, in contrast to two LTE UEs near each other.
Classic Hidden node problem in Unlicensed Spectrum
LTE receiver de-sensing due to 802.11 STA transmission

## Slide 10: Coexistence Issues with Licensed Bands
RAN4 needs clear directions for the bands combinations and supported channel bandwidths in order to study the Harmonics and IMD products RF impact.
There are likely more in-device co-existence issues and thus we will probably have similar discussion as previous in-device coexistence work.
=> Coexistence with existing licensed bands will need to be studied and resolved.

## Slide 11: Questions that need Answers ASAP

## Slide 12: Which Bands/Sub Bands?
When we design a solution for unlicensed bands it should be robust enough to be applicable to a wide range of potential spectrum within each region.
Therefore we need clear guideline from the operators on which bands/sub-bands are targeted for LTE unlicensed band, to come up with a coexistence framework that is robust.
=> We need to have an understanding of which bands the LTE Unlicensed solution needs to apply in order to properly scope the work

## Slide 13: What does coexistence and fairness with Wi-Fi Mean?
When there are 802 devices and LTE in unlicensed deployed in the same band in the same area what is the metric to determine wireless medium/channel access fairness?
The metric or metrics should be defined early either in the definition of the SID or early in the process.
=> Need to define a Fairness Metric to ensure fair coexistence with 802.

## Slide 14: Deployment Scenarios and RF Related Aspects
There are large contiguous blocks of spectrum and for example 802.11ac uses channels up to 160 Mhz. What is the targeted channel bandwidth and the aggregation level for LTE-U carriers? Are we discussing the increase of the number of aggregated channels?
Are we discussing deploying this like LTE CA scenario 1 or scenario 4 or both?
Which combinations of FDD and TDD are we supporting in the licensed and unlicensed carriers? Are we supporting TDD uplink in the unlicensed carrier?
=> Different Carrier Aggregation Parameters and Deployment Scenarios can have unique RF impacts and unclear requirements can explode work significantly; we should provide clear direction to ensure focused RAN4 work.

## Slide 15: Summary (1 of 2)
To balance the need to be as efficient as possible with our time and provide a robust answer to how to include unlicensed bands in LTE, we need to be as exact as possible in how we define the study that the working groups will undertake otherwise.
The questions pointed out in the previous slides are a good subset of the issues that are best known before or very early in a study by the working groups. If they are not known early:
  The time schedule will take a hit or
  We end up with a quick and dirty probably suboptimal solution.

## Slide 16: Summary (2 of 2)
These questions could be answered by:
  Starting a RAN plenary study as proposed in RP-140240 to more clearly define the requirements including the answers to many of the proposed questions from this paper.
  Conducting email discussions on the public reflectors to define the requirements/focus the work.
  Starting work at working group level with more realistic timelines (stretching out the work longer than as was defined in RP-140259).

## Slide 17
Thank You!