## Slide 1: An operator view on LTE in unlicensed spectrum
TeliaSonera
Contact: per.emanuelsson@teliasonera.com
RWS-140011

## Slide 2: Unlicensed spectrum for a mobile operator?
Exponential traffic growth in mobile networks
  TeliaSonera mobile networks: ~60% yearly growth in traffic
  After five years: Traffic increase of a factor of 10
To cope with this traffic increase, we need:
  Increased spectral efficiency
  Densification of networks (small cells, dual connectivity(?), ...)
  ”All the spectrum we can get”
Licensed spectrum preferred, but:
  Unlicensed spectrum valuable for ”offloading licensed spectrum”
  Unlicensed spectrum to be used for (mainly) best effort traffic
Conclusion: Also unlicensed spectrum necessary to use
Key question: WLAN or LTE in unlicensed spectrum?

## Slide 3: LTE-U concept proposed in 3GPP RAN – License-Assisted Access
Unlicensed spectrum to be used as secondary carrier in LTE Carrier Aggregation
  All control information on primary (licensed spectrum) carrier
  QoS traffic on primary carrier
  Secondary (unlicensed) carrier used for (mainly) best effort traffic
No “standalone mode” for LTE-U
LTE-U to be TDD and/or SDL
LTE features that need to be specified
  LTE FDD/TDD CA – already ongoing
  “Listen before talk” or similar
  New frequency bands for LTE

## Slide 4: SWOT LTE License-assisted access compared to WiFi
WEAKNESSES
Will take time before we have support for LTE-U in the majority of terminals
STRENGTHS
Easier to integrate with EPC
Easier and more cost efficient O&M
Higher spectral efficiency
  Needs to be verified
Higher user bit rate (carrier aggregation)
OPPORTUNITIES
Very cost efficient capacity as well as user bit rate booster of our 4G network
Better user experience for our customers
Possible to reduce the number of RATs in our network – Lower production cost
THREATS
Could open up for unfair competition
WRC allocates less licensed spectrum for mobile usage
Market fragmentation in unlicensed bands
S
W
T
O

## Slide 5: Analysis of the threats
Unfair competition
  Threat: New players could use unlicensed spectrum to avoid regulatory requirements (coverage, LI, …)
  Not likely, since:
    Licensed spectrum needed
    ”Big core network machinery” needed
  Also: Already possible today with WiFi
Less spectrum allocated to mobile usage by WRC
  Nothing new: Already today mobile operators use WiFi
  Mobile industry needs to show that licensed spectrum needed for QoS
Market fragmentation
  WiFi will remain very important => Terminals will still support WiFi
  Not a major effort to include LTE-U if LTE already supported
Conclusion: The threats are not likely to materialize

## Slide 6: Analysis of the opportunities
Capacity booster
  Higher spectral efficiency than for WiFi
    Indicated in contributions at the WS in Paris in January
    Needs to be verified in RAN1 simulations
Better user experience
  Higher user bit rate – because of carrier aggregation
  Seamless mobility between ”licensed and unlicensed”
Lower production cost
  Easier integration with EPC
  WiFi RAT can be closed down
  WiFi O&M can be closed down
Conclusion: The opportunities look good! 

## Slide 7: TeliaSonera position
TeliaSonera is positive to the proposed concept of “License-Assisted Access”
We would like to have this specified in 3GPP Rel-13
We will not support a ”stand alone mode” for LTE-Unlicensed
  Main benefit with Carrier Aggregation
  Unlicensed secondary carrier for Best Effort Traffic
3GPP/WiFi interworking remains important
  Operator WiFi networks will remain important for a long time
Spectrum:
  5 GHz is first target (5150-5350 and 5470-5725 MHz)
  Also 2.4 GHz needs to be specified (not possible to achieve max synergies otherwise)