## Slide 1: On the Standardisation of LTE in Unlicensed Spectrum
Alcatel-Lucent
13 June 2014

## Slide 2: Introduction and Status
LTE-U is a promising enhancement by providing flexible usage and maximization of spectrum use to support the ultra capacity foreseen to be needed for 4g and beyond.
LTE offers the following benefits:
  Higher spectral efficiency and improved coverage;
  Enables improved network management and load balancing through tighter integration;
  Simplifies network management and tracking of KPIs through a single RAN.
The introduction and adoption of LTE-U has some very obvious challenges. From the radio perspective, one challenge is the coexistence with existing technologies that are operating in these unlicensed spectrum such as Wifi. The other is unpredictable interference to LTE from other technologies.
3GPP should proceed deliberately with well defined and controlled Study Item scope after the completion of Release 12.

## Slide 3: SI Overview and Motivation
One of the main objective is to ensure timely completion of Rel-12. Hence a reduced scope SI for LTE-U is proposed to begin in RAN#65 after Core spec functional freeze of Rel-12.
To ensure global benefits, possible physical layer enhancements (e.g. LBT) are evaluated in the proposed SI to address coexistence requirements in many regions.
The emphasis of the SI is on a licensed-assisted LTE-unlicensed operation.
Proposal to have work in 3GPP separated into two Phases: Phase 1 and Phase 2:
  Phase 1 with first priority: SI followed by WI in Rel-13, addressing an SCell which operates in unlicensed spectrum and is a Supplemental DL carrier in an LTE CA configuration, where the PCell operates in licensed spectrum and uses LTE FDD
    Includes methods to address coexistence issues on unlicensed bands for an identified exemplary band (e.g. 5 GHz)
  Phase 2 with secondary priority (starts after completion of Phase 1 SI): an SCell operates in unlicensed spectrum and comprises both UL and DL in an LTE CA configuration and/or an LTE dual connectivity configuration, where the PCell operates in licensed spectrum and can be LTE FDD or LTE TDD.

## Slide 4: Phase Approach Options
The following different options are considered for Release 13:
  Option 1:
    SID: DL only & DL+UL
    WID: DL only & DL+UL
  Option 2:
    SID: DL only & DL+UL
    WID: DL only
  Option 3:
    SID: DL only for 1st phase in Rel13 + DL+UL for 2nd phase in Release 13
    WID: DL only for Release 13
Option 3 is preferred as it uses the SDL CA based approach as baseline to study the feasibility and addresses issues and concerns. Given the complexities and multi-faceted nature of this new feature, this option also has the least specifications impact with realistic chance of completion within Release 13. Detailed time plan is provided next.

## Slide 5: Proposed Timeline: 3GPP Releases 12 and 13 for LTE-U
6/2014
9/2014
12/2014
3/2015
6/2015
9/2015
#64
#65
#66
#67
#68
#69
12/2015
#70
3/2016
#71
6/2016
#72
3/2014
#63
Rel-12 Core spec functional freeze
Start of Rel-13
RAN1 LTE-U study item
Phase 1 (highest priority)
Phase 2 (lower priority)
Rel-13: 15-18 Month Release
3GPP Phase 1 (SDL FDD CA ) SI
3GPP Phase 2 (TDD UL/DL and advanced techniques) Study item
3GPP LTE-U work item focussing on phase 1 only and one band (5 GHz)
3GPP LTE-U work item 2 focussing on phase 2,
TDD UL/DL, more advanced techniques
more bands
Dual connectivity
3GPP LTE-U phase 1 specifications ready
band (5 GHz)
with LBT-like enhancements
Work item of 3GPP Phase 1