## Slide 1: Review of Regulatory Requirements for Unlicensed spectrum
Alcatel-Lucent, Alcatel-Lucent Shanghai Bell, Ericsson, Huawei, HiSilicon, IAESI, LG, Nokia, NSN, Qualcomm, NTT Docomo
13 June 2014

## Slide 2: Overview
This presentation summarizes the relevant aspects identified was the regulatory requirements around the world for unlicensed spectrum.
Information for the following countries is available:
Full details are found in RP-140808, “Review of Regulatory Requirements for Unlicensed Spectrum,” Alcatel-Lucent, Alcatel-Lucent Shanghai Bell, Ericsson, Huawei, HiSilicon, IAESI, LG, Nokia, NSN, Qualcomm, NTT Docomo.

## Slide 3: Europe: Spectrum
The 5150-5350 MHz and the 5470-5725 MHz bands are referred here as the broadband radio access networks (BRAN) bands where the wireless access systems (WAS) including RLAN equipment are operating in.
The 5725-5875 MHz band (in the BRAN domain) is used by the fixed wireless access (FWA) networks and finally the intelligent transport systems (ITS) utilize the 5855-5925 MHz band.
The European Commission has recently submitted to CEPT a mandate to study the conditions for the extension of the 5 GHz range designated for WAS/RLANs [17] in order to allow the use by WAS/RLANs of the whole 5150-5925 MHz band.

## Slide 4: Europe: Dynamic Frequency Selection (DFS)
ETSI mandates the usage of DFS in some bands as shown in Table below.
Parameter | Requirement | Comments
DFS Threshold (dBm) for WAS/RLAN | -62(dBm) + 10(dBm/MHz) - EIRP Spectral density (dBm/MHz) + G(dBi) | *No DFS requirements on 5150 MHz – 5350 MHz *G denotes antenna gain
DFS Threshold (dBm) for FWA | -69 (dBm) + 23(dBm/MHz) - EIRP Spectral density (dBm/MHz) + G(dBi) | *No DFS requirements on 5850 MHz – 5875 MHz *G denotes antenna gain
Channel Availability check | 60 seconds outside 5600-5650 MHz | Master mode
 | 10 minutes inside 5600-5650 MHz | 
Channel move time | 10 seconds | Master and slave modes
Non-occupancy time | 30 minutes | After radar detection in either channel availability check or in-service monitoring
Uniform Spreading is required across the frequency ranges 5150 -5350 MHz and 5470-5725 MHz. Uniform Spreading is not applicable for equipment that only operates in 5150-5250 MHz band. |  | 

## Slide 5: Europe: Listen-Before-Talk (LBT)
Listen-Before-Talk (LBT) mechanism is requested independently of whether the channel is occupied or not, the LBT parameters being given in Table 2.1.1-5a and 2.1.1-5b.
Requirements on frame-based equipment and the requirements on load-based equipment are summarized below. Note that no LBT requirement is requested for the FWA band.
Parameter | Requirement | Comment
Clear Channel Assessment (CCA) time | Minimum 20μs | 
Channel Occupancy time | Minimum 1 ms, maximum10 ms | 
Idle period | Minimum 5% of channel occupancy time | 
Fixed frame period | Equals to Channel Occupancy time + Idle Period | 
Short control signaling transmission time | Maximum duty cycle of 5% within an observation period of 50ms | Part of Channel occupancy time
CCA Energy detection threshold | Assuming receive antenna gain G=0dBi: If EIRP=23dBm at transmitter Threshold ≤ -73 dBm/MHz Otherwise (different transmit power levels, PH) Threshold = -73(dBm/MHz) + 23(dBm) – PH(dBm) | For WAS/RLAN

## Slide 6: Europe: LBT for Load-Based Equipment
Parameter | Requirement | Comment
Clear Channel Assessment (CCA) time | Minimum 20μs | 
Extended CCA time | Duration of a random factor N multiplied by the CCA observation time. N shall be randomly selected in the range 1..q every time, q=4…32 | 
Channel Occupancy time | <= (13/32) × q ms | 
Idle period | Extended CCA time | 
Short control signaling transmission time | Maximum duty cycle of 5% within an observation period of 50ms | Part of Channel occupancy time
CCA Energy detection threshold | Assuming receive antenna gain G=0dBi: If EIRP=23dBm at transmitter Threshold ≤ -73 dBm/MHz Otherwise (different transmit power levels, PH) Threshold = -73(dBm/MHz) + 23(dBm) – PH(dBm) | For WAS/RLAN

## Slide 7: USA: Spectrum
U-NII-x bands denote frequency bands for Unlicensed National Information Infrastructure devices usage that are governed by §15.407.
There is also an overlapping ruling of §15.247 from 5.725 to 5.85 GHz. A device could choose to follow either U-NII rulings or §15.247 rulings when operating within the frequency range.

## Slide 8: USA: Paragraph 15.407 Rules for UNII Devices
 |  | UNII-1 | UNII-2A | UNII-2C | UNII-3 | Comments
Frequency Range (GHz) |  | 5.15 – 5.25 | 5.25-5.35 | 5.47-5.725 | 5.725-5.825 | 
Max conducted output power < min(a, b) (dBm) |  | 30 | 24 | 24 | 30 | 
 |  | 4+10logB | 11+10logB | 11+10logB | 17+10logB | B is the 26-dB emission bandwidth in MHz
Peak PSD (dBm/MHz) |  | 4 | 11 | 11 | 17 | 
Assumed Antenna Gain (dBi) |  | 6 | 6 | 6 | 6* | Peak power is reduced by G-6 dB for directional antennas with gain > 6 dBi; * UNII-3 fixed point to point operation power scaling threshold is 23 dBi
Out of band emission | Frequency Support (GHz) | Outside 5.15 – 5.35 | Outside 5.25 – 5.35 | Outside 5.47-5.725 | Outside 5.715-5.835 | 
 | EIRP (dBm/MHz) | -27 | -27 | -27 | -27 | Resolution bandwidth 1 MHz
 | Frequency Support (GHz) |  | 5.15-5.25 |  | 5.715-5.725 5.825-5.835 | 
 | EIRP (dBm/MHz) |  | Same as UNII-1 |  | -17 | 
Transmit Power Control |  | N/A | TPC to 6 dB below a mean EIRP of 30 dBm. No TPC for mean EIRP < 27 dBm |  | N/A | 

## Slide 9: USA: DFS requirements for UNII-2 Devices
 | Levels | Comments
Max EIRP (dBm) | 23 to 30 | * DFS power is averaged in 1 micro-second for 0 dBi antenna. * Uniform spread over available channels.
DFS Threshold (dBm) | -64 | 
Max EIRP (dBm) | <23 | 
DFS Threshold (dBm) | -62 | 
Channel Availability check | 60 seconds | Master mode
Channel move time | 10 seconds | Master and slave modes
 | 200 ms normal operation | 
Non-occupancy time | 30 minutes | After radar detection in either channel availability check or in-service monitoring

## Slide 10: Other Unlicensed Spectrum - 1
Canada: 5.15 – 5.25GHz, 5.25-5.35 GHz, 5.47-5.60 and 5.65-5.725 GHz, 5.725-5.825 GHz. Note: the use of RLANs is forbidden in the band 5600-5650 MHz in order to protect the meteorological radars from interference caused by RLANs.
Brazil: In Brazil, the bands 5250-5350 MHz, 5470-5590 MHz, 5650-5725 MHz and 5725-5850 MHz are allowed to RLANs [20]. Bands 5150-5250 MHz and 5250-5350 MHz are restricted to indoor use, and DFS is mandated in the band 5470-5725 MHz.
Mexico: In Mexico, the bands 5150-5250 MHz, 5250-5350 MHz, 5470-5600 MHz, 5650-5725 MHz and 5725-5875 MHz are open to RLANs.
China: The 5150-5350 MHz frequency band is open to unlicensed RLANs indoor deployment in China. Furthermore, mandatory DFS / TPC or DFS only with a 3 dB backoff of the max mean EIRP is required for 5250-5350 MHz.
Japan: 5.15-5.25 GHz, 5.25-5.35 GHz, and 5.47-5.725 GHz. DFS is required for 5.25-5.35 GHz and 5.47-5.725 GHz.

## Slide 11: Other Unlicensed Spectrum - 2
Korea: 5.1-5.25 GHz, 5.25-5.35 GHz, 5.47-5.65 GHz, 5.725-5.825 GHz, 2.4- 2.4835 GHz. DFS and TPC are required for the 5.25-5.35 GHz and 5.47-5.65 GHz.
India: Bands 5150-5250 MHz, 5250-5350 MHz and 5725-5875 MHz are allowed to RLANs.
Taiwan: Bands 5250-5350 MHz, 5470-5590 MHz, 5650-5725 MHz and 5725-5850 MHz are allowed to RLANs.
Singapore: Bands 5150-5250 MHz, 5250-5350 MHz, 5470-5725MHz and 5725-5850 MHz are open to RLANs.
Australia: Band bands 5150-5250 MHz, 5250-5350 MHz and 5470-5725 MHz, except the sub-band 5600-5650 MHz, are open to RLANs. DFS and TPC are mandatory in the bands 5250-5350 MHz and 5470-5725 MHz.