## Slide 1: Automotive Perspective on Licensed Assisted Access
29 August 2015
General Motors
Research & Development
Advanced Technical Center Israel (ATCI)
Vehicle Connectivity Group

## Slide 2
The LAA goal is to provide complementary resources to LTE operators by utilizing the 5 GHz band through carrier aggregation
One of the design goals is to enable fair coexistence with the existing WiFi networks (TR-36.889)
Vehicles may include multiple WiFi APs
In spite of the efforts to achieve fair coexistence, the WiFi would still be put at a disadvantage compared to the LAA due to some of its inherent properties which may have been overlooked
Introduction
STA
AP
AP
UE
UE

## Slide 3
Co-Existence Issues
Automotive issues:
  Hidden nodes problem
  High mobility APs
  Vehicle APs with dense UEs environment
General issues:
  LBT protocol-differences between WiFi and LTE
  Inefficient spectral utilization

## Slide 4
Hidden Nodes Problem
Can LTE “Hear” WiFi Devices?
The LBT protocol requires the LTE device to perform Clear Channel Assessment (CCA) before transmitting
The question is: Does the fact the AP can detect the eNB transmission necessarily mean that the eNB can detect the WiFi signal?
AP
Is there complete reciprocity between the two paths?

## Slide 5
 | eNB | AP
Transmit power |  | Due to cost considerations
Range | and beyond | Up to
 | eNB | AP
Transmit power |  | 
Range |  | 
AP
Such a setup would lead to the “starvation” of WiFi devices.
Hidden Nodes Problem
Can LTE “Hear” WiFi Devices?

## Slide 6
High Mobility APs
The LBT duration is , whereas the TXOP (in case of LTE) is several milliseconds.
Assuming the UE speed is and :
  The coherence time of the channel:
  .
Due to high Doppler, the channel during TXOP and the channel between vehicle AP and eNB during LBT may vary significantly
As a consequence, data transmission could suffer from collision, although clear channel has been identified during LBT

## Slide 7
Extended Vehicular A (9 taps)
SNR per SubFrame- PDF for average SNR of 10 dB
2 taps
High Mobility APs

## Slide 8
Extended Vehicular A (9 taps)
2 taps
High Mobility APs
SNR per SubFrame- CDF for average SNR of 10 dB

## Slide 9
UEs within the vehicle or in its close surrounding become potential competitors to the vehicle APs.
Even scenarios with low vehicle density become high load scenarios.
Vehicle APs with Dense UEs Environment
Vehicle APs widely exposed to outdoor UEs

## Slide 10
LBT: LTE vs. WiFi
The LBT scheme in TR 36.889

## Slide 11
LTE-LBT looks similar to WiFi protocol, however it differs in several aspects:
DIFS/EIFS-
The are the equivalent of
However, if the last frame which occupied the channel is received incorrectly, other WiFi devices defer for
Problem in the last frame
Random “backoff time”
Waiting for the channel to be idle
Waiting for the channel to be idle
()
Random “backoff time”
transmitting
EIFS ()
The channel (occupied by a WiFi signal):
WiFi that wants to transmit:
LTE that wants to transmit:
LTE has advantage of over WiFi, even though the WiFi started to check the channel first.
LBT: LTE vs. WiFi

## Slide 12
2. RTS/CTS (Request/Clear to Send)-
WiFi networks use RTS/CTS protocol to solve hidden node problems
All STAs which use the relevant AP and detected one of the messages would defer from transmission for the specified duration before applying the CCA protocol
If transmission loss occurs, the eNB (which cannot decode RTS/CTS) will start the LBT protocol as soon as the energy level indicates idle
STA1 is CTS,
Estimated duration:
AP
STA 3
STA 1
STA 2
Defer
for amount of time
Defer
for amount of time
RTS,
Estimated duration:
LBT: LTE vs. WiFi
In issues 1,2 the problems occur since LTE devices cannot decode inter WiFi communication

## Slide 13
3. Contention Window (CW) Update-
CW update is performed when re-transmission is required
WiFi has an exponential CW update mechanism
Both LTE and WiFi re-transmit at the absence of an ACK
In WiFi the ACK arrives within few tens of micro seconds from the end of data transmission, whereas in LTE it takes 3ms for an ACK to arrive
As a consequence, when WiFi and LTE devices compete over the same band, WiFi devices may increase the CW several times before the LTE will consider re-transmission
LBT: LTE vs. WiFi

## Slide 14
Inefficient Spectral Utilization
WiFi can only transmit over bandwidths of 20, 40, 80, 160 MHz using the defined channels
Allowing LTE the use of 5, 10, 15 MHz carrier components would result in:
  Higher interference to adjacent channels than would be caused by 20MHz transmission (since the spectral mask is given in dBc)
  Spectral utilization inefficiency
20MHz
5MHz
f

## Slide 15
Summary
In spite of the efforts to establish fair coexistence, LTE still has leverage over WiFi
In order to improve balance between LTE and WiFi we recommend the followings:
  Using only carrier components of 20MHz to prevent inefficient and unfair spectral utilization
  To mitigate the gap between WiFi and LAA CCA protocols we offer:
    Considering longer
    Enabling only minimal TXOP (e.g., 1ms if possible)
    Use the WiFi CW update mechanism
  To mitigate the high mobility APs problem:
    Reduce use of LAA for UEs with high speed
    Enabling only minimal TXOP

## Slide 16
While the recommendations above are essential to enable fair coexistence, they are not sufficient and require further studying
The hidden nodes problem is challenging due to the significant gap between WiFi and LTE resources and infrastructures
The inability of LTE to understand “WiFi language” causes it to interfere more than a WiFi device which contradict the fair coexistence definition
Viewing vehicle APs as part of the existing WiFi networks results in new scenarios of high density WiFi and LAA which need to be taken under consideration
In light of the above, additional simulations are required for better understanding the full impact of LAA on mobile WiFi APs
Conclusions

## Slide 17: Thank You

## Slide 18
3. Contention Window (CW) Update-
Note: WiFi has an exponential CW update mechanism, meaning:
  Let denote the number of re-transmissions.
  Let denote the CW size at re-transmission .
  .
  .
  is given by:
3GPP hadn’t committed to use the same update mechanism. Applying different mechanism may put the WiFi at greater disadvantage.
LBT: LTE vs. WiFi