## Slide 1: Telefónica 5G vision
Telefónica Global CTO
3GPP RAN Workshop
17th-18th September 2015
Ignacio Berberana, Javier Lorca & Kevin Holley

## Slide 2: Why do we need 5G?
2
Better way of providing current services (lower cost, improved performance, improved experience continuity,…)
Support of new services that cannot be provided with 4G Technologies (ultra low latency, massive IoT/MTC services,…)
Capacity to personalize services for specific applications (vertical industrial applications, safety,…)
Why do we need a new mobile system generation?
Why not rely on the evolution of existing systems like LTE?
We expect three main drivers to justify the development of 5G:
Source: GSMA
Notes: Good slide to start with, text on right is too small but probably ok here.

## Slide 3: What new services/use cases cannot be supported with 4G
3
1End-to-end latency in 4G is in the order of 30-40 ms
2Reliability in 4G systems is not higher than 98-99%
3As defined in “NGMN 5G White Paper”, available at: https://www.ngmn.org/uploads/media/NGMN_5G_White_Paper_V1_0.pdf
Source: NGMN 5G White Paper
Use cases that cannot be supported by 4G
Use cases that cannot be supported by 4G
While many foreseen use cases can be supported with 4G evolution, some of them cannot:
  Massive IoT/MTC services
  Ultra-low latency1 (<1 ms E2E)
  Ultra-high reliability2 (>99.999%)
Not all use cases are feasible from an economic viewpoint
  Are users willing to pay more?
However, even when supported by 4G, the ability to support multitudes of use cases through SW-defined network slices3 is another driver for a new NW architecture
Notes: Text on this slide is too small to be read. Right hand matrix is OK small but left hand something needs to be done

## Slide 4: Telefonica High-Level Requirements for the RAN
4
Business drivers require 5G RAN to reduce costs
  More users per spectrum / site, at lower cost
  Flexibility to deploy centralized / distributed / hybrid RAN approaches
  Flexibility to address different use cases on the same network infrastructure by means of network slices, as described by the NGMN White Paper
  Serve users via legacy 4G network where 4G meets needs
  Avoid integration with 2G/3G: only tight interworking with 4G
New capabilities to drive new business, with strong focus on cost effectiveness:
  Higher speed (and more consistent throughout the cell)
  Built-in IoT capabilities
  Exploitation of higher frequencies (including mmWave regime) for capacity, in cooperation with lower frequencies for coverage and control
  Ultra-low latency at both control and user planes (only for specialized applications, with clear business case)
  Opening parts of the network to third parties, to monetize connectivity

## Slide 5: Some Views on the RAN
5
Increasing the density of network accesses should not come at high unsustainable cost (e.g. backhaul costs and interference issues should scale linearly with the number of accesses)
RAN virtualization should be an integral part of 5G:
  Flexibility between distributed and centralized topologies should be sought
  Network functions should be decoupled from network nodes through SDN/NFV
Evolved LTE should be an essential part of 5G:
  New RAT should be developed for frequencies above 6 GHz
  Basic control mechanisms should be provided by evolved LTE below 6 GHz
  IoT could require a new RAT for lower frequencies (or be based on evolved LTE)
Some technology options for 5G require careful prior consideration:
  Strong deviations from OFDM should not be promoted unless advantages clearly surpass drawbacks, especially below 6 GHz
  Both FDD and TDD duplexing options should be explored
    Massive MIMO in TDD should be given a key role in new deployments
    Massive MIMO in FDD should wait until more research confirms its feasibility without excessive feedback signaling
  Full duplex should be exploited for repeaters/relays, not for the access
  Non-orthogonal multiple access schemes should coexist with orthogonal schemes

## Slide 6: Conclusions
6
Telefónica key goals for 5G are:
  Network architecture based on SDN/NFV exploiting network slices for RAN&CN
    The Future CN will upgraded through software only
  Ability to provide the right network slice to a UE depending on the service
  New use cases (IoT, ultra-low latency, ultra-high reliability…) must be economically viable
  Interworking should be limited to 4G, which should also play a key role in 5G coverage and control (at frequencies below 6 GHz)
  We should not create cost in replicating unused ISDN services from the 1980s in 5G.
Meanwhile, Telefónica believes that 4G networks should be allowed to grow and improve through some of the innovations proposed for 5G

## Slide 8: Backup

## Slide 9: ANNEX I: 5G technological solutions A lot of new technological components are expected to be incorporated
A.I
When selecting the technology solutions it is key to ensure that they support the identified technical requirements
Improved performance
Business flexibility
Economic efficiency
Massive MIMO SDN High frequency bands
New waveforms
Interference alignment Carrier Aggregation
Advanced receivers
Cognitive Management
NFV Fog computing
Device to Device
Full Duplex
Non Orthogonal Multiple Access
Fixed Mobile Convergence
Ultra Dense Networks
A lot of new technical proposals from a multitude of parties (vendors, operators, universities,…) that may help to fulfill the different requirements
Some of them can be applied also to evolved 4G systems
Not all of them necessarily consistent and compatible
If selected for the future standards, a huge business opportunity

## Slide 10: ANNEX II: Some technical issues that require clarification
A.II
New waveforms:
Does the advantages provided by non orthogonal multiple access compensate for the potential additional complexity in devices?
Is tunable OFDM the best way to integrate LTE radio interface in the 5G radio interface, preserving backwards compatibility?
Single RAT/multi RAT:
Same radio interface for all potential frequency bands? Need to preserve backwards compatibility with LTE? Both in the user plane and the control plane or only in the control plane?
Should a specific radio interface be developed for some special use cases (e.g. massive IoT, ultra low latency services)?
Massive MIMO:
Is M-MIMO feasible in high frequency bands? If yes, how high? How many users can be served when using high frequency bands? Is FDD feasible with reasonable feedback complexity?
Full duplex:
Will full duplex be feasible in user devices or only in network elements (e.g. relays)?
Device centric/cell-less architectures
Is this the natural trend in ultra-dense networks? Can centralized processing improve the (so far, not very promising) performance of CoMP?
Notes: Text is too small. Lots of space wasted here.

## Slide 11: ANNEX III: Some views on Massive MIMO1
A.III
Main current concern is the lack of applicability for FDD
  Sparsity assumption for feedback compression seems unclear at cm-waves
Overall BS cost should be kept reasonable with 100+ antennas
  There is some evidence showing that less expensive components can be used
  Hybrid RF structures may be required
  Is there a sweet spot for the number of RF chains vs. analog phase shifters?
Outdoor to indoor propagation at mm-waves seems limited by penetration losses thereby requiring additional beamforming
  To what extent is capacity reduced by the extra beamforming?
Need to address baseband power consumption vs. RF power consumption
  Can RF hardware be drastically simplified thanks to the lower TX power?
  Impact of increased RF impairments must be studied carefully
Pilot contamination issues must be studied
Trying to marry massive MIMO with centralized RAN leads to critical cost issues (mainly at the fronthaul) that should be addressed
1 The research leading to these results has received funding from the European Union's Seventh Framework Programme ([FP7/2007-2013]) under grant agreement n° 619086
Notes: Text is too small. Lots of space wasted here.